## Slide 1: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᑦ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᑦ ᑲᑎᒪᔨᖏᑕ ᕿᒥᕐᕈᓂᖓᑦ ᕼᐅᑉ ᐸᐃᒥ ᐱᓕᕆᐊᖑᔪᒥᒃ ᑐᒡᓕᐊᓂ Type A-ᒥᒃ ᐃᒥᓕᕆᓂᕐᒧᑦ ᓚᐃᓴᓐᓯᑖᖑᔪᒪᔪᒧᑦ
Notes: Hello everyone, I am John Roesch, the Senior Hope Bay Project Officer for the Department of Lands and Environment for the Kitikmeot Inuit Association. I am responsible for project oversite for the KIA and provide input into the regulatory process on the Hope Bay Project to both the NWB and NIRB. In performing this role, I make use of KIA’s consultants who are subject matter experts in the areas of hydrology, hydrogeology, fisheries, aquatic environment, and geotechnical engineering.

## Slide 2: ᐱᔾᔪᑎᖓ ᓴᖅᑭᑕᐅᓂᖓᑕ
ᓴᖅᑭᑦᑎᖁᓪᓗᒋᑦ ᓇᐃᓈᖅᓯᒪᔪᓂᒃ ᐅᓂᒃᑳᓕᐊᖏᓐᓂᒃ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᑲᑎᒪᔨᖏᑕ ᕿᒥᕐᕈᓚᐅᕐᓂᖓᓐᓂᒃ TMAC ᑎᒥᖁᑎᖓᑦᑕ ᑐᒃᓯᕋᐅᑎᖓᓐᓂᒃ ᕼᐅᑉ ᐸᐃᒥ ᐱᓕᕆᐊᖃᕈᒪᓪᓗᑎᒃ ᑐᒡᓕᐊᓂ ᐱᓕᕆᐊᒃᓴᒥᒃ Type A-ᒧᑦ ᐃᒥᓕᕆᓂᕐᒧᑦ ᓚᐃᓴᓐᓯᑖᕈᒪᓪᓗᑎᒃ ᑐᒃᓯᕋᐅᑎᒥᒃ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᕿᒥᕐᕈᓇᑦᓯᐊᓚᐅᖅᑐᑦ ᐃᖃᓗᖃᕐᓂᖏᓐᓂᒃ ᐊᒻᒪᓗ ᐃᖃᓗᐃᑦ ᓇᔪᒐᖏᓐᓂᒃ, ᐃᒪᕐᒥᐅᑕᑦ ᑭᓲᓂᖏᓐᓂᒃ, ᐊᒻᒪᓗ ᐃᒥᕐᒥᒃ ᓇᐅᑦᑎᖅᓱᐊᖃᕐᖢᑎᒃ.
8-ᖑᔪᑦ ᐱᔾᔪᑎᐅᔪᑦ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᑦ ᓯᕗᕐᖓᒍᑦ ᑲᑎᒪᓂᐅᑉ ᐊᒻᒪᓗ ᑲᑎᒪᑎᓪᓗᒋᑦ ᒪᐃ 2018-ᒥ.
Notes: The purpose of this presentation is to provide a brief summary of our final submission on the Hope Bay Project Phase 2 Type A water license applications. Our review covered hydrology, hydrogeology, fisheries, aquatic environments, water quality, and monitoring. KIA conducted the review in a collaborative manner with TMAC Resources Inc. out of which we brought forward 8 issues which were resolved prior and at the Technical Meeting in May 2018.

## Slide 3: ᐊᕕᒃᑕᐅᔪᒪᔪᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᑐᒐᒃᓴᑦ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐊᒻᒪᓗ ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐃᒪᖁᑎᖏᓐᓂᓗ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᖏᖃᑎᖃᓚᐅᖅᑐᑦ TMAC-ᑯᓐᓂᒃ ᑲᑎᓪᓗᒋᑦ ᐅᓄᕐᓂᖃᖅᑐᑦ ᑐᖅᑯᖅᑕᐅᓂᐊᖅᑐᑦ $61,174,597 ᐊᑐᒐᒃᓴᑦ Doris-Madrid-ᒥ Type A-ᒥᒃ ᐃᒥᓕᕆᓂᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᖏᖃᑎᖃᓚᐅᖅᑐᑦ TMAC-ᑯᓐᓂᒃ ᑲᑎᓪᓗᒋᑦ ᐅᓄᕐᓂᖃᖅᑐᑦ ᑐᖅᑯᖅᑕᐅᓂᐊᖅᑐᑦ $36,712,621 ᐊᑐᒐᒃᓴᑦ ᐹᔅᑕᓐᒥ Type A-ᒥᒃ ᐃᒥᓕᕆᓂᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᑐᒃᓯᕋᓚᐅᖅᑐᑦ 85%-ᒥᒃ ᐱᔪᒪᓪᓗᑎᒃ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᓂᒃ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖏᓐᓂ ᐊᒻᒪᓗ 15% ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖏᓐᓂ ᐊᒻᒪᓗ ᐃᒪᖓᓂ Doris-Madrid-ᒥ ᐊᑐᖅᑕᐅᒐᔭᖅᑐᓂᒃ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᓂᒃ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᑐᒃᓯᕋᓚᐅᖅᑐᑦ 23-ᓂᒃ ᐊᑐᒐᒃᓴᓂᒃ ᑐᖅᑯᖅᑕᐅᖁᔨᓪᓗᑎᒃ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖏᓐᓄᑦ ᐊᒻᒪᓗ 77% ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖏᓐᓄᑦ ᐊᒻᒪᓗ ᐃᒪᖁᑎᖏᓐᓄᑦ ᐊᑐᒐᒃᓴᓂᒃ ᐹᔅᑕᓐᒥ ᑐᖅᑯᖅᑕᐅᖁᔨᓪᓗᑎᒃ.
Notes: The KIA had agreed with TMAC on $61.2 million for the Doris-Madrid security with a split of 85% and 15% split for IOL and Crown Land and Water, respectively. KIA also agreed with TMAC on $36.7 million for the Boston security with a split of 23% and 77% split for IOL and Crown Land and Water. Our review of reclamation security was conducted by our geotechnical engineering consultant and the split of IOL and Crown Land and Water was based on 100% allocation of specified mine site components to either land or water as per TMAC’s request to facilitate execution of reclamation work.
The KIA is open to the receipt of staged security from TMAC subject to particular water license conditions. TMAC has provided both KIA and CIRNA with a proposed staged split of security for the Hope Bay Project Phase2. KIA has had discussions with TMAC and CIRNA on the overall reclamation security for Doris-Madrid and Boston, the split in land and water for each water license and the staging of security.

## Slide 4: ᐊᕕᒃᑕᐅᔪᒪᔪᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᑐᒐᒃᓴᑦ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐊᒻᒪᓗ ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐃᒪᖁᑎᖏᓐᓂᓗ
CIRNAC-ᑯᑦ ᐋᖅᑭᒡᓱᐃᓯᒪᓕᖅᑐᑦ ᑲᑎᓪᓗᒋᑦ ᐅᓄᕐᓂᕆᔭᖏᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ Doris-Madrid-ᒧᑦ $65,774,448 ᐊᒻᒪᓗ $40,543,869-ᖑᔪᑦ ᐹᔅᑕᓐᒥ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ.
CIRNAC-ᑯᑦ ᐋᖅᑭᒡᓯᓯᒪᓕᖅᑐᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᕕᒃᑕᐅᓂᐊᕐᓗᑎᒃ ᐃᒪᓐᓇ 56.2% ᓄᓇᒧᑦ ᐊᒻᒪᓗ 43.8% ᐃᒥᕐᒧᑦ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ Doris Madrid-ᒧᑦ ᐊᒻᒪᓗ ᐊᕕᒃᑕᐅᓗᓂ 50.2% ᓄᓇᒧᑦ ᐊᒻᒪᓗ 49.8% ᐃᒪᕐᒧᑦ ᐹᔅᑕᓐᒧᑦ.
ᐱᖓᓲᓕᖅᑲᖓᔪᓂᒃ ᐊᖏᖃᑎᒌᒍᑎᖃᖅᑐᖃᓚᐅᖏᑦᑐᖅ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᑮᓇᐅᔭᑦ ᐱᓪᓗᒋᑦ ᐊᑐᖅᑕᐅᔪᒃᓴᑦ ᓄᓇᒧᑦ ᐊᒻᒪᓗ ᐃᒫᓄᑦ ᐊᕕᒃᑕᐅᓪᓗᑎᒃ.
TMAC-ᑯᑦ ᑐᒃᓯᕋᐅᑎᓕᐅᖅᓯᒪᓕᖅᑐᑦ ᐊᒡᒍᖅᑐᖅᓯᒪᐅᕐᓗᒋᑦ ᑐᖅᑯᖅᑕᐅᕙᓪᓕᐊᓂᐊᕐᒪᑕ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᕿᒥᕐᕈᓯᒪᓕᖅᑐᑦ ᑕᒪᑐᒧᖓ ᐊᒻᒪᓗ ᐊᖏᖃᑎᖃᖅᓯᒪᓕᕐᖢᑎᒃ.
Notes: CIRNAC proposes $65.8 million in total security for Doris-Madrid and $40.5 million for Boston. This represents a difference of $4.6 million and $4.2 million respectively between CIRNAC’s Doris-Madrid and Boston total security amounts and those put forward by TMAC and KIA.
CIRNAC’s land and water split of security is 56.2% and 43.8% for Doris-Madrid and 50.2% and 49.8% for Boston which is substantially different from KIA and TMAC’s land and water split. CIRNAC only applied 100% allocation of security to a select few mine site components and not to all components.
Currently there is no three-way agreement on either the total amount of security or the split between land and water.
TMAC has proposed staged security for Doris-Madrid and Boston, which KIA reviewed and agrees with. The tranches for staged security meet KIA’s requirements for receiving staged security for major mine site components on geographical basis with a planned construction schedule.

## Slide 5: ᐊᕕᒃᑕᐅᔪᒪᔪᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᑐᒐᒃᓴᑦ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐊᒻᒪᓗ ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖓᓐᓂ ᐃᒪᖁᑎᖏᓐᓂᓗ ᐊᑐᒐᒃᓴᑦ Doris-Madrid-ᒥ
Tranche | KIA % of Sub-Total | KIA $ | CIRNA % of Sub-Total | CIRNA $ | Sub-Total | Sub-Total %
Phase 1 | 40.2% | $24,600,961 | 11.0% | $6,705,192 | $31,306,153 | 51.2%
Roberts Bay | 0.8% | $486,065 | 0.0% | $18,347 | $504,412 | 0.8%
Boston All-Weather Road | 1.0% | $588,867 | 0.0% | $0 | $588,867 | 1.0%
Wind Turbines | 8.0% | $4,863,440 | 0.0% | $0 | $4,863,440 | 8.0%
Madrid North Earthworks | 0.2% | $133,800 | 0.0% | $0 | $133,800 | 0.2%
Madrid South Earthworks | 0.1% | $41,042 | 0.0% | $0 | $41,042 | 0.1%
Madrid North Buildings | 3.3% | $2,044,069 | 2.8% | $1,682,576 | $3,726,645 | 6.1%
Madrid South Buildings | 1.3% | $810,632 | 0.3% | $185,459 | $996,091 | 1.6%
Tailings | 29.7% | $18,164,740 | 0.9% | $550,686 | $18,715,426 | 30.6%
Madrid North Mining | 0.3% | $160,717 | 0.0% | $5,843 | $166,560 | 0.3%
Madrid South Mining | 0.2% | $126,318 | 0.0% | $5,843 | $132,161 | 0.2%
Total | 85% | $52,020,651 | 15% | $9,153,946 | $61,174,597 | 100%
Notes: Depicted here is KIA’s the proposed staged security for Doris-Madrid which was provided to both TMAC and CIRNA.
The tailings tranche requires the greatest amount of security for reclamation work. The cost of tailings reclamation is driven by the amount of cover required for the tailings surface area. TMAC has proposed to provide tailings security in two letters of credit, one being provided 60 days prior to reaching 2.5 M Tonnes tailings deposit in the TIA indicating the start of Phase 2. The second is provided 60 days prior to the disposition of 7.7 M Tonnes of tailings into the TIA.
TMAC has provided KIA sufficient information on the planned expansion of the tailings surface area justifying the receipt of TIA tranche security in two Letters of Credits.
The KIA believes that this proposed staged security is equitable in meeting both KIA’s and CIRNA’s security requirements given the relative risk exposure in each of the construction and operational stages.

## Slide 6: ᐊᕕᒃᑐᖅᑕᐅᓯᒪᓗᑎᒃ ᐊᑐᖅᑕᐅᒐᔭᖅᑐᑦ ᑐᖅᑯᑕᐅᒐᔭᕐᓂᖏᑦ ᐃᓄᐃᑦ ᓄᓇᖁᑎᖏᑕ ᐃᓗᐊᓂ ᐊᒻᒪᓗ ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖏᓐᓂ ᐃᒪᖁᑎᖏᓐᓂᓗ
Tranche | KIA % of Sub-Total | KIA $ | CIRNA % of Sub-Total | CIRNA $ | Sub-Total | Sub-Total %
Mining | 0.6% | $206,966 | 2.6% | $942,845 | $1,149,811 | 3.1%
Tailings | 0.2% | $59,418 | 67.1% | $24,652,310 | $24,711,728 | 67.3%
Earthworks | 2.0% | $743,470 | 2.6% | $942,845 | $1,686,315 | 4.6%
Buildings | 20.5% | $7,530,662 | 4.5% | $1,634,104 | $9,164,766 | 25.0%
Total | 23.3% | $8,540,516 | 76.7% | $28,172,104 | $36,712,620 | 100%
Notes: Depicted here is KIA’s proposed staged security for Boston, which was provided to both TMAC and CIRNA. The tailings tranche requires the greatest amount of security for the Boston TMA. The Boston TMA is a dry stacked tailings requiring both lining and closure cover. The cost is driven by the amount of lining and cover required by the tailing surface area, which can be controlled by building the TMA in three cells. Given this, tailings tranche security can be provided in three installments as proposed by TMAC.
The first letter of credit would be provided 60 days prior to the commissioning of the process plant and production of tailings. The second letter of credit would be provided 60 days prior to 1.7 M Tonnes of tailings disposition to the TMA. The third letter of credit would be provided 60 days prior to the disposition of 3.4 M tonnes of tailings into the TMA.
The KIA believes that this proposed staged security is equitable in meeting both KIA’s and CIRNA’s security requirements given the relative risk exposure in each of the construction and operational stages.

## Slide 7: ᒪᓕᒐᖏᑦ ᐊᒡᒍᖅᑐᖅᓯᒪᐅᖅᑐᓂᒃ ᑐᖅᑯᐃᖃᑦᑕᕐᓂᐅᑉ ᐊᑐᒐᒃᓴᓂᒃ ᕼᐅᑉ ᐸᐃᒥ ᑐᒡᓕᐊᓂ ᐱᓕᕆᐊᒥ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᒪᑐᐃᖓᑦᓯᐊᖅᑐᑦ ᑐᓂᔭᐅᔪᒪᒍᑎᒃ ᐊᒡᒍᖅᑐᖅᓯᒪᐅᖅᑐᓂᒃ ᑐᖅᑯᖅᑕᐅᔪᓂᒃ ᐊᑖᒍᑦ ᓇᓗᓇᐃᖅᑕᐅᓯᒪᔪᑦ ᐃᒥᕐᒧᑦ ᓚᐃᓴᓐᓯᖓᑕ ᒪᓕᒐᖏᑕ ᐃᓗᐊᓂ.
  ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᑐᓂᔭᐅᔭᕆᐊᖃᖅᑐᑦ ᑐᖅᑯᖅᑕᐅᕙᓪᓕᐊᔪᓂᒃ ᓴᓇᔾᔪᑕᐅᕙᓪᓕᐊᓂᐊᖅᑐᓂᒃ ᐅᓪᓗᑦ 60 ᓯᕗᕐᖓᒍᑦ ᓴᓇᒋᐊᓚᐅᖏᓐᓂᖏᓐᓂ ᑐᖅᑯᖅᑕᐅᓗᑎᒃ.
  ᐊᒡᒍᖅᑐᖅᓯᒪᐅᑎᓪᓗᒍ ᑐᖅᑯᖅᑕᐅᕙᓪᓕᐊᔪᑦ ᒪᓕᒃᓯᒪᔭᕆᐊᖃᕐᓂᐊᖅᑐᑦ ᓄᓇᕗᒥ ᐃᒥᓕᕆᓂᕐᒧᑦ ᑲᑎᒪᔨᖏᑕ ᐱᓕᕆᔭᕆᐊᖃᖅᑕᖏᑕ ᐱᕙᓪᓕᐊᔾᔪᓯᖏᓐᓄᑦ.
  TMAC-ᑯᑦ ᑐᓂᓯᖃᖅᑐᑦ ᐊᕐᕌᒍᑕᒫᓐ ᓇᐃᓈᖅᓯᒪᔪᓂᒃ ᐅᓂᒃᑳᓕᐊᓂᒃ ᓴᓇᔭᐅᕙᓪᓕᐊᔪᖅ ᐱᕙᓪᓕᐊᓂᖓᑕ ᐅᓂᒃᑳᓕᐊᓂᒃ.
  ᓴᓗᒻᒪᖅᓴᐃᓂᕐᒧᑦ ᐊᑭᖏᑦ ᐅᓪᓗᒥᓯᐅᑎᕈᖅᑕᐅᖃᑦᑕᕆᐊᖃᖅᑐᑦ ᐊᑯᓚᐃᑦᑐᒃᑯᑦ ᐊᒻᒪᓗ ᕿᒥᕐᕈᔭᐅᖃᑦᑕᕐᓗᑎᒃ.
  ᖄᒃᑲᓐᓂᐊᒍᑦ ᑐᖅᑯᑦᑕᐅᔪᑦ ᑐᓂᔭᐅᑎᓪᓗᒋᑦ ᐃᓗᐊᓂ ᐅᓪᓗᑦ 60 ᕿᒥᕐᕈᓚᐅᖅᑎᓪᓗᒋᑦ ᐊᒻᒪᓗ ᐃᓱᒪᓕᐅᓚᐅᖅᑎᓪᓗᒋᑦ ᓄᓇᕗᒥ ᐃᒥᓕᕆᓂᕐᒧᑦ ᑲᑎᒪᔨᖏᑦ.
Notes: As stated previously, the KIA is open to receiving security using the proposed staged split under particular water license conditions.
The KIA must receive security 60 days prior to construction for each phase of construction for a defined set of major mine site components and infrastructure on a geographic basis. The receipt of staged security is subject to the NWB process where TMAC is required to provide proof of security being issued.
The reclamation costs must be updated periodically and reviewed by KIA and CIRNA and provided to the NWB. If additional security is determined to be required by the NWB, Sabina must provide it within 60 days of the determination.
The KIA has discussed these conditions with both TMAC and CIRNA.

## Slide 8: ᓄᖅᑲᕈᑎ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐅᒃᐱᕈᓱᒃᑐᑦ ᐃᓘᓐᓇᖏᑦ ᐱᔭᕐᓂᖏᑦᑐᓄᑦ ᐃᓱᒫᓗᒍᑕᐅᔪᑦ ᐋᖅᑭᒡᑕᐅᕙᓪᓕᐊᒃᐸᑕ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᓐᓄᑦ ᐊᒻᒪᓗ TMAC-ᑯᑦ ᑎᒥᖁᑎᖏᓐᓄᑦ ᐃᓱᒫᓗᒍᑕᐅᔪᖅ ᓴᓗᒻᒪᖅᓴᐃᔾᔪᑎᒃᓴᓄᑦ ᑐᖅᑯᐃᓂᖅ ᐋᖅᑭᒡᑕᐅᔪᓐᓇᕋᔭᖅᑐᖅ ᐊᖏᕈᑕᐅᓗᑎᒃ ᐃᓘᓐᓇᖏᓐᓄᑦ.
ᖁᐊᓇ
ᐊᐱᖅᑯᑎᒃᓴᑦ?
Notes: The KIA believes that with all technical issues being successfully resolved the final issue of staged security and particular water license conditions can be concluded with both TMAC and CIRNA through further discussion and cooperation.
Given this and the substantial benefits that will be obtained for Inuit from the Hope Bay Project Phase 2 and its IIBA, we believe that the issuing of the Type A Water licences for Doris-Madrid and Boston is warranted and in the best interest of the Inuit people.
We thank you for listening and we are open to any questions.