## Slide 1
Water Licence
Amendment And Renewal Application from Type “A” Water Licence 2 AM-DOH1335
Nunavut Water Board Technical Meeting
and Pre-hearing Conference
July 16-17, 2026
Notes: Crown-Indigenous Relations and Northern Affairs Canada, referred to as “the department” or “CIRNAC”, would like to thank the Nunavut Water Board for organizing this Technical Meeting and pre-hearing conference and giving us the opportunity to present CIRNAC’s position on the Amendment and Renewal Application of Type “A” Water License 2AM-DOH1335 submitted by Agnico Eagle Mine Limited (AEM) for the Doris-Madrid/Hope Bay Project .
My name is Pauline Firmin and I work for CIRNAC as a Regional Coordinator. Joining me today is Andrew Keim, Manager of Water Resources; and Tony Brown from Arcadis and Gerd Wiatzka from Arcadis joining online.

## Slide 2
Presentation Outline
Role and Responsibilities
Contributions to the Water Licence Application Review
Technical Review
Conclusion
Notes: This presentation will progress in the following order:
We will begin with the department’s Role and Responsibilities,
Followed by the department’s Contributions to the Water Licence Review.
We will then go through the Technical Review Comments, grouped by categories, that the department submitted to the Nunavut Water Board during the Technical Review stage. CIRNAC submitted twenty-three technical comment on June 19th, 2026.
We will wrap up the presentation with a conclusion
We will then open the floor to questions.

## Slide 3
Roles and Responsibilities
Crown-Indigenous Relations and Northern Affairs Canada’s (CIRNAC) responsibilities, mandate, and obligations are in alignment with the following:
Crown-Indigenous Relations and Northern Affairs Act
Nunavut Agreement
Nunavut Land Claims Agreement Act
Nunavut Waters and Nunavut Surface Rights Tribunal Act and the associated regulations
Nunavut Planning and Project Assessment Act
Territorial Lands Act and the associated regulations
Arctic Waters Pollution Prevention Act
Notes: CIRNAC is a regulatory intervener. The Water Resources Division works to conserve, protect and increase understanding of Nunavut’s water resources; provides advice to the Nunavut Water Board on matters of water licensing under Article 13 of the Nunavut Land Claims Agreement; supports water planning and policy development and develops water monitoring programs in Nunavut.
The department’s responsibilities, mandate, and obligations are in alignment with the following acts, legislations and regulations.
Crown-Indigenous Relations and Northern Affairs Act
The Nunavut Agreement
Nunavut Land Claims Agreement Act
Nunavut Waters and Nunavut Surface Rights Tribunal Act and the associated regulations
Nunavut Planning and Project Assessment Act
Territorial Lands Act and the associated regulations
Arctic Waters Pollution Prevention Act

## Slide 4
Contributions to Water Licence Application Review
CIRNAC made the following submissions to the Nunavut Water Board regarding
March 19 2026 – First Round of the Review of the Licence Completeness Check
April 20, 2026 – Second Round of the Review of the Licence Completeness Check
May 1, 2026 – CIRNAC’s Response to Round 2 of the Information Request Responses to the NWB
May 14, 2026 - Participation in a Working group with Agnico Eagleand the Kitikmeot Inuit Association
June 4 and 5, 2026 – Participation in a Working group with Agnico Eagle, ECCC, DFO and the Kitikmeot Inuit Association
June 19, 2026– CIRNAC’s submission of technical review comments
Notes: As the Nunavut Water Board has explained in their introduction and application history, Agnico Eagle, provided the Nunavut Water Board with an amendment and renewal application in regard to water licence 2AM-DOH1335.
The application has undergone a completeness check where CIRNAC commented on March 19 and April 20. In addition, CIRNAC communicated with the NWB on May 1 regarding the end of the completeness check. Technical review comments were submitted on June 19. Agnico response to comments on the Technical Review were submitted to the water board on July 3rd.
All technical comments are labeled as either resolved, partially resolved or not resolved. In the interest of time, we will only cover partially resolved or unresolved comments. We have used the term “resolved” to indicate that a resolution was found and that Agnico has resolved the department's concern. We have used the term “Partially Unresolved” to indicate that information provided by Agnico have only partially resolved the department’s concern or that further commitment is needed to resolve the concern. In cases where Agnico has not resolved or partially resolved CIRNAC’s concerns, comments are labeled as unresolved.
In the interest of time, technical review comments have been grouped according to CIRNAC’s main concerns.

## Slide 5: CIRNAC’s Recommendations Water Source Quality and Quantity (R-01 to R-03)
Key message : Robust baseline water data, comprehensive monitoring, discharge criteria, and adaptive management triggers are needed to support effective assessment and management of project water impacts throughout the mine life.
Lack of current seasonal water quality data and available capacity for Windy, Patch, and Doris Lakes and long-term (construction, operation and mine life), seasonally representative water quality monitoring.
Lack of a summary table of expected water quality and quantity over time for all sumps, monitoring stations, and discharge points, including adaptive management criteria/triggers for mitigation and contingency measures (where applicable).
CIRNAC requires information to access that water quality and quantity would not change based on the increase water withdrawal and mine activities proposed in this Water Licence amendment renewal application, to ensure protection of the receiving environment and informed regulatory oversight.
Unresolved
Notes: Three of the departments technical comments were related to water source quality and capacity.
CIRNAC seeks a robust baseline water quality data, comprehensive monitoring, discharge criteria and adaptative management triggers to support the effective assessment of current water quality and capacity and potential project water impacts throughout the mine life.
The information provided did not include the current baseline water quality data in a consolidated format, to support the assessment of baseline conditions and potential project effects. With respect to monitoring, the proponent indicated that they only plan on doing two years of sampling during operations at Windy Lake to confirm FEIS prediction and sampling will stop if predictions are confirmed. CIRNAC is looking clarification on how this would support the evaluation of potential changes in water quality during the full duration of operations.
The information provided didn’t include the requested consolidated summary of expected water quality and quantity across all relevant site locations, such as sumps, contact water ponds, collection points, or tundra discharge locations. Also, adaptive management criteria, water quality criteria, and associated management actions have not been presented in a consolidated format. CIRNAC is concerned that, without clearly presenting expected conditions alongside adaptive management and water quality criteria, it may be more difficult to identify early warning signs of water management issues. In the event of an unplanned discharge or spill, this could increase risks to the receiving environment.
CIRNAC is seeking to ensure that changes, if any, due to the increase water withdrawal and mine activities proposed in this Water Licence amendment renewal application could be properly identified and mitigated.
These comments are unresolved.

## Slide 6: CIRNAC’s Recommendations Water Management and Water Intake Infrastructure (R-04 & R-05)
Key Message: Information on water extraction systems and all water management infrastructure is required to support the affirmation that all current water management and water intake infrastructure is adequate to support the increase water withdrawal and mine activities proposed in this Water Licence amendment renewal application.
Lack a description of the current and planned method(s) of extraction and a description of the operating capacity of the pump(s).
Lack information regarding current water management infrastructure, including :
  Existing storage reservoirs;
  Watercourse crossings including pipelines, bridges, culverts or roads;
  Watercourse trainings including channel and bank alterations, culverts, spurs, erosion control, and artificial accretion;
  Diversions including ditches and dikes and their purposes.
CIRNAC is seeking consolidated information on water withdrawal operations and water management infrastructure to demonstrate that the current infrastructure is adequate to support the increase water withdrawal and mine activities proposed in this Water Licence amendment renewal application.
Unresolved
Notes: Two of the departments technical comments were related to water management and water intake infrastructure.
CIRNAC requested that Agnico provide a description of the methods of water extraction currently in use, as well as the operating capacity of the pumps associated with those systems. We also requested that Agnico provide complete and consolidated information regarding existing water management infrastructure. The requested information is necessary to assess whether the existing infrastructure remains suitable under the proposed amendment and renewal application.
As part of the July 3rd response, the proponent has affirmed that no changes to current infrastructure are necessary for the activities proposed under the amendment to proceed. However, the proponent has not shared any analysis or documentation to corroborate this statement at this time.
CIRNAC is seeking consolidated information on water withdrawal operations and water management infrastructure, such as the analysis or documentation supporting Agnico’s statement, to demonstrate that the current infrastructure is adequate to support the increase water withdrawal, water use and mine activities proposed in this Water Licence amendment renewal application.

## Slide 7: CIRNAC’s Recommendations Prediction Of Climate Trends
Key Message: Future climate change, including worst-case warming scenarios, must be considered in project planning and assessment to evaluate potential effects on infrastructure, operations, and water management.
Lack a description of the predicted future climate trends at the project site, including worst-case scenario projections using the Intergovernmental Panel on Climate Change’s Shared Socioeconomic Pathway – Representative Concentration Pathway 5-8.5.
CIRNAC recommends that the full sensitivity analysis be provided and an updated ICRP contains climate trends modelling using SSP5-8.5 scenario, to ensure the project is designed and managed with adequate consideration of long-term climate risks.
Partially resolved
Notes: The next Technical comment is related to prediction of climate trends.
Agnico has relied on the SSP2-4.5 climate scenario for its climate trend modelling and indicated that this scenario was considered the most appropriate given the project timeline into the 2030s and 2040s. They also provided limited results of a sensitivity analysis comparing the 4.5 and 8.5 model, which suggested relatively limited differences in some areas during the operational phase.
However, the sensitivity analysis comparing the 4.5 and 8.5 models was not provided as part of the application package and the summary of results presented focus on process water discharge, saline discharge, and water quality concentrations during the operational period. The results presented do not necessarily address other climate-sensitive factors relevant to the project, for example permafrost stability or extreme weather events. Agnico did indicate that the SSP2-8.5 scenario might be relevant to closure and post-closure planning.
CIRNAC recommends that the full sensitivity analysis be provided and when updated, the ICRP contains climate trends modelling using SSP5-8.5 scenario, to ensure the project is designed and managed with adequate consideration of long-term climate risks.
This comment is considered partially resolved, as the proponent did provide part of the sensitivity analysis and the comment could be resolved depending on the proponent’s commitment to share the requested information and to use the 8.5 scenario when updating the ICRP.

## Slide 8: CIRNAC’s Recommendations Information Gaps And Management Plans
Key Message: Updated management and emergency response plans and completion of outstanding information requests are needed to support a comprehensive assessment of project risks and mitigation measures.
The Water Management, Spill Contingency, Dam Emergency, and Emergency Response Plans should be updated within 90 days of issuance of the licence to ensure consistencies and address all relevant project phases.
CIRNAC recommends that the proponent provide responses to the information gaps to support the review process.
E.g. drainage patterns within the solid waste disposal area(s), a detailed list of proposed proximal sources, a map of the sources, and volume measurements of each source prior to using the proximal source.
CIRNAC is seeking greater clarity, complete documentation, and fulfillment of proponent commitments to ensure the project can be effectively reviewed and managed throughout all phases of development.
Partially resolved
Notes: The next department’s comments are related to Information Gaps and Management plans.
The proponent has provided clarification regarding the water management plan. CIRNAC is recommending that the Water Management, Spill Contingency, Dam Emergency, and Emergency Response Plans should be updated within 60 days of issuance of the licence to ensure consistencies and address all relevant project phases. CIRNAC is looking forward to working with the proponent to update other outstanding plans as needed and determine a timeline for submission. The issue is partially resolved, as a resolution could be achieved with commitments from the proponent.
In addition, CIRNAC recommends that the proponent provide responses to the information gaps to support the review process. In particular, CIRNAC requested that Agnico provide a detailed depiction of the drainage patterns within the solid waste disposal area(s).The proponent’s referenced map in Appendix 4-F Figure 3-1 does not show a zoomed in portion containing the landfill in Quarry 2 (the map cut off just prior to quarry 2) and as such does not depict the drainage pattern. The department considers this comment to be unresolved.
Also, CIRNAC requested that Agnico provide a detailed list of proposed proximal sources, a map of the sources, and volume measurements of each source. The proponent’s response on June 18th did not contain information regarding proposed proximal sources, or measures put in place to minimize impacts of withdrawal on water levels and flow rates of proximal sources. The department considers this comment to be unresolved. CIRNAC recommends that the board ensure that Agnico provide a list of proximal sources, as well as measures put in place to minimize impacts, prior to any withdrawal from those proximal sources.

## Slide 9
Status of CIRNAC TRCs R-10 to R-23
Key message: AEM's July 3, 2026 responses leave most CIRNAC requests unresolved.
In addition to TRC that were presented, CIRNAC submitted 14 Technical Review Comments on June 19, 2026: R-10 to R-23.
Those comments included 48 separate requests.
Responses received from AEM on the technical comments above;
27 of 48 responses (56%) were deemed non-responsive.
Only 3 of 48 requests (6%) were resolved or substantially clarified.
In the interests of time, the following slides will focus on only Four substantive deficiencies rather than reviewing all 48 requests. CIRNAC and AEM continue to engage to resolve these deficiencies through commitments from AEM. The wording of those commitments has yet to be finalized.
Notes: In addition to topics addressed by Pauline, I will provide an update on the status of additional Technical Review Comments submitted by CIRNAC to the NWB on June 19, 2026. That submission included 14 new Technical Review Comments (R-10 to R-23), which included 48 separate requests to AEM. Based on CIRNAC’s review of AEM’s July 3, 2026 responses, 27 of the 48 requests (i.e., 56%) were classified as non-responsive, meaning that AEM did not answer the specific request or provided information only peripherally related to it.
By extension, CIRNAC concluded that AEM provided 21 responses (i.e., 44%) that directly or partially dealt with CIRNAC’s specific requests. However, in most of those instances, the topic of the request has not been adequately resolved and additional information is required. Overall, only 3 of the 48 requests (i.e., 6%) were classified as resolved or substantially clarified; the remaining 94% of requests are unresolved.
In recognition of the limited time we have available today, CIRNAC will not provide a detailed update on the status of all 48 requests; doing so is beyond the time available to deliver this presentation. Instead, after the technical session, CIRNAC will separately file an update on the status of its Technical Review Comments with the Nunavut Water Board.
CIRNAC and AEM continue to engage to resolve these deficiencies through commitments from AEM. The wording of those commitments has yet to be finalized.
In the interim, during today’s presentation, I will focus on four substantive deficiencies with the Amendment Application.

## Slide 10: Deficiency 1: Tailings Management Strategy Remains Uncertain
Key message: The application does not clearly define what tailings strategy the NWB is being asked to approve.
The application identifies a phased transition to filtered dry-stack tailings as a preferred alternative.
AEM continues to indicate in responses that they preserve continued slurry deposition as an option and only characterize dry-stack implementation as conditional.
It remains unclear whether approval is being sought for:
a major expansion of slurry-tailings deposition;
a transition to dry-stack tailings; or
both ?
The alternatives have different implications for water demand, seepage, dust, closure and long-term water quality which have not been answered by AEM.
CIRNAC feels that in order to provide appropriate comment and recommendation AEM must commit to one strategy or fully assess each alternative and provide supporting documentation
Unresolved
Notes: The application does not clearly define the tailings management configuration that the NWB is being asked to approve. Notably, the original application documents describe a phased transition from slurry deposition to filtered dry-stack tailings as the preferred alternative. That preferred alternative is described as comprising an additional 9 Mt of slurry tailings, 25 Mt of filtered tailings in a “dry stack” and 7 Mt of paste tailings.
Contrary to what is stated in the application documents, during technical meetings held in Ottawa on June 4th, AEM’s representatives indicated that the tailings dry-stack was simply an option and that the company’s preferred alternative was to continue with the approved slurry deposition method. At the time CIRNAC noted the inconsistency between AEM’s statements in the meeting and the application document. Subsequently, on June 5th, AEM’s representatives indicated that they had mis-communicated and that the preferred tailings management approach was, indeed, to transition to dry-stack, consistent with the application documents.
However, AEM's subsequent responses to TRCs preserve the option to continue slurry deposition as the preferred tailings management strategy and characterize implementation of filtered tailings as conditional. There remains, therefore, confusion regarding what tailings management strategy is currently under review and subject to approval. Is it a significant expansion in the slurried tailings approach? Is it a new dry-stack tailings method? Or is AEM seeking approval for both methods.
This is not a minor design refinement. Slurry deposition and filtered dry-stack tailings have very different implications for water recovery and freshwater demand, TIA water inventory, dam-raise requirements, seepage and infiltration, oxygen exposure and geochemical behaviour, fugitive dust generation, closure design and long-term water quality.
The NWB should be able to identify the project configuration that it is being asked to approve and CIRNAC needs to understand what it should be reviewing. AEM's current position effectively seeks authorization for multiple very different tailings management configurations while retaining discretion to select between them later.
AEM should either clearly identify and commit to the proposed tailings management strategy or provide sufficient technical assessment of each alternative configuration that it seeks authorization to implement. This fundamental information should be provided during the current licensing phase, not through subsequent design submittals.

## Slide 11: Deficiency 2: Water Quality Predictions Rely on an Uncommitted Configuration
Key message: AEM takes best case modelling credit for dry-stack tailings combined with a geomembrane cover, but has not committed to either.
The long-term water quality and load balance modelling assumes transition to filtered dry-stack tailings, which may not occur.
Closure source terms assume a low-permeability geomembrane cover over the dry stack.
AEM now states that the geomembrane is only one potential mitigation measure, to be used 'if required.'
The modelling therefore demonstrates performance for the most favorable of tailings configuration options, but not necessarily the configuration AEM will construct at closure.
Modelled assumptions must be aligned with enforceable project and closure commitments.
Unresolved
Notes: The most significant technical deficiency with AEM’s application and TRC responses is the disconnect between the configuration assumed in water quality modelling and the configuration AEM is prepared to commit to implement. Specifically, the long-term water quality and load balance modelling assumes that the operation will transition to filtered dry-stack tailings. In addition, the source-term report assumes that the dry-stack tailings will be covered by a geosynthetic membrane followed by approximately 1 m of construction rock.
In essence, AEM’s modelling takes credit for a low-permeability geomembrane over the dry-stack area. However, AEM has also stated that the geomembrane is merely one possible mitigation measure and that further analysis will determine the appropriate mitigation 'if required.'
CIRNAC is concerned that AEM has taken water-quality credit for implementation of filtered tailings and a low-permeability geomembrane cover but has not committed to implementing either the modelled tailings configuration or the geomembrane closure measure.
In the opinion of CIRNAC it is not technically or regulatorily appropriate to use a high-performance and potentially costly closure mitigation to obtain approvals and then characterize that same mitigation as optional.
AEM should therefore do one or more of the following:
• commit to the modelled dry-stack and geomembrane configuration; or
• model the alternative tailings and closure configurations it seeks to retain; or
• demonstrate that any alternative ultimately selected will achieve environmental performance equivalent to or better than the modelled configuration.
Until this issue is resolved, CIRNAC lacks confidence that the water quality modelling will be reflective of actual management strategies. Water quality modelling must be aligned with enforceable project and closure commitments.

## Slide 12: Deficiency 3: Tailings Closure Concept Is Too Preliminary
Key message: Closure assumptions are being used to support approval before the closure design is adequately defined.
The current ICRP does not adequately define the dry-stack closure concept.
Information missing from the current submission include; lack of a selected cover system, infiltration target, oxygen-control strategy or measurable acceptance criteria.
AEM expects water quality to be acceptable without long-term treatment, but has not technically demonstrated that conclusion.
AEM proposes to materially update the ICRP after licence approval.
An updated ICRP addressing the amended tailings strategy should be reviewed and approved during the current proceeding.
Unresolved
Notes: AEM's responses confirm that the closure concept for the tailings facility remains preliminary and will be advanced through future closure updates. While CIRNAC accepts that not that every closure detail must be finalized during the current licensing process, the Department concludes that the current closure concept is not aligned with the proposed amendment. The deficiency is that the closure strategy for the project's tailings facility has not been selected, despite closure assumptions already being incorporated into the models used to predict long-term water quality.
The current closure does not adequately establish the proposed dry-stack cover system, required infiltration performance, the strategy for limiting oxygen ingress and sulphide oxidation, long-term seepage quality and quantity for the actual closure configuration, performance under future climate conditions, whether long-term active water treatment may be required, or measurable closure performance objectives and acceptance criteria. Despite this, AEM concludes, without technical evidence, that it expects closure water quality objectives to be achieved without long-term treatment. The deficiency is particularly significant because the available predictive modelling assumes a geomembrane that AEM has not committed to install.
CIRNAC notes that AEM proposes to update the closure plan after approval of the licence amendment. In CIRNAC's view, this reverses the appropriate regulatory sequence. Closure assumptions are already being used to support approval of the amended project and approximately 34 Mt of permanent tailings storage. In this context, an updated closure plan addressing the amended tailings management strategy should be submitted, reviewed and approved during the current licensing process. In the opinion of CIRNAC, it would be inappropriate to provide approval based on favorable closure assumptions embedded in predictive modelling and then determine the actual closure concept after approval.

## Slide 13: Deficiency 4: Expansion Has Not Been Reconciled with the Previous EA
Key message: AEM has not demonstrated, despite request, that the amended project remains within the previously assessed environmental envelope.
Mill throughput increases from 2,000 tpd to approximately 8,000 tpd.
Tailings placed in the TIA increase from approximately 18 Mt to approximately 34 Mt.
The amendment also involves major increases in mining and a substantially longer overall mine life.
AEM has not provided a direct FEIS comparison for total mined tonnes, waste rock, tailings or total project duration.
AEM should provide a complete quantitative reconciliation of the amended project against the FEIS.
Unresolved
Notes: AEM repeatedly characterizes the Operational Update as an optimization or refinement of the previously assessed Hope Bay Project. However, it has not provided the quantitative reconciliation necessary to substantiate that conclusion. For example, the application includes significant changes in project scale, including but not limited to: an increase in mill throughput from the previously licensed 2,000 tpd to approximately 8,000 tpd; an increase in tailings placed in the TIA from the previously approved approximately 18 Mt to approximately 34 Mt; major increases in the quantity of mining; and a significant extension to the Life of Mine.
Despite these changes, AEM has not provided a direct comparison of FEIS total mined tonnes versus revised total mined tonnes, FEIS waste rock quantities versus revised waste rock quantities, FEIS tailings quantities versus revised tailings quantities, or the original total project operating duration versus actual operations to date plus the proposed remaining mine life. Without this basic information, CIRNAC remains unable to verify AEM's central assertion that the amended project remains within the previously assessed environmental impact envelope.

## Slide 14: Conclusion
CIRNAC will continue to work together with AEM, the Nunavut Water Board and other interveners through the water licence application review process with the aim of protecting Nunavut’s inland water resources while promoting sustainable development.

## Slide 15
Qujannamiik
Thank you
Merci
ᖁᔭᓐᓇᒦᒃ