## Slide 1: Kitikmeot Inuit Association
Technical Submission
Doris North Type A Water Licence Amendment Application
Notes: Hello, I am John Roesch, the Senior Hope Bay Project Officer for the Department of Lands and Environment for the Kitikmeot Inuit Association. I am responsible for project oversite for the KIA and provide input into the regulatory process on the Hope Bay Project to both the NWB and NIRB. In performing this role, I make manage KIA’s consultants who are subject matter experts in the areas of wildlife, fisheries, aquatic environment, and geotechnical engineering.

## Slide 2: Technical Overview
This presentation provides an summary of KIA’s Technical Submission of TMAC’s amendment application regarding:
    Major Issues related to Type A Water Licence
    Final Environmental Assessment Guidelines
    KIA statement
    Recommendation
Notes: This presentation-follows the order presented in KIA’s Technical Submission, as prescribed by NWB – it focuses on key issues associated with mine infrastructure & the water licence changes.

## Slide 3: Major Issues to the Project and Type A Water Licence: Water Quality Predictions
Site-Wide Water and Load Balance:
Site-Wide Water and Load Balance (KIA-11A)
  Issue: The water quality modeling does not consider the effects of climate change & varying hydrological conditions.
  Recommendation: Update the water quality model to include climate change and define hydrological conditions that will affect the water load balance.
  Response and Status: TMAC ran variable hydrology models with sensitivity analysis.
  The review of changes in wet & dry condition indicated no impact on the load balance model or effluent quality. The issue is resolved.
Notes: Water Quality Predictions: Site Water and Load Balance
Site-Wide Water and Load Balance (KIA-11A)
  Issue: The water quality modeling does not consider the effects of climate change & varying hydrological conditions.
  Recommendation: Update site water quality model to include climate change as per the latest IPPCC. Define hydrological conditions modeled & how that will affect the water load balance.
  Response and Status: TMAC had run variable hydrology models based on 1953 to 2014 data. Water quality results of this sensitivity analysis was reviewed at the technical meeting in January.
  The review of changes in wet & dry condition indicated no impact on the load balance model or effluent quality. The issue is resolved.

## Slide 4: Major Issues to the Project and Type A Water Licence: Water Quality Predictions
Site-Wide Water and Load Balance:
Site-Wide Water and Load Balance (KIA-11B)
  Issue: The water & load balance model uses median values as inputs.
  Recommendation: Use 75th percentile concentrations as input values into model for “enriched” conditions.
  Response and Status: TMAC ran a sensitivity analysis using the 75th percentile inputs for background concentrations resulting in low toxicity levels below CCME and MMER guidelines. This issue is resolved.
Notes: Water Quality Predictions: Site-Wide Water and Load Balance
Site-Wide Water and Load Balance (KIA-11B)
  Issue:Water & load balance model uses median values to predict water quality & loadings which may underestimate potential effects to surface water.
  Recommendation: Use 75th percentile concentrations as input values into model to consider “enriched” conditions.
  Response and Status: TMAC had run a sensitivity analysis of the water & load balance using the 75th percentile for background concentrations & other input source terms. The results indicate low toxicity levels below CCME and MMER guidelines. This issue is resolved.

## Slide 5: Major Issues to the Project and Type A Water Licence: Water Quality Predictions
Site-Wide Water and Load Balance:
Site-Wide Water and Load Balance (KIA-11C)
  Issue: The model did not predict cyanide, mercury & selenium in the TIA, and mercury in the effluent discharge to Roberts Bay.
  Recommendation: Complete additional analysis for mercury, selenium, and cyanide concentrations in the TIA water.
  Response and Status: The model was updated to include cyanide, selenium, and mercury in the TIA & discharge to Robert’s Bay. Concentrations for cyanide, copper, mercury, and selenium were found to be extremely low. The issue is resolved.
Notes: Water Quality Predictions: Site-Wide Water and Load Balance
Site-Wide Water and Load Balance (KIA-11C)
  Issue: The model did not predict cyanide, mercury & selenium in TIA, & mercury in the effluent discharging to Roberts Bay from the Marine Outfall Box due to high detection limits or lack of data.
  Recommendation: Complete additional analysis for mercury & selenium using low-level detection limits. Also obtain additional information to predict cyanide concentrations in the source terms.
  Response and Status: TMAC updated the modeling to include cyanide, selenium, & mercury in the TIA & point of discharge to Robert’s Bay. Results indicate concentrations for cyanide, copper, mercury, and selenium were extremely low. The issue is resolved.

## Slide 6: Major Issues to the Project and Type A Water Licence: Water Quality Predictions
Groundwater Quality and Volume Predictions:
Hydrology (KIA-10)
  Issue: How groundwater inflow will be handled, including post closure.
  Recommendation: Provide details on the variance in the volume & quality of groundwater inflow and its management.
  Response and Status: The requested information was provided to KIA’s satisfaction and the issue is resolved.
Notes: Water Quality Predictions: Groundwater Quality and Volume Predictions
Hydrology (KIA-10)
  Issue: There was little discussion on how groundwater inflow (@ 3,000m3/d) will be handled, including post closure.
  Recommendation: Provide additional details regarding the variance in the volume & quality of groundwater to be managed; & management of ground water inflows during mining operations to provide assurance that dewatering rates would effectively handle groundwater inflows.
  Response and Status: TMAC provided the requested information to KIA’s satisfaction and the issue is resolved.

## Slide 7: Major Issues to the Project and Type A Water Licence: Water Quality Predictions
Roberts Bay Discharge:
Potential Interaction with Marine Environment (KIA-7)
  Issue: Saline groundwater & water from TIA have the potential to interact with marine environment.
  Recommendation: Variance in water discharge, chemical differences & the potential impact on seawater should be addressed in further detail.
  Response and Status: The information on groundwater quality and the saline variation of ocean discharge was below CCME guidelines. This issue is resolved.
Notes: Water Quality Predictions: Roberts Bay Discharge
Potential Interaction with Marine Environment (KIA-7)
  Issue: Saline groundwater & water from TIA have the potential to interact with marine environment. This concerns the variability of TIA discharge, salinity levels, & chemical differences between saline groundwater & seawater.
  Recommendation: Variance in water discharge, chemical differences & the potential impact on seawater should be addressed in further detail.
  Response and Status: TMAC provided information on groundwater quality and the saline variation of ocean discharge was below CCME guidelines. This issue is resolved.

## Slide 8: Major Issues to the Project and Type A Water Licence: Roberts Bay Discharge Monitoring
Aquatic Monitoring Framework (AEMP and EEM Program):
Roberts Bay Discharge and AEMP (KIA-6)
  Issue: Roberts Bay hosts waterfowl and mammals that feed on benthic food items like bivalves. Update AEMP in Roberts Bay to protect wildlife.
  Recommendation: AEMP changes should include increased sampling locations and frequency for diffuser outfall.
  Response and Status: The sensitivity analysis of water load balance indicates TIA effluent concentrations are below CCME and MMER guidelines. Proposed sampling locations in Robert Bay and the TIA were found to adequate for AEMP. This issue is resolved.
Notes: Roberts Bay Discharge Monitoring: Aquatic Monitoring Framework (AEMP and EEM Program)
Roberts Bay Discharge and AEMP (KIA-6)
  Issue: Roberts Bay hosts 9 waterfowl & at least 2 mammal species. That feed on benthic food items like bivalves. Update AEMP in Roberts Bay to protect wildlife.
  Recommendation: AEMP changes should include increased sampling locations and frequency for diffuser outfall.
  Response and Status: The sensitivity analysis of water load balance indicates TIA effluent concentrations are below CCME and MMER guidelines. Hydrodynamic modeling of discharge indicates dilutions of >180:1 within 1 m of diffuser and dilutions of 1000:1 to 10,000:1 at a distance of 250 m from the diffuser. Proposed sampling locations in Robert Bay and the TIA were reviewed and found adequate for AEMP. This issue is resolved.

## Slide 9: Major Issues to the Project and Type A Water Licence: Roberts Bay Discharge Monitoring
Effluent Discharge Criteria:
Mixing Zone Delineation (KIA-8)
  Issue: The methods used to predict water quality in Roberts Bay does not determine the size & properties of the mixing zone where water quality will be above the CCME guidelines.
  Recommendation: The size & shape of the mixing zone, where water quality will be above CCME guidelines should be modeled & presented, using 75th percentile concentrations.
  Response and Status: 3-D modeling of mixing zones, plume movement, and water quality concentrations using 75th percentile concentrations indicates that CCME water quality requirements were met within 1 m of the diffuser. The issue is resolved.
Notes: Roberts Bay Discharge Monitoring : Effluent Discharge Criteria
Mixing Zone Delineation (KIA-8)
  Issue: The methods used to predict water quality in Roberts Bay does not determine the size & properties of the mixing zone where water quality will be above the CCME guidelines.
  Recommendation: The size & shape of the mixing zone, where water quality will be above CCME guidelines should be modeled & presented, using 75th percentile concentrations.
  Response and Status: TMAC used a three-dimensional hydrodynamic modeling to simulate mixing zones, plume movement, & predict water quality concentrations (CCME) using 75th percentile concentrations. All marine CCME water quality requirements were met within 1 m of the diffuser with water quality similar to baseline conditions. The issue is resolved.

## Slide 10: Major Issues to the Project and Type A Water Licence: Roberts Bay Discharge Monitoring
Marine Water Quality Objectives:
Prediction of Environmental Effects on Water Quality (KIA-12)
  Issue: A water quality model is needed to determine the concentrations of nitrate in the mixing zone, and between deep and surface layers.
  Recommendation: Update the site water quality model to include the mixing zone modeling in Robert’s bay to predicts concentrations of nitrate and other parameters in the mixing zone, deep layer, and surface layer.
  Response and Status: The modeling results on plume size, shape, and concentration indicates that nitrate and other parameters were found to be well below CCME guidelines with the plume trapped well below the surface water layer. This issue is resolved.
Notes: Roberts Bay Discharge Monitoring: Marine Water Quality Objective
Prediction of Environmental Effects on Water Quality (KIA-12)
  Issue: A water quality model is needed to determine the concentrations of nitrate in the mixing zone & between deep & surface layers. Enriched nitrate in the surface layer may cause excessive algal growth.
  Recommendation: Update site water quality model to include the mixing zone modeling in Robert’s bay that predicts the concentrations of nitrate & other parameters in the mixing zone, deep layer & surface layers.
  Response and Status: TMAC has provided modeling results on plume size, shape, & concentration in Roberts Bay & Melville Sound. Nitrate and other parameters were found to be well below CCME guidelines with the plume trapped well below the surface water layer. This issue is resolved.

## Slide 11: Major Issues to the Project and Type A Water Licence: Roberts Bay Discharge Monitoring
Marine Water Quality Objectives:
Increasing Contaminants of Potential Concern in Roberts Bay (KIA-9)
  Issue: How will future projects affect water quality in Robert’s Bay?
  Recommendation: TMAC should provide a discussion on how CCME water quality criteria in Robert’s Bay will be met after Phase 2 starts.
  Response and Status: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue was discussed and resolved by KIA and TMAC at the January Technical Meeting.
Notes: Roberts Bay Discharge Monitoring: Marine Water Quality Objectives
Increasing Contaminants of Potential Concern in Roberts Bay (KIA-9)
  Issue: How will future projects affect water quality in Robert’s Bay?
  Recommendation: TMAC should provide a discussion on how CCME water quality criteria in Robert’s Bay will be met after Phase 2 starts.
  Response and Status: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue was discussed and resolved by KIA and TMAC at the January Technical Meeting.

## Slide 12: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Use of Waste Rock in construction:
Waste Rock Management Plan:
No Issues
Notes: Waste Rock Tailings: Use of Waste Rock in construction & Waste Rock Management Plan
No Issues

## Slide 13: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Tailings Management:
TIA Expansion Capacity (KIA-1)
  Issue: Does the TIA have sufficient capacity for Madrid/Boston projects?
  Recommendation: TMAC should provide an assessment of TIA capacity for future projects & should include these project in the CEA.
  Response and Status: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue is resolved.
Notes: Waste Rock and Tailings: Tailings Management
TIA Expansion Capacity (KIA-1)
  Issue: Does the TIA have sufficient capacity for Madrid/Boston projects?
  Recommendation: TMAC should provide an assessment of TIA capacity for future projects & should include these project in the CEA.
  Response and Status: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue was discussed and resolved by KIA and TMAC at the January Technical Meeting.

## Slide 14: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Tailings Management:
TIA Wildlife Attraction and Deterrence (KIA-2)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  Recommendation: An adaptive management program detailing the frequency, thresholds, and methods of monitoring and mitigation.
  Response and Status: TMAC has agreed to develop a monitoring plan to detect wildlife attraction and feeding in or near the TIA. This includes a risk assessment and implementation of wildlife deterrents as necessary.
  The issue is resolved.
Notes: Waste Rock and Tailings: Tailings Management
TIA Wildlife Attraction and Deterrence (KIA-2)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  Recommendation: An adaptive management program with several details on frequency, thresholds, and methods of monitoring and mitigation.
  Response and Status: TMAC has agreed to develop a monitoring plan to detect wildlife attraction & feeding in or near the TIA, in combination with other monitoring. Based on results, will conduct a risk assessment & implement wildlife deterrents as necessary.
  This issue was discussed thoroughly and was resolved by KIA and TMAC.

## Slide 15: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Tailings Management:
TIA NPAG Tailings Cover Depth (KIA-5)
  Issue: The proposed 0.3 m depth of quarry rock cap for the tailings beach upon closure is not sufficient.
  Recommendation: Use 75th percentile leach as input values into model when predicting containment release from the TIA.
  Response and Status: The tailings beach source terms were recalculated using the 75th percentile leach rates. Results indicate that the 0.3 m tailing cover is adequate and the development of boils is low. This issue is resolved.
Notes: Waste Rock and Tailings: Tailings Management
TIA NPAG Tailings Cover Depth (KIA-5)
  Issue: The proposed 0.3 m depth of quarry rock cap for the tailings beach upon closure is not sufficient.
  Recommendation: Use 75th percentile leach as input values into model when predicting containment release from the TIA.
  Response and Status: TMAC had recalculated the tailings beach source terms using the 75th percentile leach rates from the humidity cell tests. Results of new model indicate that the 0.3 m tailing cover is adequate and the development of boils is low. This issue is resolved.

## Slide 16: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Tailings Monitoring:
TIA Floatation Tailings Dust Fall and Leaching (KIA-3)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  Recommendation: An adaptive management program detailing the frequency, thresholds, and methods of monitoring and mitigation.
  Response and Status: A sensitivity analysis of TIA water quality indicates a very low concentration of toxic substances that are well below CCME guidelines.
  The issue is resolved.
Notes: Waste Rock and Tailings: Tailings Monitoring
TIA Floatation Tailings Dust Fall and Leaching (KIA-3)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  Recommendation: An adaptive management program with several details on frequency, thresholds, and methods of monitoring and mitigation.
  Response and Status: The review of TIA water quality from the sensitivity analysis indicated that tailings were very low in concentration of toxic substances and were well below CCME guidelines.
  This issue was discussed thoroughly and was resolved by KIA and TMAC.

## Slide 17: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Tailings Monitoring:
TIA Elevated Parameters of Potential Concern Upon Closure(KIA-4)
  Issue: Water and load balance model uses median values to predict water quality & loadings.
  Recommendation: Use 75th percentile concentrations for model inputs for “enriched” conditions.
  Response and Status: A sensitivity analysis of the water & load balance using the 75th percentile concentrations for model inputs resulted in toxicity levels being below CCME and MMER guidelines, and being non-toxic to Caribou and Birds. This issue is resolved.
Notes: Waste Rock and Tailings: Tailings Monitoring
TIA Elevated Parameters of Potential Concern Upon Closure(KIA-4)
  Issue: Water & load balance model uses median values to predict water quality & loadings which may underestimate potential effects to surface water.
  Recommendation: Use 75th percentile concentrations as input values into model to consider “enriched” conditions.
  Response and Status: TMAC had run a sensitivity analysis of the water & load balance using the 75th percentile for background concentrations & other input source terms. Results were found to below CCME and MMER guidelines and the water was non-toxic to Caribou and Birds. This issue is resolved.

## Slide 18: Major Issues to the Project and Type A Water Licence: Waste Rock and Tailings
Underground Disposal of Impacted Waste Rock:
No Issues
Notes: Waste Rock and Tailings: Underground Disposal of Impacted Waste Rock
No Issues

## Slide 19: Major Issues to the Project and Type A Water Licence: Mitigation Measures
Doris Lake and Outflow Water Levels:
Doris Lake Water Levels (KIA-13)
  Issue: Groundwater inflow could affect Doris Lake water levels, fisheries, spawning habitat, and egg incubation.
  Recommendation: Include baseline information to update the effects assessment, guide mitigation and monitoring plans.
  Response and Status: Additional data collection to quantify effects to fish & fish habitat in Doris Lake was done and reviewed. The issue is resolved.
Notes: Mitigation Measures: Doris Lake and Outflow Water Levels
Doris Lake Water Levels (KIA-13)
  Issue: Groundwater inflow will affect Doris Lake water levels. Potential effects on fisheries, in particular spawning habitat & egg incubation, are currently unknown.
  Recommendation: Additional work was completed in 2015 to characterise the fish habitat around Doris Lake. It is recommend that this baseline information be presented, & used to update the effects assessment & guide mitigation & monitoring plans, as needed.
  Response and Status: TMAC has completed additional data collection to quantify effects to fish & fish habitat in Doris Lake. This information was reviewed & assessed. The issue is resolved.

## Slide 20: Major Issues to the Project and Type A Water Licence: Mitigation Measures
Construction and Operation of Roberts Bay Discharge Pipeline:
Road and Water Crossing:
Sediment Quality:
Effluent Buoyancy: KIA-12
Dust Suppressant of Tailings:
No Issues
Notes: Mitigation Measures: Construction and Operation of Roberts Bay Discharge Pipeline, Road and Water Crossing, Sediment Quality, Effluent Buoyancy, and Dust Suppressant of Tailings
No Issues

## Slide 21: Major Issues to the Project and Type A Water Licence: Water Treatment
Water and Sewage Treatment:
No Issues
Notes: Water Treatment: Water and Sewage Treatment
No Issues

## Slide 22: Major Issues to the Project and Type A Water Licence: Management Plans and Reports
Content of Plans:
The KIA has been involved with and reviewed the EEM Program, AEMP, GWMP, TIA OMS Manual, and the proposed changes to the SNP and found everything to be adequate.
No Issues
Notes: Management Plans and Reports: Content of Plans
The KIA has been involved with and reviewed the EEM Program, AEMP, GWMP, TIA OMS Manual, and the proposed changes to the SNP and found everything to be adequate.
No Issues

## Slide 23: Major Issues to the Project and Type A Water Licence: Management Plans and Reports:
Updates to Plans:
Approval of Plans:
No Issues
Notes: Management Plans and Reports: Update to Plans and Approval of Plans
No Issues

## Slide 24: Final Environmental Assessment Guidelines:
Eco-Systemic & Socio-Economic Effects:
Framework Agreement and IIBA,
Net Smelter Royalty Agreement,
Water and Wildlife Compensation Agreement,
Mineral Rights Agreement with NTI, and
KIA shareholdings in TMAC Resources Inc.
All of this creates substantial benefits for Inuit in the Kitikmeot region.
Notes: The KIA receives monetary compensation through a variety of agreements. Direct compensation through the Framework Agreement and IIBA for land access, quarry materials and water usage. Royalties from gold production plus shareholdings in TMAC.
NTI also gets a royalty on profit under its Mineral Rights Agreement with TMAC Resources Inc. All of this creates a substantial benefit for Inuit in the region.

## Slide 25: KIA Statement:
KIA has resolved all technical issues brought forward to the Technical Meeting through our on-going collaboration with TMAC Resources Inc.
The final resolution of reclamation security is still pending at this time.
Notes: KIA has resolved all technical issues brought forward to the Technical Meeting through our on-going collaboration with TMAC Resources Inc.
The final resolution of reclamation security is still pending at this time.

## Slide 26: KIA Statement:
The KIA and TMAC have signed a water compensation agreement as part of the Framework Agreement for the Doris North Project.
This agreement addresses Inuit Article 20 rights and TMAC compensation obligations.
Direct compensation is provide to KIA for land access, quarry materials and water usage.
KIA also receives royalties from gold production as does NTI.
Notes: In addition to the technical issues raised, the KIA has signed with TMAC a comprehensive Framework Agreement for land access compensation and an Inuit Impact and Benefit Agreement (IIBA).
The IIBA addresses Inuit interests in the areas of employment, contracting, and training in relation to the Hope Bay Project as a whole through its entire life span.
Under the IIBA an Inuit Environmental Advisory Committee (IEAC) has been established with TMAC which complements KIA’s current environmental activities in the Department of Lands and Environment. The IEAC allows for the local community to have input directly to TMAC on environmental concerns.
Through the Implementation Committee with KIA and TMAC representatives, measures of employment, business development, and training are being developed which fulfills socio-economic obligations under the NLCA.

## Slide 27: KIA Statement:
KIA currently has $3.49 million is letters of credit from TMAC.
KIA also currently has $8.0 million Corporate Guarantee under Schedule K of the Commercial Lease for Doris North for a total of $11.49 million.
In addition to this, KIA has a General Security Agreement (GSA) under Schedule I of the Commercial Lease providing a claim on TMAC Assets.
Notes: The KIA currently has $3.49 million in letters of credit, an $8.0 million Corporate Guarantee, and General Security Agreement to back the Corporate Guarantee giving KIA a claim on TMAC assets.

## Slide 28: KIA Statement:
The KIA considers the current amount of security to be inadequate for the Doris North mine site.
KIA’s engineering consultant reviewed TMAC and INAC Reclamation Security cost estimates.
Major conclusions:
  $28.94 million quantum is reasonable and more accurate.
  $24.20 and $4.74 million land and water split (84% Land,16% Water).
  Residual risks and cost escalation identified with a contingency of 20%, KIA agrees with TMAC quantum and contingency.
Notes: The current amount of security of $11.49 million is inadequate security for the Doris North mine site give project changes and development.
The KIA’s engineering consultant has reviewed TMAC and INAC reclamation cost models. TMAC’s $28.94 million quantum for security is reasonable and the split in land and water liability is 84% and 16%.
A contingency of 20% exists within the TMAC reclamation estimate. Residual risks and cost escalators as well as questions raised by KIA’ consultant were discussed with TMAC and their engineering consultant. All questions were satisfactorily answered and the KIA accepts and supports TMAC’s reclamation cost estimate for the Doris North mine site.

## Slide 29: KIA Statement:
INAC’s reclamation cost estimate is $44.12 million.
$43.42 million (98%) is IOL and $0.7 million (2%) is Crown Land.
Of the $43.42 million, $19.71 million (45%) was allotted to land liability and $23.72 million (55%) was allotted to water liability.
KIA finds this split of land and water liability to be unreasonable given its experience with the Orbit 25 brine spill.
Notes: INAC’s engineering consultant has a reclamation cost estimate of $44.12 million which is substantially higher than TMAC’s estimate. This primarily due to indirect costs being 175% higher than TMAC’s estimate of indirect costs. INAC’s estimate uses a 5 year time horizon for reclamation in contrast to TMAC’s approximately 2 year time-horizon for preforming reclamation work. INAC’s estimate has about 50% the productivity of TMAC’s estimate which KIA finds questionable.
The INAC estimate acknowledges that 98% of the quantum is associated with IOL while only 2% is Crown Land.
The $43.42 million of IOL security has a split of land water liability of 45% and 55% respectively which the KIA finds unreasonable given our experience with the Newmont and Orbit 25 brine spill at Boston Camp in July of 2011.
Drilling fluid containing potassium chloride had spilled onto the land and subsequently entered a near by water body. About 1200 square metres of tundra was damaged due to elevated chloride levels. The deleterious substance had entered the water body and dissipated quickly in a few days with no loss of fish or damage to the aquatic environment.
Environment Canada at the time charged Newmont and Orbit Grant with breaking Federal environmental laws. Both Newmont and Orbit Grant agreed to contribute to Environment Canada’ environmental fund. No reclamation work was done by the Federal Government to the lake since no damage was done.
KIA investigated possible means of land reclamation, if no actions are taken it will take 15 to 20 years for the land to recover through natural revegetation. Human intervention would require experimentation in the restoration of tundra and remediation work based on experimental results. The human intervention and reclamation of land would be about $3 million.
This clearly illustrates that the liability is primarily with the land and not the water. INAC’s split of land and water liability of 45% and 55% would expose KIA to an excessive amount of risk.

## Slide 30: KIA Statement:
Given this and the substantial benefits that will be obtained for Inuit from the project we believe that the amendment of the Doris North Type A Water Licence is warranted and in the best interest of the Inuit people pending the satisfactorily resolution of reclamation security and the split of land and water liability.
Notes: The KIA strongly believes that given the substantial benefits to the Inuit and that all technical issue have been resolved that the amendment of the Doris North Type A Water Licence is warranted. This pending satisfactorily resolving the split of land and water liability with INAC.
If the split of land and water liability is not resolved, KIA still supports the amendment of the water licence and exercise the conditions of its Framework Agreement and Commercial Lease with TMAC to meet its reclamation needs.

## Slide 31: Recommendations:
KIA recommends approval of the TMAC application for amendment to Certificate 003 for the Doris North Project.
Thank you
Questions?
Notes: KIA recommends approval of the TMAC application for amendment of the Type A Water licence for the Doris North mine site.
Thank you
Questions?