## Slide 1: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ
ᐊᐅᓚᑦᓯᔾᔪᑎᓄᑦ ᑎᑎᕋᖅᓯᒪᔪᑦ ᑐᓂᔭᐅᔪᑦ
ᑐᐊᕆᔅ ᓄᐊᑦ ᐅᔭᕋᖕᓂᐊᕐᕕᖓᓐᓂ Type A ᐃᒪᓕᕆᔾᔪᑎᒥᒃ ᓚᐃᓴᓐᓯᖓᓐᓄᑦ ᐋᖅᑭᒋᐊᕆᔪᒪᓪᓗᑎᒃ ᑐᒃᓯᕋᐅᑎᓕᐊᖏᓐᓄᑦ
Notes: Hello, I am John Roesch, the Senior Hope Bay Project Officer for the Department of Lands and Environment for the Kitikmeot Inuit Association. I am responsible for project oversite for the KIA and provide input into the regulatory process on the Hope Bay Project to both the NWB and NIRB. In performing this role, I make manage KIA’s consultants who are subject matter experts in the areas of wildlife, fisheries, aquatic environment, and geotechnical engineering.

## Slide 2: ᐊᐅᓚᑦᓯᔾᔪᑎᑦ ᖃᓄᐃᓕᖓᖕᒪᖔᑕ
ᐅᑯᐊ ᐅᓂᒃᑳᖑᔪᑦ ᓇᐃᓈᖅᓯᒪᔪᑦ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐊᐅᓚᑦᓯᔾᔪᑎᓄᑦ ᑎᑎᕋᖅᓯᒪᔪᑎᒍᑦ ᑐᓂᔭᖏᓐᓂᒃ TMAC-ᑯᑦ ᐋᖅᑭᒋᐊᕈᑎᒋᔪᒪᔭᖓᓐᓄᑦ ᑐᒃᓯᕋᐅᑎᖓᓐᓄᑦ ᐱᓪᓗᒋᑦ ᐅᑯᐊ:
    ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐊᒃᑐᐊᓂᖃᖅᑐᑦ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ
    ᑭᖑᓪᓕᖅᐹᖅᓯᐅᑎᑦ ᐊᕙᑎᒧᑦ ᕿᒥᕐᕈᓂᕐᒧᑦ ᒪᓕᒐᖏᑦ
    ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᖏᑦ
    ᐊᑐᓕᖁᔭᓕᐊᖅ
Notes: This presentation-follows the order presented in KIA’s Technical Submission, as prescribed by NWB – it focuses on key issues associated with mine infrastructure & the water licence changes.

## Slide 3: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑕᐅᔪᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒥᒃ ᓱᕈᖅᐸᓪᓕᐊᑎᑦᓯᓂᐊᕐᓂᖓᓄᑦ ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ
ᓇᔪᒐᖓ - ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ:
ᓇᔪᒐᖓ-ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ (KIA-11A)
  ᐱᔾᔪᑕᐅᔪᖅ: ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑕᐅᔪᖅ ᐱᖃᓯᐅᔾᔨᓯᒪᖏᒻᒪᑦ ᐊᒃᑐᐃᓂᕆᔪᓐᓇᖅᑕᖓᓂᒃ ᓯᓚᐅᑉ ᐊᓯᔾᔨᖅᐸᓪᓕᐊᓂᖓᑕ ᐊᒻᒪ ᐊᓯᔾᔨᖅᐸᓪᓕᐊᓂᖏᑕ ᐃᒪᐅᑉ ᐃᖏᕐᕋᓂᖏᑕ.
  ᐊᑐᓕᖁᔭᓕᐊᑦ: ᑐᓴᖅᑎᑦᓯᓂᖅ ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑎ ᐱᖃᓯᐅᔾᔨᓯᒪᖁᓪᓗᒍ ᓯᓚᐅᑉ ᐊᓯᔾᔨᖅᐊᓪᓕᐊᓂᖓᓄᑦ ᐊᒻᒪ ᓇᓗᓇᐃᖅᑕᐅᓗᑎᒃ ᐃᒪᐅᑉ ᐊᖏᕐᕋᓂᕆᔭᖓ ᐊᒃᑐᐃᓂᖃᕈᓐᓇᕐᓂᖓᓂᒃ ᐃᒪᐅᑉ ᐅᓯᔭᐅᓂᕆᔭᖓᑕ ᐅᖁᒪᐃᓐᓂᖓᓂᒃ.
  ᕿᐅᔾᔪᑎ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC-ᑯᑦ ᐊᐅᓚᑦᓯᓚᐅᖅᑐᑦ ᐊᔾᔨᒌᖏᑦᑐᓂᒃ ᐃᒪᐅᑉ ᐃᖏᕐᕋᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑎᓂᒃ ᐊᑐᕐᖢᑎᒃ ᐃᒃᐱᖕᓇᕐᓂᖏᓐᓄᑦ ᖃᐅᔨᓴᐅᑎᓂᒃ.
  ᕿᒥᕐᕈᔭᐅᓂᖏᑦ ᐊᓯᔾᔨᖅᑕᐅᔪᑦ ᐃᓗᐊᓂ ᐃᒪᖅᓱᑦ ᐊᒻᒪ ᐸᓂᖅᑐᑦ ᓄᓇᐃᑦ ᓇᓗᓇᐃᖅᓯᓚᐅᖏᑦᑐᖅ ᐊᒃᑐᐃᓂᖃᕋᔭᖏᓐᓂᖓᓂᒃ ᐅᓯᔭᐅᔪᓄᑦ ᐆᒃᑐᕋᐅᑕᐅᔪᒧᑦ ᐅᕝᕙᓘᓐᓃᑦ ᐃᒪᕐᓗᑯᑦ ᐃᒋᑕᐅᔪᑦ ᐱᐅᓂᕆᔭᖓ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Water Quality Predictions: Site Water and Load Balance
Site-Wide Water and Load Balance (KIA-11A)
  Issue: The water quality modeling does not consider the effects of climate change & varying hydrological conditions.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Update site water quality model to include climate change as per the latest IPPCC. Define hydrological conditions modeled & how that will affect the water load balance.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC had run variable hydrology models based on 1953 to 2014 data. Water quality results of this sensitivity analysis was reviewed at the technical meeting in January.
  The review of changes in wet & dry condition indicated no impact on the load balance model or effluent quality. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.

## Slide 4: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑕᐅᔪᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒥᒃ ᓱᕈᖅᐸᓪᓕᐊᑎᑦᓯᓂᐊᕐᓂᖓᓄᑦ ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ
ᓇᔪᒐᖓ - ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ:
ᓇᔪᒐᖓ-ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ (KIA-11B)
  ᐱᔾᔪᑎ: ᐃᒪᕐᒧᑦ ᐊᒻᒪ ᐅᓯᔭᐅᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑎᐅᔪᖅ ᐊᑐᕐᒪᑕ ᐊᑯᓐᓂᐊᓃᑦᑐᓂᒃ ᑭᒡᓕᖃᕐᖢᑎᒃ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓᓂᒃ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᑐᖔᕐᓗᑎᒃ 75th ᐳᓴᓐᑎᒥᒃ ᑭᒡᓕᖃᖅᑎᑦᑎᓗᑎᒃ ᐆᒃᑐᕋᐅᑎᒧᑦ “ᐱᐅᓯᒋᐊᖅᑕᐅᖁᓪᓗᒋᑦ” ᖃᓄᐃᓐᓂᐅᔪᑦ.
  ᑭᐅᔾᔪᑎ ᐊᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC-ᑯᑦ ᖃᐅᔨᓴᐃᓚᐅᕐᒪᑕ ᐃᒃᐱᖕᓂᕐᓂᖓᓄᑦ ᐊᑐᕐᖢᑎᒃ 75th ᐳᓴᓐᑎᒥᒃ ᑭᒡᓕᖃᖅᑎᑦᑎᓪᓪᓗᑎᒃ ᓱᕈᕐᓇᖅᑐᖓ ᐊᒃᐸᓯᖕᓂᖅᓴᐅᖁᓪᓗᒍ ᐅᑯᓇᓐᖓᑦ ᓱᕈᕐᓇᖅᑐᑦ CCME ᐊᒻᒪᓗ MMER ᒪᓕᒐᖏᓐᓂᑦ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Water Quality Predictions: Site-Wide Water and Load Balance
Site-Wide Water and Load Balance (KIA-11B)
  Issue:Water & load balance model uses median values to predict water quality & loadings which may underestimate potential effects to surface water.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Use 75th percentile concentrations as input values into model to consider “enriched” conditions.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC had run a sensitivity analysis of the water & load balance using the 75th percentile for background concentrations & other input source terms. The results indicate low toxicity levels below CCME and MMER guidelines. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 5: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑕᐅᔪᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒥᒃ ᓱᕈᖅᐸᓪᓕᐊᑎᑦᓯᓂᐊᕐᓂᖓᓄᑦ ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ
ᓇᔪᒐᖓ - ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ:
ᓇᔪᒐᖓ-ᐃᒪᐅᑉ ᐊᖏᓂᖓ ᐊᒻᒪ ᐅᓯᔭᐅᔪᓐᓇᕐᓂᖓ (KIA-11C)
  ᐱᔾᔪᑎ: ᐆᒃᑐᕋᐅᑎᐅᔪᖅ ᓇᓕᖅᑯᑦᑕᐃᔾᔪᑎᖃᓚᐅᖏᒻᒪᑦ ᓱᕈᕐᓇᖅᑐᓄᑦ cyanide, ᐊᑭᕐᕉᔭᖃᕐᓂᖓᓂᒃ & selenium ᐃᓗᐊᓂ ᖃᐅᔨᓴᐃᔾᔪᑎᖏᑕ, ᐊᒻᒪᓗ ᐊᑭᕐᕉᔭᖃᕐᓂᖓᓂᒃ ᐃᒪᕐᓗᑯ ᐃᕐᕈᖅᓴᐃᔾᔪᑎᕕᓂᖅ ᐃᒋᑕᐅᓯᒪᔪᖅ ᑯᕕᔭᐅᓯᒪᓪᓗᓂ ᕋᐴᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓄᑦ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐱᔭᕇᖅᑕᐅᓗᑎᒃ ᕿᒥᕐᕈᓇᒍᑎᐅᔪᑦ ᐊᑭᕐᕉᔭᕐᒥᒃ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓᓄᑦ, ᓴᐃᓕᐊᒻᒥᒃ, ᐊᒻᒪᓗ ᓴᐃᓇᐃᑦᒥᒃ ᐃᓗᐊᓂ ᐃᒪᕐᓗᑰᑉ ᐃᕐᕈᖅᓴᐃᔾᔪᑎᕕᓂᐅᑉ ᐃᒪᖓᑕ.
  ᑭᐅᔾᔪᑎ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᐆᒃᑐᕋᐅᑎᐅᔪᖅ ᓄᑖᕈᕆᐊᖅᑕᐅᓚᐅᖅᑐᖅ ᐱᖃᑎᓯᐅᔾᔨᓯᒪᓂᐊᕐᒪᑦ ᓱᕈᕐᓇᖅᑐᓂᒃ ᓴᐃᓇᐃᑦᒥᒃ, ᓴᐃᓕᐊᒻᒥᒃ, ᐊᒻᒪᓗ ᐊᑭᕐᕉᔭᕐᒥᒃ ᐃᓗᐊᓂ ᐃᒪᕐᓗᑰᑉ ᐃᕐᕈᖅᓴᐃᔾᔪᑎᕕᓂᐅᑉ ᐊᒻᒪ ᑯᕕᔭᐅᔪᑉ ᕌᐳᑦᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓄᑦ. ᖃᐅᔨᓴᖅᑕᐅᓕᕋᒥ ᖃᐅᔨᓚᐅᖅᑐᑦ ᓴᐃᓇᐃᑦ, ᑲᓐᓄᔭᖅ, ᐊᑭᕐᕉᔭᖅ, ᐊᒻᒪᓗ ᓴᐃᓕᐊᒻ ᐊᒃᐸᓯᒃᑑᓂᖏᓐᓂ. ᑕᒪᑐᒧᖓᓗ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Water Quality Predictions: Site-Wide Water and Load Balance
Site-Wide Water and Load Balance (KIA-11C)
  Issue: The model did not predict cyanide, mercury & selenium in TIA, & mercury in the effluent discharging to ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ from the Marine Outfall Box due to high detection limits or lack of data.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Complete additional analysis for mercury & selenium using low-level detection limits. Also obtain additional information to predict cyanide concentrations in the source terms.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC updated the modeling to include cyanide, selenium, & mercury in the TIA & point of discharge to Robert’s Bay. Results indicate concentrations for cyanide, copper, mercury, and selenium were extremely low. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.

## Slide 6: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑕᐅᔪᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒥᒃ ᓱᕈᖅᐸᓪᓕᐊᑎᑦᓯᓂᐊᕐᓂᖓᓄᑦ ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ
ᓄᓇᐅᑉ ᐃᓗᐊᓂ ᐃᒪᐅᑉ ᐱᐅᓂᖓ ᐊᒻᒪ ᖃᓄᖅ ᐊᒃᑎᒋᖕᒪᖔᑕ ᓇᓚᐅᑦᑖᖅᑕᐅᓯᒪᔪᑦ:
ᐃᒪᐅᑉ ᐃᖏᕐᕋᓂᐊ (KIA-10)
  ᐱᔾᔪᑎ: ᖃᓄᖅ ᓄᓇᐅᑉ ᐃᓗᐊᒍ ᐃᒪᖅ ᐃᖏᕐᕋᔪᖅ ᑲᒪᒋᔭᐅᓂᐊᕐᒪᖔᑦ, ᐱᖃᓯᐅᑎᓗᒍ ᑭᖑᕐᖓᒍᑦ ᐅᔭᕋᖕᓂᐊᕐᕕᒃ ᒪᑐᓯᒪᓕᖅᑎᓪᓗᒍ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᓇᓗᓇᐃᖅᓯᔾᔪᑎᓂᒃ ᑐᓂᓯᓗᑎᒃ ᐅᓂᒃᑳᖅᓯᒪᔪᓂᒃ ᐊᒃᑎᒋᓂᕆᔭᖓᓂᒃ ᐃᒪᐅᑉ ᓄᓇᐅᑉ ᐃᓗᐊᓃᑦᑐᑉ ᐃᖏᕐᕋᓂᕆᔭᖓᓄᑦ ᐊᒻᒪ ᖃᓄᖅ ᒥᐊᓂᕆᔭᐅᓂᐊᕐᒪᖔᑦ
  ᑭᐅᔾᔪᑎ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᑐᒃᓯᕋᖅᑕᐅᓯᒪᔪᑦ ᑐᓴᒐᒃᓴᑦ ᑐᓂᔭᐅᓯᒪᓕᖅᑐᑦ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᓐᓄᑦ ᓈᒻᒪᒋᔭᐅᓕᖅᑐᖅ ᐊᒻᒪ ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Water Quality Predictions: Groundwater Quality and Volume Predictions
Hydrology (KIA-10)
  Issue: There was little discussion on how groundwater inflow (@ 3,000m3/d) will be handled, including post closure.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Provide additional details regarding the variance in the volume & quality of groundwater to be managed; & management of ground water inflows during mining operations to provide assurance that dewatering rates would effectively handle groundwater inflows.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC provided the requested information to KIA’s satisfaction and ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.

## Slide 7: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑕᐅᔪᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒥᒃ ᓱᕈᖅᐸᓪᓕᐊᑎᑦᓯᓂᐊᕐᓂᖓᓄᑦ ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ
ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᖅ:
ᐊᒃᑐᐃᔪᓐᓇᕐᓂᖓ ᐃᒪᕐᒥᐅᑕᓄᑦ (KIA-7)
  ᐱᔾᔪᑎ: ᑕᕆᐅᖅ ᓄᓇᐅᑉ ᐃᓗᐊᓂ ᐃᒪᖅ ᐊᒻᒪ ᐃᒪᖅ ᐃᕐᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᓱᕈᖅᓯᔪᓐᓇᕐᒪᑦ ᑕᕆᐅᕐᒧᐊᕈᓂ ᐊᒻᒪ ᑕᕆᐅᕐᒥᐅᑕᓄᐊᕈᓐᓇᕐᒪᑦ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᔾᔨᒌᖏᑦᑐᑦ ᐃᒪᖅ ᑯᕕᑎᑕᐅᔪᖅ, ᓱᕈᕐᓇᖅᑐᓂᒃ ᐃᓚᖃᕐᓂᖓ ᐊᔾᔨᒌᖏᓐᓂᖏᑦ ᐊᒻᒪ ᖃᓄᖅ ᐊᒃᑐᐃᑎᒋᔪᓐᓇᕐᒪᖔᑦ ᑕᕆᐅᕐᒧᑦ ᑯᕕᑎᑕᐅᓐᓂᕈᓂ ᑕᒪᓐᓇ ᑭᐅᔭᐅᑦᑎᐊᕆᐊᖃᕐᓂᐊᖅᑐᖅ ᐃᓗᓕᑯᓘᔭᖃᕐᓗᒍ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᑐᓴᒐᒃᓴᖏᑦ ᓄᓇᐅᑉ ᐃᓗᐊᓂ ᐃᒪᐅᑉ ᐱᐅᓂᖓᑕ ᐊᒻᒪ ᑕᕆᐅᖃᕐᓂᖓᑕ ᐊᔾᔨᒌᖏᓐᓂᖓ ᑕᕆᐅᕐᒧᑦ ᑯᕕᓯᑎᓪᓗᒋᑦ ᐊᒃᐸᓯᖕᓂᖅᓴᐅᑎᓪᓗᒍ CCME ᒪᓕᒐᖏᓐᓂᑦ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: Water Quality Predictions: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge
Potential Interaction with Marine Environment (KIA-7)
  Issue: Saline groundwater & water from TIA have the potential to interact with marine environment. This concerns the variability of TIA discharge, salinity levels, & chemical differences between saline groundwater & seawater.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Variance in water discharge, chemical differences & the potential impact on seawater should be addressed in further detail.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC provided information on groundwater quality and the saline variation of ocean discharge was below CCME guidelines. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 8: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᒥᒃ ᓇᐅᑦᑎᖅᓱᐊᖃᕐᓂᖅ
ᐃᒪᕐᒥᒃ ᐃᒪᕐᒥᐅᑕᓂᒡᓗ ᓇᐅᑦᑎᖅᓱᐊᖃᕐᓂᕐᒧᑦ ᐱᓕᕆᔾᔪᑎᒃᓴᓄᑦ ᐋᖅᑭᒡᓱᖅᓯᒪᓂᖅ (AEMP-ᒧᑦ ᐊᒻᒪᓗ EEM-ᒧᑦ ᐱᓕᕆᐊᖅ):
ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᖅ ᐊᒻᒪ AEMP (KIA-6)
  ᐱᔾᔪᑎ: ᑲᖏᕐᖢᐊᓂ ᑕᕆᐅᕐᒥᐅᑕᓂᒃ ᑎᖕᒥᐊᖃᕐᒪᑦ ᐊᒻᒪ ᐃᒪᕐᒥᐅᑕᓂᒃ ᐆᒪᔪᖃᕐᒪᑦ ᓂᕿᖃᖅᑐᓂᒃ ᐃᖅᑲᕐᒥᐅᑕᐅᔪᓂᒃ ᑯᑭᐅᔭᖃᖅᑐᓂᒃ. ᑐᓴᒐᒃᓴᑦ ᐅᓪᓗᒥᓯᐅᑎᑦ ᐱᔭᐅᓗᑎᒃ AEMP-ᒧᑦ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᓴᐳᒻᒥᔭᐅᖁᓪᓗᒋᑦ ᐆᒪᔪᑦ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: AEMP ᐊᓯᔾᔨᖅᑕᐅᔪᑦ ᐱᖃᓯᐅᔾᔨᓯᒪᔭᕆᐊᖃᖅᑐᑦ ᖃᐅᔨᓴᒐᒃᓴᓂᒃ ᐱᖃᑦᑕᕐᓂᖏᑦ ᐅᓄᖅᓯᒋᐊᖅᑎᑦᓯᓂᕐᒥᒃ ᐊᑯᓚᐃᓐᓂᖅᓴᐅᓕᖅᑎᓪᓗᒋᑦ ᑯᕕᐅᔪᑦ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᐃᒃᐱᖕᓂᕐᓂᖓᓄᑦ ᕿᒥᕐᕈᓇᒍᑎ ᐃᒪᕐᒥᒃ ᐅᓯᔪᓐᓇᕐᓂᖓᓄᑦ ᓇᓗᓇᐃᖅᓯᓚᐅᖅᑐᖅ ᐃᒪᐅᑉ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓᓂᒃ ᑯᕕᖅᑕᕐᓂᕐᓗᑯᒋᔭᑦ ᓱᕈᕐᓇᖅᑐᖓ ᐊᒃᐸᓯᖕᓂᖅᓴᐅᓂᖓᓂᒃ CCME ᐊᒻᒪᓗ MMER ᒪᓕᒐᖏᓐᓂᑦ. ᑐᒃᓯᕋᐅᑕᐅᔪᖅ ᖃᐅᔨᓴᐃᕕᐅᖃᑦᑕᕈᒪᓪᓗᑎᒃ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖠᐊᓂ ᐊᒻᒪᓗ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓ ᖃᐅᔨᓴᖅᑕᐅᒐᒥ ᖃᐅᔨᔭᐅᓚᐅᖅᑐᑦ ᓈᒻᒪᖕᓂᖓᓂᒃ ᑖᒃᑯᓄᖓ AEMP-ᒧᑦ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge Monitoring: Aquatic Monitoring Framework (AEMP and EEM Program)
ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge and AEMP (KIA-6)
  Issue: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ hosts 9 waterfowl & at least 2 mammal species. That feed on benthic food items like bivalves. Update AEMP in ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ to protect wildlife.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: AEMP changes should include increased sampling locations and frequency for diffuser outfall.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: The sensitivity analysis of water load balance indicates TIA effluent concentrations are below CCME and MMER guidelines. Hydrodynamic modeling of discharge indicates dilutions of >180:1 within 1 m of diffuser and dilutions of 1000:1 to 10,000:1 at a distance of 250 m from the diffuser. Proposed sampling locations in Robert Bay and the TIA were reviewed and found adequate for AEMP. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 9: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᑦ ᓇᐅᑦᑎᖅᓱᐊᕆᔭᐅᓂᖓ
ᐃᒪᕐᓗᑯ ᑯᕕᔭᐅᓂᖓᑕ ᒪᓕᒐᖓ:
ᑲᑎᖅᓱᐃᕕᖕᒥᒃ ᓇᓗᓇᐃᖅᓯᔾᔪᑦ (KIA-8)
  ᐱᔾᔪᑎ: ᐱᐅᓯᐅᔪᑦ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ ᓇᓚᐅᑦᑖᕈᑕᐅᓗᑎᒃ ᐃᒪᐅᑉ ᐱᐅᓂᕆᔭᖓᓂᒃ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᓇᓗᓇᐃᖅᓯᖏᒻᒪᑕ ᐊᖏᓂᕆᔭᖓᓂᒃ ᐊᒻᒪ ᖃᓄᑎᒋ ᐃᓗᓕᖃᕐᒪᖔᑕ ᑕᐃᑲᓂ ᑲᑎᖅᓱᐃᕕᖕᒥ ᐃᒪᖓᑕ ᐱᐅᓂᖓ ᖁᕝᕙᓯᖕᓂᖅᓴᐅᒐᔭᕐᒪᑦ CCME ᒪᓕᒐᖏᓐᓂᑦ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᖏᓂᖓ ᐊᒻᒪ ᐋᖅᑭᒡᓱᖅᓯᒪᓂᖓ ᑲᑎᖅᓱᐃᕕᐅᑉ, ᐃᓗᐊᓂ ᐃᒪᖓᑕᐱᐅᓂᖓ ᖁᕝᕙᓯᖕᓂᖅᓴᐅᒐᔭᕐᒪᑦ CCME ᒪᓕᒐᖏᓐᓂᑦ ᐊᒻᒪ ᐆᒃᑐᕋᐅᑕᐅᓗᓂ ᑕᑯᒃᓴᐅᑎᑕᐅᓗᓂᓗ ᐊᑐᕐᓗᑎᒃ 75th ᐳᓴᓐᑎᒥᒃ ᐃᓗᓕᖃᕐᓂᖓᓂᒃ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: 3-D ᐱᖓᓲᓕᖅᑲᖓᓪᓗᓂ ᑕᑯᒃᓴᐅᔪᓐᓇᖅᑐᑉ ᐆᒃᑐᕋᐅᑎᓕᐊᖑᔪᖅ ᑲᑎᖅᓱᐃᕕᖕᒥ, ᐳᕐᔫᓪᓗ ᐃᖏᕐᕋᓂᕆᔭᖓ, ᐃᒪᐅᓪᓗ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓ ᐊᑐᕐᓗᑎᒃ 75 ᐳᓴᓐᑎᒥᒃ ᐃᓗᓕᖃᕐᒪᑦ ᓇᓗᓇᐃᖅᓯᕗᖅ CCME ᒪᓕᒐᖏᓐᓂᒃ ᐱᐅᔭᕆᐊᖃᕐᓂᖏᓐᓄᑦ ᐊᖑᒻᒪᑎᔪᑦ 1 m ᑯᕕᔭᐅᔪᐊᓂᑦ ᐅᖓᓯᖕᓂᖃᖅᑎᓪᓗᒍ. ᐱᔾᔪᑕᐅᔪᖅ ᑕᒪᑐᒧᖓ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge Monitoring : Effluent Discharge Criteria
Mixing Zone Delineation (KIA-8)
  Issue: The methods used to predict water quality in ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ does not determine the size & properties of the mixing zone where water quality will be above the CCME guidelines.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: The size & shape of the mixing zone, where water quality will be above CCME guidelines should be modeled & presented, using 75th percentile concentrations.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC used a three-dimensional hydrodynamic modeling to simulate mixing zones, plume movement, & predict water quality concentrations (CCME) using 75th percentile concentrations. All marine CCME water quality requirements were met within 1 m of the diffuser with water quality similar to baseline conditions. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.

## Slide 10: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᑦ ᓇᐅᑦᑎᖅᓱᐊᕆᔭᐅᓂᖓ
ᑕᕆᐅᑉ ᐃᒪᖓᑕ ᐱᐅᔭᕆᐊᖃᕐᓂᖓᓄᑦ ᑐᕌᒐᒃᓴᑦ:
ᓇᓚᐅᑦᑖᖅᑕᐅᔪᑦ ᐊᕙᑎᒧᑦ ᐊᒃᑐᐃᓂᕆᒐᔭᖅᑕᖓ ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ (KIA-12)
  ᐱᔾᔪᑎ: ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑎᓕᐊᖑᔪᖅ ᐱᑕᖃᕆᐊᖃᖅᑐᖅ ᖃᐅᔨᔾᔪᑕᐅᓂᐊᕐᒪᑦ ᖃᓄᑎᒋ ᓱᕈᕐᓇᖅᑐᓂᒃ ᐃᓗᓕᖃᕐᒪᖔᑦ nitrate-ᓂᒃ ᑕᐃᑲᓂ ᑲᑎᖅᓱᐃᕕᖕᒥ, ᐊᒻᒪ ᐊᑯᓐᓂᐊᓃᑦᑐᖅ ᐃᒪᖅ ᐃᑎᔪᑉ ᐊᒻᒪ ᐃᒪᐅᑉ ᖄᖓᑕ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᓄᑖᕈᕆᐊᖅᑕᐅᓗᓂ ᓇᔪᒐᖓ ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑕᐅᔪᖅ ᐱᖃᓯᐅᔾᔨᓯᒪᓕᕐᓂᐊᕐᒪᑦ ᑲᑎᖅᓱᐃᕕᖕᒥᒃ ᐆᒃᑐᕋᐅᑎᖃᕐᓗᑎᒃ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᓇᓚᐅᑦᑖᓕᕈᓐᓇᕐᓂᐊᕐᒪᑕ ᖃᓄᑎᒋ ᓱᕈᕐᓇᖅᑐᖃᕐᒪᖔᑦ nitrate-ᒥᒃ ᐊᒻᒪᓗ ᖃᓂᒋᔭᖓᓂ ᑲᑎᖅᓱᐃᕕᐅᑉ, ᐃᑎᔪᒥ, ᐊᒻᒪ ᐃᒪᐅᑉ ᖄᖓᓂ ᐃᑲᓐᓂᖅᓴᒥ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᐆᒃᑐᕋᐅᑎᓕᐊᖑᔪᖅ ᓴᖅᑎᑦᑎᓚᐅᖅᑐᖅ ᐊᖏᓂᖓᓂᒃ ᐳᔪᕐᓘᑉ, ᐋᖅᑭᒡᓯᒪᓂᖓᓂᒃ, ᐊᒻᒪ ᖃᓄᑎᒋ ᓱᕈᕐᓇᖅᑐᖃᕐᒪᖔᑦ nitrate-ᒥᒃ ᐊᒻᒪ ᖃᓂᒋᔭᖓᓃᑦᑐᑦ ᖃᐅᔨᓴᖅᑕᐅᒐᒥᒃ ᐊᒃᐸᓯᖕᓂᖅᓴᐅᓚᐅᖅᑐᑦ CCME ᒪᓕᒐᖏᓐᓂᑦ ᐳᔪᕐᓗᐊᓗ ᐃᑎᓂᖅᓴᒦᓪᖢᓂ, ᐃᒪᐅᑉ ᖄᖓᑕ ᐊᑖᓂ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge Monitoring: Marine Water Quality Objective
Prediction of Environmental Effects on Water Quality (KIA-12)
  Issue: A water quality model is needed to determine the concentrations of nitrate in the mixing zone & between deep & surface layers. Enriched nitrate in the surface layer may cause excessive algal growth.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Update site water quality model to include the mixing zone modeling in Robert’s bay that predicts the concentrations of nitrate & other parameters in the mixing zone, deep layer & surface layers.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC has provided modeling results on plume size, shape, & concentration in ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ & Melville Sound. Nitrate and other parameters were found to be well below CCME guidelines with the plume trapped well below the surface water layer. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 11: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓄᑦ ᑯᕕᔭᐅᔪᑦ ᓇᐅᑦᑎᖅᓱᐊᕆᔭᐅᓂᖓ
ᑕᕆᐅᑉ ᐃᒪᖓᑕ ᐱᐅᓂᕆᔭᕆᐊᖃᖅᑕᖓᓄᑦ ᑐᕌᒐᒃᓴᑦ:
ᐅᓄᖅᓯᕙᓪᓕᐊᓂᖓ ᓱᕈᕐᓇᖅᑐᑦ ᐃᓱᒫᓗᒍᑕᐅᑐᐃᓐᓇᕆᐊᖃᖅᐳᖅ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ (KIA-9)
  ᐱᔾᔪᑎ: ᖃᓄᕐᓕ ᓯᕗᓂᒃᓴᒥ ᐱᓕᕆᐊᖑᖃᑦᑕᕐᓂᐊᖅᑐᑦ ᐊᒃᑐᐃᓂᖃᕐᓂᐊᖅᐸ ᐃᒪᐅᑉ ᐱᐅᓂᕆᔭᖓᓂᒃ ᑕᐃᕙᓂ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ?
  ᐊᑐᓕᖁᔭᓕᐊᖅ: TMAC-ᑯᑦ ᑐᓂᓯᔭᕆᐊᖃᖅᑐᑦ ᑎᑎᕋᖅᓯᒪᔪᓂᒃ ᐅᖃᐅᑕᐅᔭᕆᐊᖃᕐᓂᐊᖅᑐᓂᒃ ᖃᓄᖅ CCME ᐃᒪᐅᑉ ᐱᐅᓂᕆᔭᕆᐊᖃᖅᑕᖓᓄᑦ ᒪᓕᒐᖏᑦ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᐊᖑᒻᒪᑎᔭᐅᓂᐊᕐᒪᖔᑕ ᑭᖑᕐᖓᒍᑦ ᑐᒡᓕᐊᓂ ᐱᓕᕆᔭᐅᔭᕆᐊᓕᒃ ᐱᒋᐊᓚᐅᖅᑎᓪᓗᒍ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᖄᒃᑲᓐᓂᐊᒍᑦ ᖃᐅᔨᓴᐃᓂᕐᒧᑦ ᓱᕈᕐᓇᖅᑐᖃᕐᒪᖔᑦ ᐊᒻᒪ ᕋᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᑲᒪᒋᔭᐅᓂᐊᖅᑐᑦ ᐱᓕᕆᐊᖃᓕᖅᐸᑕ ᑐᒡᓕᐊᓂ 2 DEIS-ᒥᒃ.
  ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐅᖃᐅᑕᐅᓚᐅᖅᑐᖅ ᐊᒻᒪᓗ ᐋᖅᑭᒡᑕᐅᓪᓗᓂ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᒻᒪᓗ TMAC-ᑯᑦ ᑲᑎᒪᓂᖃᕐᓂᐊᕐᓗᑎᒃ ᐊᐅᓚᑦᓯᔾᔪᑎᓄᑦ ᑲᒪᓗᑎᒃ ᔮᓐᓄᐊᕆᐅᓕᖅᐸᑦ.
Notes: ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge Monitoring: Marine Water Quality Objectives
Increasing Contaminants of Potential Concern in ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ (KIA-9)
  Issue: How will future projects affect water quality in Robert’s Bay?
  ᐊᑐᓕᖁᔭᓕᐊᖅ: TMAC should provide a discussion on how CCME water quality criteria in Robert’s Bay will be met after Phase 2 starts.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue was discussed and resolved by KIA and TMAC at the January Technical Meeting.

## Slide 12: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᖕᒧᑦ ᑯᕕᖅᑕᕐᕕᒃ
ᐊᑐᖅᑕᐅᓂᖓ ᐅᔭᕋᐃᑦ ᐃᒋᑕᐅᓂᐅᓴᔪᑦ ᐃᒡᓗᓕᐅᖅᑎᓄᑦ:
ᐃᒋᑕᐅᓂᐅᓴᔪᑦ ᐅᔭᕋᐃᑦ ᒥᐊᓂᕆᔭᐅᓂᖏᓐᓄᑦ ᐸᕐᓇᐅᑎᑦ:
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ
Notes: Waste Rock Tailings: Use of Waste Rock in construction & Waste Rock Management Plan
No Issues

## Slide 13: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᒃ ᑯᕕᒡᕕᖏᑦ
ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ:
ᑯᕕᖅᑕᐃᕕᒃ ᐃᒪᕐᓗᑯᓄᑦ ᐊᖏᓕᒋᐊᖅᑕᐅᓂᒃᓴᖓᓄᑦ ᐱᕕᖃᕐᕕᒋᔭᖓ (KIA-1)
  ᐱᔾᔪᑎ: ᑖᓐᓇ ᑯᕕᖅᑕᕐᕕᒃ ᐃᒪᕐᓗᑯᓄᑦ ᐊᖏᓂᖓ ᓈᒻᒪᒃᑲᓗᐊᖅᐸ ᒪᑐᕆᑦᒥ ᐊᒻᒪ ᐹᔅᑕᓐᒥ ᐱᓕᕆᕕᐅᔪᓂ?
  ᐊᑐᓕᖁᔭᓕᐊᖅ: TMAC-ᑯᑦ ᑐᓂᓯᔭᕆᐊᖃᖅᑐᑦ ᕿᒥᕐᕈᒍᑎᒋᔭᖓᓐᓂᒃ ᑯᕕᖅᑕᕐᕕᐅᑉ ᐊᖏᓂᕆᔭᖓᓂᒃ ᐊᑐᖅᑕᐅᓂᐊᖅᑎᓪᓗᒍ ᓯᕗᓂᒃᓴᒥ ᐱᓕᕆᐊᖑᔪᓄᑦ ᐊᒻᒪ ᐱᖃᓯᐅᔾᔭᐅᓯᒪᓗᑎᒃ ᑖᒃᑯᐊ ᐱᓕᕆᐊᓴᑦ ᐃᓗᐊᓂ CEA.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᖄᒃᑲᓐᓂᐊᒍᑦ ᖃᐅᔨᓴᐃᒃᑲᓐᓂᕆᐊᖃᖅᑐᑦ ᑯᕕᖅᑕᕐᕕᖕᒥᒃ & ᕌᐳᑦᔅ ᐸᐃ ᑲᖏᕐᓗᐊᓂ ᑕᒪᓐᓇ ᑭᐅᔭᐊᓂᐊᖅᑐᖅ ᐱᓕᕆᐊᖃᓕᖅᐸᑕ ᑐᒡᓕᖓᓂ 2 DEIS-ᒥᒃ.
  ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: Waste Rock and Tailings: Tailings Management
TIA Expansion Capacity (KIA-1)
  Issue: Does the TIA have sufficient capacity for Madrid/Boston projects?
  ᐊᑐᓕᖁᔭᓕᐊᖅ: TMAC should provide an assessment of TIA capacity for future projects & should include these project in the CEA.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: Additional studies for TIA & Robert’s Bay will be addressed in the Phase 2 DEIS.
  This issue was discussed and resolved by KIA and TMAC at the January Technical Meeting.

## Slide 14: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᒃ ᑯᕕᕝᕕᖏᑦ
ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ:
ᑯᕕᕝᕕᖕᒥ ᐅᒪᔪᓂᒃ ᖃᐃᑎᑦᑎᓂᖅ ᐊᒻᒪᓗ ᐆᒪᔪᓂᒃ ᐊᕙᓃᑎᑦᑎᒐᓱᐊᕐᓂᖅ (KIA-2)
  ᐱᔾᔪᑎ: ᐅᐸᒃᑕᐅᔭᒻᒪᑕ ᐆᒪᔪᓄᑦ, ᓂᕆᕕᐅᔭᖅᑐᕐᖢᑎᒃ ᑯᕕᕝᕕᐅᔪᑦ ᐱᕈᖅᑐᖃᕐᓂᖏᓐᓄᑦ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᖏᖅᑕᐅᓯᒪᔪᖅ ᒥᐊᓂᖅᓯᔾᔪᑎᓄᑦ ᐱᓕᕆᔾᔪᑎ ᓇᓗᓇᐃᖅᓯᓯᒪᓗᓂ ᐊᑯᓚᐃᓐᓂᕆᔭᖓᓂᒃ, ᑭᒡᓕᖓᓂᒃ, ᐊᒻᒪ ᐱᐅᓯᐅᓂᐊᖅᑐᓂᒃ ᓇᐅᑦᑎᖅᓱᐊᖃᖅᑎᓪᓗᒋᑦ ᐊᒻᒪ ᓱᕈᐃᑦᑕᐃᓕᒪᑎᑦᑎᑎᓪᓗᒋᑦ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC-ᑯᑦ ᐊᖏᖅᓯᒪᓕᖅᑐᑦ ᓴᓇᔪᒪᓪᓗᑎᒃ ᓇᐅᑦᑎᖅᓱᐃᔾᔪᑎᒃᓴᓄᑦ ᐸᕐᓇᐅᑎᓂᒃ ᖃᐅᔨᓴᐅᑎᐅᓂᐊᖅᑐᒥᒃ ᓂᕐᔪᑎᓂᒃ ᐅᐸᒃᑕᖅᑐᓂᒃ ᐊᒻᒪ ᓂᕆᖃᑦᑕᖅᑐᓂᒃ ᖃᓂᕆᔭᖓᓂ ᑯᕕᖅᑕᕐᕕᐅᑉ. ᑖᒃᑯᐊ ᐱᖃᓯᐅᔾᔨᓯᒪᓂᐊᖅᑐᑦ ᐊᑦᑕᕐᓇᕐᓂᖓᓂᒃ ᕿᒥᕐᕈᓴᖕᓂᕐᒥᒃ ᐊᒻᒪᓗ ᐊᑐᓕᖅᑎᑦᑎᓂᕐᒥᒃ ᐆᒪᔪᓂᒃ ᐊᕙᓃᑎᑦᑎᔾᔪᑕᐅᓂᐊᖅᑐᓂᒃ ᐱᔭᕆᐊᖃᖅᐸᑕ.
  ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Waste Rock and Tailings: Tailings Management
TIA Wildlife Attraction and Deterrence (KIA-2)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: An adaptive management program with several details on frequency, thresholds, and methods of monitoring and mitigation.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC has agreed to develop a monitoring plan to detect wildlife attraction & feeding in or near the TIA, in combination with other monitoring. Based on results, will conduct a risk assessment & implement wildlife deterrents as necessary.
  This issue was discussed thoroughly and was resolved by KIA and TMAC.

## Slide 15: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᒃ ᑯᕕᕝᕕᖏᑦ
ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ:
TIA NPAG ᑯᕕᖅᑕᕐᕕᐅᑉ ᒪᑐᖓ ᐃᑎᓂᖓᓗ (KIA-5)
  ᐱᔾᔪᑎ: ᑐᒃᓯᕋᐅᑎᖃᖅᑐᑦ 0.3 m ᐃᑎᓂᖃᕐᓗᓂ ᐅᔭᕋᒃ ᒪᑐᒋᓂᐊᖅᑕᖓ ᑯᕕᖅᑕᕐᕕᐅᑉ ᓯᒡᔭᖓᑕ ᒪᑐᓐᓂᖅᐸᑦ ᐅᔭᕋᖕᓂᐊᕐᕕᒃ ᑕᒪᓐᓇ ᓈᒻᒪᖏᑦᑐᖅ
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᑐᕐᓗᑎᒃ 75th ᐳᓴᓐᑎᒥᒃ ᐃᕐᖓᕐᓂᕆᒐᔭᖅᑕᖓᓄᑦ ᓈᓴᐅᑎᖃᖅᑎᑦᑎᓗᑎᒃ ᐆᒃᑐᕋᐅᑎᒧᑦ ᐊᑐᖅᑕᐅᖃᑦᑕᕐᓗᓂ ᓇᓚᐅᑦᑖᓕᕌᖓᑕ ᖃᓄᑎᒋ ᓱᕈᕐᓇᖅᑐᖅ ᐃᕐᖓᖅᑎᒋᖕᒪᖔᑦ ᑕᐃᑲᓐᖓᑦ ᑯᕕᖅᑕᕐᕕᐅᔪᒥᑦ TIA-ᒥᑦ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᑯᕕᖅᑕᕐᕕᐅᑉ ᓯᒡᔭᖓ ᖃᐅᔨᓴᖅᑕᐅᒃᑲᓐᓂᓚᐅᕐᒪᑦ ᐊᑐᖅᑕᐅᓪᓗᓂ 75th ᐳᓴᓐᑎᒥᒃ ᐃᕐᖓᕋᔭᕐᓂᖓ ᐊᑯᓚᐃᓐᓂᖃᖅᑎᑕᐅᓪᓗᓂ. ᖃᐅᔨᔭᐅᔪᑦ ᐃᒪᓐᓇᐃᓕᖓᓚᐅᖅᑐᑦ 0.3 m ᖁᕕᖅᑕᕐᕕᐅᑉ ᒪᑐᖓ ᓈᒻᒪᖏᒻᒪᑦ ᐊᒻᒪ ᐳᓪᓚᒃᐸᓪᓕᐊᓂᖓ ᐊᒃᐸᓯᓗᐊᖅᑐᖅ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: Waste Rock and Tailings: Tailings Management
TIA NPAG Tailings Cover Depth (KIA-5)
  Issue: The proposed 0.3 m depth of quarry rock cap for the tailings beach upon closure is not sufficient.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Use 75th percentile leach as input values into model when predicting containment release from the TIA.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC had recalculated the tailings beach source terms using the 75th percentile leach rates from the humidity cell tests. Results of new model indicate that the 0.3 m tailing cover is adequate and the development of boils is low. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 16: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᒃ ᑯᕕᕝᕕᖏᑦ
ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ:
TIA ᑯᕕᖅᑕᕐᕕᖕᒥ ᐳᒃᑕᔪᑦ ᐳᔪᕐᓗᐃᑦ ᑲᑕᒐᕐᓂᖏᑦ ᐊᒻᒪ ᐃᕐᖓᕐᓂᖓᑕ ᑰᖕᓂᖏᑦ (KIA-3)
  ᐱᔾᔪᑎ: ᐅᐸᒃᑕᐅᔭᓐᓂᖓ ᐆᒪᔪᓄᑦ, ᐊᒻᒪ ᓂᕆᕕᐅᔭᓐᓂᖓ ᐱᕈᖅᑐᖏᑦ ᖁᕕᖅᑕᕐᕕᐅᑉ, ᐊᒃᑐᐃᔭᓐᓂᖓᓗ ᐆᒪᔪᓂᒃ ᑯᕕᖅᑕᕐᕕᖕᒥᑦ ᐃᖏᕐᖓᖅᑐᖅ ᑰᒐᖅᑐᖅ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᖏᖅᓯᓗᑎᒃ ᒥᐊᓂᖅᓯᔾᔪᑎᓄᑦ ᐱᓕᕆᔾᔪᑎᐅᓂᐊᖅᑐᓂᒃ ᓇᓗᓇᐃᖅᓯᓯᒪᓗᑎᒃ ᐊᑯᓚᐃᓐᓂᖏᓐᓂᒃ, ᑭᒡᓕᖓᓂᒃ, ᐊᒻᒪ ᐱᐅᓯᐅᓂᐊᖅᑐᓂᒃ ᓇᐅᑦᑎᖅᓱᐊᖃᖅᑎᓪᓗᒋᑦ ᓱᕈᐃᑦᑕᐃᓕᒪᑎᑦᑎᔾᔪᑎᓂᒃ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᐃᒃᐱᖕᓂᕐᓂᕐᒧᑦ ᖃᐅᔨᓴᐃᔾᔪᑎᖏᑦ ᑯᕕᖅᑕᕐᕕᖕᒥ ᐃᒪᐅᑉ ᖃᓄᐃᓐᓂᕆᔭᖓᓂᒃ ᓇᓗᓇᐃᖅᓯᓯᒪᕗᑦ ᐊᒃᐸᓯᒃᑐᒻᒪᕆᐅᓂᖓᓂᒃ ᓱᕈᕐᓇᖅᑐᖅ ᐊᑖᓃᓪᖢᓂ CCME ᒪᓕᒐᖏᑕ.
  ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Waste Rock and Tailings: Tailings Monitoring
TIA Floatation Tailings Dust Fall and Leaching (KIA-3)
  Issue: Attraction to, and consumption of tails or vegetation impacted by tailing leachates by wildlife.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: An adaptive management program with several details on frequency, thresholds, and methods of monitoring and mitigation.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: The review of TIA water quality from the sensitivity analysis indicated that tailings were very low in concentration of toxic substances and were well below CCME guidelines.
  This issue was discussed thoroughly and was resolved by KIA and TMAC.

## Slide 17: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ ᐊᒻᒪ ᐃᕈᖅᑐᐃᔾᔪᑎᕕᓂᖅ ᐃᒪᕐᓗᒃ ᑯᕕᕝᕕᖏᑦ
ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ:
ᑯᕕᖅᑕᕐᕕᒃ ᐊᒻᒪ ᖃᓂᒋᔭᖓ ᖁᕝᕙᕆᐊᖅᓯᒪᔪᑦ ᖃᓄᐃᓐᓂᐅᔪᑦ ᐃᓱᒫᓗᒍᑕᐅᔪᓐᓇᖅᑐᑦ ᐅᔭᕋᖕᓂᐊᕐᕕᒃ ᒪᑐᑎᓪᓗᒍ (KIA-4)
  ᐱᔾᔪᑎ: ᐃᒪᖅ ᐊᒻᒪ ᐃᒪᖃᕈᓐᓇᕐᓂᖓᓄᑦ ᐆᒃᑐᕋᐅᑎᐅᔪᖅ ᐊᑐᕐᒪᑕ ᐊᑯᓐᓂᖅᓱᖅᑐᓂᒃ ᐅᓄᕐᓂᐅᔪᓂᒃ ᓇᓚᐅᑦᑖᕈᑕᐅᓪᓗᑎᒃ ᐃᒪᐅᑉ ᐱᐅᓂᖓᓄᑦ ᐊᒻᒪ ᖃᓄᑎᒋ ᓱᕈᕐᓇᖅᑐᖃᕐᓂᖓᓂᒃ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐊᑐᕐᓗᑎᒃ 75th ᐳᓴᓐᑎᒥᒃ ᓱᕈᕐᓇᖅᑐᖃᕐᓗᓂ ᐆᒃᑐᕋᐅᑎᓕᐅᕐᓗᑎᒃ ᑖᒃᑯᐊ ᐊᑐᖅᑕᐅᖔᓕᕐᓗᑎᒃ “ᐱᐅᓯᒋᐊᖁᓪᓗᒍ” ᖃᓄᐃᓐᓂᐅᔪᖅ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᐃᒃᐱᖕᓂᕐᓂᖓᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᔪᖅ ᐃᒪᐅᑉ ᐊᒻᒪ ᐃᒪᖃᕈᓐᓇᕐᓂᖓᓄᑦ ᐊᑐᕐᖢᑎᒃ 75th ᐳᓴᓐᑎ ᓱᕈᕐᓇᖅᑐᖃᖅᑎᓪᓗᒍ ᐆᒃᑐᕋᐅᑎᓕᐊᖑᓗᓂ ᐊᑐᖅᑕᐅᔪᖅ ᓴᖅᑭᑦᑎᓚᐅᖅᑐᖅ ᖃᐅᔨᓴᖅᑕᐅᑎᓪᓗᒍ ᐊᒃᐸᓯᖕᓂᖅᓴᐅᓂᖓᓂᒃ CCME ᐊᒻᒪ MMER ᒪᓕᒐᖏᓐᓂᒃ, ᐊᒻᒪ ᐊᑦᑕᕐᓇᖏᓐᓂᖏᓐᓂᒃ ᑐᒃᑐᓄᑦ ᐊᒻᒪᓗ ᑎᖕᒥᐊᓄᑦ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.
Notes: Waste Rock and Tailings: Tailings Monitoring
TIA Elevated Parameters of Potential Concern Upon Closure(KIA-4)
  Issue: Water & load balance model uses median values to predict water quality & loadings which may underestimate potential effects to surface water.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Use 75th percentile concentrations as input values into model to consider “enriched” conditions.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC had run a sensitivity analysis of the water & load balance using the 75th percentile for background concentrations & other input source terms. Results were found to below CCME and MMER guidelines and the water was non-toxic to Caribou and Birds. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓚᐅᖅᑐᖅ.

## Slide 18: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᖁᕕᖅᑕᕐᕕᒃ ᒥᐊᓂᕆᔭᐅᓂᖓ
ᓄᓇᐅᑉ ᐊᑖᓄᑦ ᐃᒋᑦᑎᕕᒃ ᐊᒃᑐᐃᓂᖓ ᐃᒋᑕᒃᓴᑦ ᐅᔭᕋᑦ:
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ.
Notes: Waste Rock and Tailings: Underground Disposal of Impacted Waste Rock
No Issues

## Slide 19: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᓱᕈᔾᔭᐃᖅᓯᓯᒪᓂᕐᒧᑦ ᒪᓕᒐᐃᑦ
ᑐᐊᕆᔅ ᑕᓯᐊᓂ ᐊᒻᒪ ᑕᑕᓗᐊᖅᑎᓪᓗᒍ ᑯᕕᕝᕕᐅᑉ ᐊᖏᓂᖓ:
ᑐᐊᕆᔅ ᑕᓯᐊᓂ ᐃᒪᖓᑕ ᐊᖏᓂᖓ (KIA-13)
  ᐱᔾᔪᑎ: ᓄᓇᐅᑉ ᐊᑖᒍᑦ ᑰᖃᖅᑐᖅ ᐊᒃᑐᐃᓂᐊᖅᑐᖅ ᑐᐊᕆᔅ ᑕᓯᐊᑕ ᐃᒪᖓᑕ ᐃᑎᓂᖓᓂᒃ, ᐃᖃᓗᖏᓐᓂᒃ, ᐃᕐᓂᐅᕐᓂᖏᓐᓂᒃ, ᐊᒻᒪ ᒪᓐᓂᑦ ᐱᕈᕋᓱᖕᓂᖏᓐᓂᒃ.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: ᐱᖃᓯᐅᔾᔨᓯᒪᓗᑎᒃ ᑭᒡᓕᒋᓂᐊᖅᑕᖓᓂᒃ ᑐᓴᒐᒃᓴᓂᒃ ᐅᓪᓗᒥᓯᐅᑎᓂᒃ ᓄᑖᕈᕆᐊᖅᑕᐅᓗᑎᒃ ᐊᒃᑐᐃᓂᖃᕋᔭᕐᓂᖓᓄᑦ ᖃᐅᔨᓴᕈᑕᐅᔪᑦ, ᒪᓕᒐᖃᖅᑎᑕᐅᓗᑎᒃ ᓱᕈᔾᔭᐃᖅᓯᓯᒪᔾᔪᑎᑦ ᐊᒻᒪᓗ ᓇᐅᑦᑎᖅᓱᐊᖃᕐᓂᕐᒧᑦ ᐸᕐᓇᐅᑎᖏᑦ.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: ᖄᒃᑲᓐᓂᐊᒍᑦ ᑐᓴᒐᒃᓴᓂᒃ ᓄᐊᑦᑎᓂᐊᖅᑐᑦ ᓇᓗᓇᐃᖅᓯᔾᔪᑕᐅᓂᐊᖅᑐᓂᒃ ᐊᒃᑐᐃᓂᖏᓐᓂᒃ ᐃᖃᓗᖕᓂᒃ ᐊᒻᒪ ᐃᖃᓗᑦ ᓇᔪᒐᖓᓂᒃ ᑐᐊᕆᔅ ᑕᓯᐊᓂ ᐱᓕᕆᐊᖑᓚᐅᖅᑐᖅ ᑕᒪᓐᓇ ᐊᒻᒪᓗ ᕿᒥᕐᕈᓇᒃᑕᐅᓪᓗᓂ. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.
Notes: Mitigation Measures: Doris Lake and Outflow Water Levels
Doris Lake Water Levels (KIA-13)
  Issue: Groundwater inflow will affect Doris Lake water levels. Potential effects on fisheries, in particular spawning habitat & egg incubation, are currently unknown.
  ᐊᑐᓕᖁᔭᓕᐊᖅ: Additional work was completed in 2015 to characterise the fish habitat around Doris Lake. It is recommend that this baseline information be presented, & used to update the effects assessment & guide mitigation & monitoring plans, as needed.
  ᑭᐅᔾᔪᑎᑦ ᐊᒻᒪ ᖃᓄᐃᓕᖓᓕᕐᒪᖔᑦ: TMAC has completed additional data collection to quantify effects to fish & fish habitat in Doris Lake. This information was reviewed & assessed. ᑕᒪᑐᒧᖓ ᐱᔾᔪᑕᐅᔪᖅ ᐋᖅᑭᒡᑕᐅᓯᒪᓕᖅᑐᖅ.

## Slide 20: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᓱᕈᔾᔭᐃᖅᓯᓯᒪᓂᕐᒧᑦ ᒪᓕᒐᐃᑦ
ᓴᓇᔭᐅᓂᖓ ᐊᒻᒪ ᐊᐅᓚᑕᐅᓂᖓ ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊᓂ ᑯᕕᓯᕝᕕᐅᓪᓗᓂ ᓱᓪᓗᖅ:
ᐊᖅᑯᑎ ᐊᒻᒪᓗ ᐃᒪᕐᒥ ᐃᑳᕈᑎ:
ᓄᓇ ᐃᖅᑲᕐᒦᑦᑐᖅ ᐱᐅᓂᖓ:
ᓱᕈᐃᑦ ᐳᒃᑕᓂᖏᑦ: KIA-12
ᐳᔪᕐᓗᐃᔭᐅᑎ ᖁᕕᖅᑕᕐᕕᖕᒥ:
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ
Notes: Mitigation Measures: Construction and Operation of ᕌᐳᔅ ᐸᐃ ᑲᖏᕐᖢᐊ Discharge Pipeline, Road and Water Crossing, Sediment Quality, Effluent Buoyancy, and Dust Suppressant of Tailings
No Issues

## Slide 21: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᐃᒪᕐᒧᑦ ᓴᓗᒻᒪᖅᓴᐃᕕᒃ
ᐃᒪᕐᒧᑦ ᐊᒻᒪ ᑭᓈᓗᖕᓄᑦ ᓴᓗᒻᒪᖅᓴᐃᕕᒃ:
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ.
Notes: Water Treatment: Water and Sewage Treatment
No Issues

## Slide 22: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᒥᐊᓂᖅᓯᔾᔪᑎᓄᑦ ᐸᕐᓇᐅᑎᑦ ᐊᒻᒪᓗ ᐅᓂᒃᑳᓕᐊᑦ
ᐃᓗᓕᖏᑦ ᐸᕐᓇᐅᑎᑦ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐃᓚᐅᖃᑕᐅᓯᒪᓕᖅᐳᑦ ᐱᓕᕆᖃᑕᐅᓪᓗᑎᒃ ᐊᒻᒪ ᕿᒥᕐᕈᓯᒪᓕᖅᑐᑦ EEM-ᒧᑦ ᐱᓕᕆᐊᒥᒃ, AEMP, GWMP, TIA OMS ᑎᑎᕋᖅᓯᒪᔪᓂᒃ ᒪᓕᒋᐊᓕᖏᓐᓂᒃ, ᐊᒻᒪ ᐊᓯᔾᔨᖅᑕᐅᔪᒪᔪᓂᒃ SNP-ᒧᑦ ᐊᒻᒪ ᑕᒪᒃᑯᓂᖓ ᖃᐅᔨᓚᐅᖅᑐᑦ ᓈᒻᒪᒃᑐᐃᓐᓇᐅᓂᖏᓐᓂᒃ.
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ.
Notes: Management Plans and Reports: Content of Plans
The KIA has been involved with and reviewed the EEM Program, AEMP, GWMP, TIA OMS Manual, and the proposed changes to the SNP and found everything to be adequate.
No Issues

## Slide 23: ᐊᖏᔫᑎᑦ ᐱᔾᔪᑎᑦ ᐱᓕᕆᐊᒧᑦ ᐊᒻᒪ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᒧᑦ: ᒥᐊᓂᖅᓯᔾᔪᑎᓄᑦ ᐸᕐᓇᐅᑎᑦ ᐊᒻᒪᓗ ᐅᓂᒃᑳᓕᐊᑦ:
ᐅᓪᓗᒥᓯᐅᑎᕈᖅᑕᐅᓂᖏᑦ ᐸᕐᓇᐅᑎᑦ:
ᐊᖏᖅᑕᐅᓂᖏᑦ ᐸᕐᓇᐅᑎᑦ:
ᐱᔾᔪᑎᑕᖃᖏᑦᑐᖅ
Notes: Management Plans and Reports: Update to Plans and Approval of Plans
No Issues

## Slide 24: ᑭᖑᓪᓕᖅᐹᒥ ᐊᕙᑎᐅᑉ ᖃᐅᔨᓴᖅᑕᐅᓂᖓᓄᑦ ᒪᓕᒐᖏᑦ:
ᐊᕙᑎᒥᐅᑕᓂᒃ ᐊᒻᒪ ᐃᓅᓯᕐᒧᑦ ᑮᓇᐅᔭᓕᐅᕋᓱᐊᕐᓂᕐᒧᑦ ᐊᒃᑐᐃᓂᖅ:
ᐋᖅᑭᒡᓱᖅᓯᒪᓂᖓ ᐊᖏᖃᑎᒌᒍᑎᑉ ᐊᒻᒪ ᐃᓄᐃᑦ ᐊᒃᑐᖅᑕᐅᓂᖏᓐᓄᑦ ᐃᑲᔫᓯᐊᖏᓐᓄᑦ ᐊᖏᖃᑎᒌᒍᑎ,
ᑖᒃᓯᔭᖅᓯᒪᓕᖅᑎᓪᓗᒍ ᐅᔭᕋᖕᓂᒃ ᐊᐅᒃᑎᑕᐅᓯᒪᔪᓂᑦ ᓂᖏᖅᑕᕐᓂᕐᒧᑦ ᐊᖏᖃᑎᒌᒍᑎ,
ᐃᒪᕐᒧᑦ ᐊᒻᒪ ᐆᒪᔪᓄᑦ ᐊᑭᓕᖅᑕᐅᖔᕈᑎᓄᑦ ᐊᖏᖃᑎᒌᒍᑎ,
ᐅᔭᕋᒃᓴᓄᑦ ᐱᔪᓐᓇᐅᑎᖃᕐᓂᕐᒧᑦ ᐊᖏᖃᑎᒌᒍᑎ ᓄᓇᕗᑦ ᑐᓐᖓᕕᒃ ᑎᒥᖓᓐᓄᑦ, ᐊᒻᒪᓗ
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐃᓚᒋᔭᐅᔾᔪᑎᖃᕐᓂᖏᓐᓄᑦ TMAC Resources ᑎᒥᖓᓐᓄᑦ.
ᐃᓘᓐᓇᖏᑦ ᑖᒃᑯᐊ ᐊᒃᓱᑲᓪᓚᒃ ᓴᖅᑭᑦᑎᓯᒪᔪᑦ ᐃᑲᔪᕈᑎᓂᒃ ᐃᓄᖕᓄᑦ ᕿᑎᕐᒥᐅᓂ.
Notes: The KIA receives monetary compensation through a variety of agreements. Direct compensation through the Framework Agreement and IIBA for land access, quarry materials and water usage. Royalties from gold production plus shareholdings in TMAC.
NTI also gets a royalty on profit under its Mineral Rights Agreement with TMAC Resources Inc. All of this creates a substantial benefit for Inuit in the region.

## Slide 25: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐋᖅᑭᒡᓯᓯᒪᓕᖅᑐᑦ ᐃᓘᓐᓇᖏᓐᓂᒃ ᐊᐅᓚᑦᓯᔾᔪᑎᓄᑦ ᐱᔾᔪᑕᐅᔪᓂᒃ ᓴᖅᑭᑕᐅᓯᒪᔪᓂᒃ ᐊᐅᓚᑦᓯᔾᔪᑎᓕᕆᓂᕐᒧᑦ ᑲᑎᒪᔾᔪᑎᖃᖅᑎᓪᓗᒋᑦ ᐊᖅᑯᑕᐅᓪᓗᓂ ᑲᔪᓯᔪᒃᑯᑦ ᐱᓕᕆᖃᑎᖃᕐᓂᕆᔭᕗᑦ TMAC Resources ᑎᒥᖓᓐᓂᒃ.
ᑭᖑᓪᓕᖅᐹᒥ ᐋᖅᑭᒡᑕᐅᔾᔪᑎᖓ ᓴᓗᒻᒪᖅᓴᖅᑕᐅᔾᔪᑎᒃᓴᓄᑦ ᑮᓇᐅᔭᑦ ᑐᖅᑯᖅᑕᐅᔪᒃᓴᑦ ᓱᓕ ᐱᔭᕇᖅᑕᐅᓯᒪᖏᒻᒪᑦ ᒫᓐᓇᐅᔪᖅ.
Notes: KIA has resolved all technical issues brought forward to the Technical Meeting through our on-going collaboration with TMAC Resources Inc.
The final resolution of reclamation security is still pending at this time.

## Slide 26: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᒻᒪᓗ TMAC-ᑯᑦ ᐊᑎᓕᐅᖅᓯᒪᓕᖅᑐᑦ ᐃᒪᕐᒧᑦ ᐊᑭᓕᖅᑐᐃᔾᔪᑎᒃᓴᒧᑦ ᐊᖏᖃᑎᒌᒍᑎᒥᒃ ᐃᓚᒋᓪᓗᓂᐅᒃ ᐋᖅᑭᒡᓱᖅᓯᒪᓂᖓᑕ ᐊᖏᖃᑎᒌᒍᑎᐅᑉ ᑐᐊᕆᔅ ᐅᐊᖕᓇᖓᓂ ᐱᓕᕆᔭᐅᔪᑉ.
ᑖᓐᓇ ᐊᖏᖃᑎᒌᒍᑎᐅᔪᖅ ᑭᐅᓯᓯᒪᔪᖅ ᐃᓄᐃᑦ ᓄᓇᑖᕈᑎᑎᒍᑦ ᓈᓴᐅᑎᖓᓂᒃ 20-ᑯᑦ ᐱᔪᓐᓇᐅᑎᖏᓐᓂᒃ ᐊᒻᒪᓗ TMAC-ᑯᑦ ᐊᑭᓕᖅᑐᐃᔭᕆᐊᖃᕐᓂᖏᓐᓄᑦ ᐱᓕᕆᐊᒃᓴᕆᔭᖓᓐᓄᑦ.
ᑐᕋᐃᓐᓇᖅᑐᒃᑯᑦ ᐊᑭᓕᖅᑐᐃᓂᖅ ᑐᓂᔭᐅᕗᖅ ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᓐᓄᑦ ᓄᓇᒧᑦ ᐃᓯᕈᑎᐅᔪᓄᑦ, ᐅᔭᕋᐃᔭᕈᑎᐅᔪᓄᑦ ᐊᒻᒪᓗ ᐃᒪᐅᑉ ᐊᑐᖅᑕᐅᓂᖓᓄᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐱᖃᑦᑕᕐᒥᔪᑦ ᓂᖏᖅᑕᕈᑎᓂᒃ ᒎᓗᓕᐅᖅᑐᓂᒃ ᐱᖃᑦᑕᕐᒥᔪᑦ ᓄᓇᕗᑦ ᑐᓐᖓᕕᒃ ᑎᒥᖓᑦ.
Notes: In addition to the technical issues raised, the KIA has signed with TMAC a comprehensive Framework Agreement for land access compensation and an Inuit Impact and Benefit Agreement (IIBA).
The IIBA addresses Inuit interests in the areas of employment, contracting, and training in relation to the Hope Bay Project as a whole through its entire life span.
Under the IIBA an Inuit Environmental Advisory Committee (IEAC) has been established with TMAC which complements KIA’s current environmental activities in the Department of Lands and Environment. The IEAC allows for the local community to have input directly to TMAC on environmental concerns.
Through the Implementation Committee with KIA and TMAC representatives, measures of employment, business development, and training are being developed which fulfills socio-economic obligations under the NLCA.

## Slide 27: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐱᖃᖅᑐᑦ $3.49 ᒥᓕᐊᓐᓂᒃ ᐊᑭᖃᖅᑐᓂᒃ ᑎᑎᖅᑲᓂᒃ ᑮᓇᐅᔭᓐᖑᕈᓐᓇᖅᑐᓂᒃ ᐱᔭᐅᓯᒪᔪᑦ TMAC-ᑯᓐᓂᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐅᓪᓗᒥ ᐱᖃᕐᒥᔪᑦ $8.0 ᒥᓕᐊᓐᓂᒃ ᑯᐊᐳᕆᓴᒧᑦ ᐊᑭᓕᖅᑕᐅᔾᔪᑎᒃᓴᓂᒃ ᐊᑖᒍᑦ ᐅᐃᒍᖓᑕ K ᑮᓇᐅᔭᓕᐅᕋᓱᐊᖅᑐᓄᑦ ᐊᑐᖅᑐᐊᖅᑕᐅᓂᖓᓄᑦ ᑐᐊᕆᔅ ᐅᐊᖕᓇᖓ ᑲᑎᓪᓗᒍ ᐊᑐᖅᑐᐊᕈᑎ $11.49 ᒥᓕᐊᓐ.
ᐃᓚᒋᓪᓗᓂᐅᒃ ᑖᔅᓱᒪ, ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐱᓯᒪᖕᒥᔪᑦ ᑐᖅᑯᐃᓂᕐᒧᑦ ᐊᖏᖃᑎᒌᒍᑎᓂᒃ (GSA) ᐊᑖᒍᑦ ᐅᐃᒍᖓ I ᑮᓇᐅᔭᓕᐅᕋᓱᐊᕐᓂᐊᕐᓗᓂ ᐊᑐᖅᑐᐊᕐᓂᕐᒧᑦ ᑐᓂᓯᒪᔪᑦ ᐱᖃᕐᓂᕋᐅᑎᒥᒃ TMAC-ᑯᑦ ᐱᖁᑎᓂᖏᓐᓂᒃ.
Notes: The KIA currently has $3.49 million in letters of credit, an $8.0 million Corporate Guarantee, and General Security Agreement to back the Corporate Guarantee giving KIA a claim on TMAC assets.

## Slide 28: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐃᓱᒪᕗᑦ ᐅᓪᓗᒥᐅᔪᖅ ᐅᓄᕐᓂᕆᔭᖏᑦ ᓴᓗᒻᒪᖅᓴᐃᔾᔪᑎᒃᓴᑦ ᑮᓇᐅᔭᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᒥᒐᓗᐊᖅᑐᒋᔭᐅᓪᓗᑎᒃ ᑐᐊᕆᔅ ᐅᐊᖕᓇᖓᓂ ᐅᔭᕋᖕᓂᐊᕐᕕᖕᒧᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐸᕐᓇᐃ ᖃᐅᔨᒪᔨᑕᐅᔪᖅ ᕿᒥᕐᕈᓇᓚᐅᕐᒪᑦ TMAC-ᑯᑦ ᐊᒻᒪᓗ ᐃᓄᓕᕆᔨᑐᖃᒃᑯᑦ ᓴᓗᒻᒪᖅᓴᐃᔾᔪᑎᒃᓴᓄᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᑭᖏᓐᓂᒃ ᒥᒃᓴᐅᓴᒃᓯᒪᔪᓂᒃ.
ᐊᖏᔫᑎᑦ ᖃᐅᔨᔭᐅᔪᑦ:
  $28.94 ᒥᓕᐊᓐ ᐃᓄᐃᓴᖕᓂᖅᐹᖑᔪᑦ ᓈᒻᒪᒃᐳᑦ ᐊᒻᒪ ᓇᓕᖅᑯᑦᑎᓯᒪᓂᖅᓴᐅᓪᓗᓂ.
  $24.20 ᐊᒻᒪᓗ $4.74 ᒥᓕᐊᓐ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ ᓄᓇᒧᑦ ᐊᒻᒪ ᐃᒪᕐᒧᑦ ᐊᕕᒃᑕᐅᓪᓗᓂ (84% ᓄᓇᒧᑦ,16% ᐃᒪᕐᒧᑦ).
  ᐊᒥᐊᒃᑯᐊ ᐊᑦᑕᕐᓇᖅᑐᖅ ᐊᒻᒪ ᐊᑭᑦᑐᕆᑎᒋᔪᓐᓇᖅᑕᖓ ᓇᓗᓇᐃᖅᑕᐅᓯᒪᕗᖅ ᓇᐅᑦᑎᐅᒪᔾᔪᑎᖃᖅᑎᓪᓗᒍ 20%-ᒥᒃ, ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᖏᖃᑎᖃᖅᑐᑦ TMAC-ᑯᑦ ᐃᓄᐃᓴᖕᓂᖅᐹᖁᑎᖓᓐᓄᑦ ᐊᒻᒪᓗ ᓇᐅᑦᑎᐅᒪᔾᔪᑎᖏᓐᓄᑦ.
Notes: The current amount of security of $11.49 million is inadequate security for the Doris North mine site give project changes and development.
The KIA’s engineering consultant has reviewed TMAC and INAC reclamation cost models. TMAC’s $28.94 million quantum for security is reasonable and the split in land and water liability is 84% and 16%.
A contingency of 20% exists within the TMAC reclamation estimate. Residual risks and cost escalators as well as questions raised by KIA’ consultant were discussed with TMAC and their engineering consultant. All questions were satisfactorily answered and the KIA accepts and supports TMAC’s reclamation cost estimate for the Doris North mine site.

## Slide 29: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᐃᓄᓕᕆᔨᑐᖃᒃᑯᑦ ᓴᓗᒻᒪᓴᐃᓂᕐᒧᑦ ᐊᑭᒋᓂᐊᖅᑕᖓᓂᒃ ᒥᒃᓴᐅᓴᒃᓯᓯᒪᕗᑦ $44.12 ᒥᓕᐊᓐᖑᓪᓗᓂ.
$43.42 ᒥᓕᐊᓐ (98%) ᐃᓄᐃᑦ ᓄᓇᖁᑎᖏᓐᓄᑦ ᐊᒻᒪᓗ $0.7 ᒥᓕᐊᓐ (2%) ᒐᕙᒪᒃᑯᑦ ᓄᓇᖁᑎᖏᓐᓄᑦ.
ᑖᒃᑯᓇᓐᖓᑦ $43.42 ᒥᓕᐊᓐᓂᑦ, $19.71 ᒥᓕᐊᓐ (45%-ᖓ) ᑐᓂᔭᐅᓚᐅᖅᑐᖅ ᓄᓇᓄᑦ ᒪᓕᒐᖅᑎᒍᑦ ᐊᑭᓕᕆᐊᓕᖕᓄᑦ ᐊᑐᖅᑕᐅᓂᐊᕐᓗᓂ ᐊᒻᒪᓗ $23.72 ᒥᓕᐊᓐ (55%) ᑐᓂᔭᐅᓚᐅᖅᑐᖅ ᐊᑐᖅᑕᐅᓂᐊᕐᓗᓂ ᐃᒪᕐᒧᑦ ᒪᓕᒐᖅᑎᒍᑦ ᐊᑭᓕᕆᐊᓕᖕᓄᑦ.
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᖃᐅᔨᒪᕗᑦ ᑖᒃᑯᐊ ᓄᓇᒧᑦ ᐊᒻᒪ ᐃᒪᕐᒧᑦ ᒪᓕᒐᖅᑎᒍᑦ ᐊᑭᓕᕆᐊᖃᖅᑐᑦ ᐊᒥᒐᓗᐊᕐᓂᖏᓐᓂᒃ ᒪᓕᒡᓗᒋᑦ ᐊᑐᖅᑕᐅᓯᒪᔪᑦ Orbit 25 brine-ᒥᒃ ᑯᕕᑎᓪᓗᒋᑦ.
Notes: INAC’s engineering consultant has a reclamation cost estimate of $44.12 million which is substantially higher than TMAC’s estimate. This primarily due to indirect costs being 175% higher than TMAC’s estimate of indirect costs. INAC’s estimate uses a 5 year time horizon for reclamation in contrast to TMAC’s approximately 2 year time-horizon for preforming reclamation work. INAC’s estimate has about 50% the productivity of TMAC’s estimate which KIA finds questionable.
The INAC estimate acknowledges that 98% of the quantum is associated with IOL while only 2% is Crown Land.
The $43.42 million of IOL security has a split of land water liability of 45% and 55% respectively which the KIA finds unreasonable given our experience with the Newmont and Orbit 25 brine spill at Boston Camp in July of 2011.
Drilling fluid containing potassium chloride had spilled onto the land and subsequently entered a near by water body. About 1200 square metres of tundra was damaged due to elevated chloride levels. The deleterious substance had entered the water body and dissipated quickly in a few days with no loss of fish or damage to the aquatic environment.
Environment Canada at the time charged Newmont and Orbit Grant with breaking Federal environmental laws. Both Newmont and Orbit Grant agreed to contribute to Environment Canada’ environmental fund. No reclamation work was done by the Federal Government to the lake since no damage was done.
KIA investigated possible means of land reclamation, if no actions are taken it will take 15 to 20 years for the land to recover through natural revegetation. Human intervention would require experimentation in the restoration of tundra and remediation work based on experimental results. The human intervention and reclamation of land would be about $3 million.
This clearly illustrates that the liability is primarily with the land and not the water. INAC’s split of land and water liability of 45% and 55% would expose KIA to an excessive amount of risk.

## Slide 30: ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑕ ᐅᖃᐅᓯᒃᓴᖓ:
ᑕᐃᒪᓕ ᑕᒪᓐᓇ ᐊᒃᓱᑲᓪᓚᒃ ᐃᔪᖅᓯᓂᖃᕈᓐᓇᕐᓂᖓᓄᑦ ᐃᓄᖕᓄᑦ ᑖᓐᓇ ᐱᓕᕆᐊᖑᔪᖅ ᐅᒃᐱᕈᓱᒃᐳᒍᑦ ᐋᖅᑭᒋᐊᖅᑕᐅᒃᐸᑦ ᑐᐊᕆᔅ ᐅᐊᖕᓇᖓᓂ Type A ᐃᒪᕐᒧᑦ ᓚᐃᓴᓐᓯᖓ ᐱᔾᔪᑎᖃᑦᑎᐊᕐᓂᖓᓂᒃ ᐊᒻᒪ ᐊᑲᐅᓛᖑᒐᔭᕐᓂᖓᓂᒃ ᐃᓄᖕᓄᑦ ᓈᒻᒪᒋᔭᐅᑐᐊᖅᐸᑦ ᓴᓗᒻᒪᖅᓴᐃᔾᔪᑎᒃᓴᓄᑦ ᑮᓇᐅᔭᑦ ᑐᖅᑯᖅᑕᐅᓯᒪᔪᑦ ᐊᒻᒪ ᐊᕕᒃᑕᐅᓯᒪᓂᕆᔭᖓ ᓄᓇᒧᑦ ᐊᒻᒪ ᐃᒪᕐᒧᑦ ᒪᓕᒐᖅᑎᒍᑦ ᐊᑭᓕᖅᑕᐅᔭᕆᐊᖃᖅᑐᑦ.
Notes: The KIA strongly believes that given the substantial benefits to the Inuit and that all technical issue have been resolved that the amendment of the Doris North Type A Water Licence is warranted. This pending satisfactorily resolving the split of land and water liability with INAC.
If the split of land and water liability is not resolved, KIA still supports the amendment of the water licence and exercise the conditions of its Framework Agreement and Commercial Lease with TMAC to meet its reclamation needs.

## Slide 31: ᐊᑐᓕᖁᔭᓕᐊᑦ:
ᕿᑎᕐᒥᐅᑦ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᖏᑦ ᐊᑐᓕᖁᔭᓕᐅᖅᐳᑦ ᐊᖏᖅᑕᐅᖁᓪᓗᒍ TMAC-ᑯᑦ ᑐᒃᓯᕋᐅᑎᖓᑦ ᐋᖅᑭᒋᐊᖅᑕᐅᖁᓪᓗᒍ ᓇᓗᓇᐃᒃᑯᑕᖓᑦ 003 ᑐᐊᕆᔅ ᐅᐊᖕᓇᖓᓂ ᐱᓕᕆᔭᐅᔪᒥ.
ᖁᐊᓇᖅ
ᐊᐱᖅᑯᑎᒃᓴᐃᓐ?
Notes: KIA recommends approval of the TMAC application for amendment of the Type A Water licence for the Doris North mine site.
Thank you
Questions?