## Slide 1: Meliadine Type A Water License
Community Meeting
October 14, 2015,
Rankin Inlet, NU
Hutchinson
Environmental Sciences Ltd.

## Slide 2: Overview ᕿᒥᕐᕈᓂᖅ ᐱᓕᕆᐊᖑᔪᓂᒃ
Our review was comprised of 27 separate information requests and technical comments
We have communicated with AEM over the past month, clarifying issues and reaching resolutions where possible
  21 of our concerns are resolved at this point
ᕿᒥᕐᕈᓂᖅᐳᑦ ᐃᓗᓕᖃᓚᐅᖅᑐᖅ 27ᓂᒃ ᐊᔾᔨᒌᖏᑦᑐᓂᒃ ᑐᓴᒃᑲᓂᕈᒪᔾᔪᑎᓂᒃ ᐊᒻᒪ ᐃᓱᒪᒋᔭᑉᑎᓐᓂᒃ.
ᐅᖃᖃᑎᒋᓯᒪᔭᕗᑦ AEMᑯᑦ ᑕᖅᑭᐅᓚᐅᖅᑐᒥ ᑐᑭᓯᓐᓇᖅᓯᒋᐊᕈᑎᓂᒃ ᐅᖃᐅᓯᖃᖅᖢᑕ ᐊᒻᒪ ᐋᖅᑭᒃᓯᑉᓗᑕ ᐃᓚᖏᓐᓂᒃ.
21ᓂᒃ ᐃᓱᒫᓗᑕᐅᓚᐅᖅᑐᓂᒃ ᐋᖅᑭᒃᓯᓯᒪᓕᖅᑐᒍᑦ ᒫᓐᓇᒧᑦ.

## Slide 3: Overview ᕿᒥᕐᕈᓂᖅ ᐱᓕᕆᐊᖑᔪᓂᒃ
This presentation accompanies our submission to the Nunavut Water Board on October 5, 2015
  “R151002_J150077_Meliadine WL A Technical Review_FINAL”
  That submission documents our concerns and resolutions as of the submission date
ᑖᒻᓇ ᐃᓗᓕᖃᖅᑐᖅ ᑐᓂᓚᐅᖅᑕᑉᑎᓐᓂᒃ ᓄᓇᕗᒻᒥ ᐃᒪᓕᕆᔨᒃᑯᓐᓄᑦ ᐊᒃᑑᐸ 5, 2015ᒥ
“R151002_J150077_Meliadine WLA Technical Review_Final”
ᑕᐃᒻᓇ ᑐᓂᓚᐅᖅᑕᕗᑦ ᓇᓗᓇᐃᕆᔪᖅ ᐃᓱᒫᓗᑎᑉᑎᓐᓂᒃ ᐊᒻᒪ ᐋᖅᑭᒋᐊᕈᑕᐅᓚᐅᖅᑐᓂᒃ ᑕᐃᑲᓂ ᐅᑉᓗᕐᒥ.

## Slide 4: Guiding Principles ᑐᙵᕕᒋᑉᓗᒋᑦ ᒪᓕᓚᐅᖅᑕᕗᑦ ᐅᑯᐊ
Our review is guided by
  Nunavut Water Board’s (NWB) water quality framework
    protect, manage and regulate freshwaters in Nunavut in a manner that will provide the optimum benefits for the residents of the territory in particular and Canadians in general
  The Nunavut Land Claims Agreement, and
  The right of Kivalliq Inuit to minimized changes to the environment
      ᕿᒥᕐᕈᓂᕆᔭᕗᑦ ᒪᓕᓚᐅᖅᑐᖅ ᐅᑯᓂᖓ
        ᓄᓇᕗᒻᒥ ᐃᒪᓕᕆᔨᒃᑯᑦ ᐃᒪᑦᑎᐊᕙᖃᕐᓂᕐᒧᑦ ᒪᓕᒐᖏᑦ
          ᒥᐊᓂᕆᓗᒍ, ᐊᐅᓚᑦᑎᐊᕐᓗᒎᖅᑐᖅᑕᐅᓂᖓ ᐃᒪᐃᑦ ᑕᓯᕐᓂ ᓄᓇᕗᒻᒥ ᐱᐅᓂᖅᐹᑎᒍᑦ ᐱᕙᓪᓕᐅᑕᐅᔪᓐᓇᖁᑉᓗᒍ ᐊᖏᓂᖅᐹᒥᒃ ᐃᓄᖁᑎᖏᓐᓄᑦ ᓄᓇᕗᑦ ᐊᒻᒪ ᑲᓇᑕᒥᐆᑦ.
        ᓄᓇᕗᑦ ᐊᖏᖃᑎᒌᒍᑖ, ᐊᒻᒪ
        ᑭᕙᓪᓕᕐᒥ ᐃᓄᐃᑦ ᐊᔪᙱᓐᓂᖏᑦ ᒥᑭᓂᖅᐹᒥᒃ ᐊᒃᑐᖅᑕᐅᖁᑉᓗᒍ ᐊᕙᑎᖓᑦ

## Slide 5: Overview of Concerns ᑕᑯᒋᐊᕐᓂᖅ ᐃᓱᒫᓗᑎᓂᒃ

## Slide 6: Freshwater Quality
Concerns
KIA-WL-04, 06, 11, 19, 22, 23
Freshwater quality in the collection ponds at closure
Use of Inuit Qaujimajatuqangit to monitor the freshwater environment
Contact water at Itivia Harbour
Discharges from the Meliadine sewage treatment plant
Adequate treatment of process water prior to discharge
ᐃᓱᒫᓗᑦ
KIA-WL-04, 06, 11, 19, 22, 23
ᐃᒪᐅᑉ ᖃᓄᐃᓐᓂᖓ ᑕᓯᕋᕐᓂ ᑲᑎᖅᓱᐃᕕᙱ ᒪᑐᓕᖅᐸᑦ
ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᑦ ᐊᑐᖅᑕᐅᓂᖏᑦ ᖃᐅᔨᓴᖅᑎᓪᓗᒋᑦ ᐃᒪᐅᑉ ᖃᓂᐅᓂᖓᓂᒃ
ᐃᒪᖅ ᐃᑎᕕᐋᓂ
ᑯᕕᑎᑕᐅᔪᑦ ᐃᒪᕐᓘᑦ ᑕᓯᕐᔪᐊᑉ ᐃᒪᕐᓘᑎᖃᕐᕕᐊᓂᑦ
ᐃᒪᕐᓗᑏᑦ ᓴᓗᒻᒪᖅᑕᐅᑎᐊᕆᐊᖃᕐᓂᖏᑦ ᑯᕕᓚᐅᓚᐅᖃᖅᑎᓐᓇᒋᑦ

## Slide 7: Freshwater Quality
Status
AEM has agreed to:
  Update standards for freshwater in the collection ponds after the mine has closed
  Work with the KIA to incorporate Inuit Qaujimajatuqangit into monitoring and determining the significance of observed changes
  Continue to use established standards when dealing with contact water at Itivia
  Treat process and contact water as needed to ensure it is safe for discharge to Meliadine Lake
ᖃᓄᐄᓕᕐᓂᖓ
AEM ᐊᖏᖅᑐᖅ:
  ᓄᑕᐅᓯᒋᐊᕐᓂᐊᖅᓗᒋᑦ ᐃᒪᐅᑉ ᖃᓂᐅᓂᖏᓐᓄᑦ ᖃᐅᔨᓴᕐᓃᑦ ᒪᑐᒃᐸᑦ ᐅᔭᕋᒃᑕᕆᐊᖅ
  ᐱᓕᕆᖃᑎᒋᓗᒋᑦ ᑭᐊᑯᑦ ᐊᑐᓕᖁᑉᓗᒋᑦ ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᓐᓂᒃ ᖃᐅᔨᓴᕌᖓᑕ ᐅᔾᔨᖅᑐᕌᖓᑕᓗ ᐊᓯᔾᔨᖅᐸᓪᓕᐊᔪᓂᒃ
  ᐊᑐᕐᓂᐊᕐᓗᑎᒃ ᒪᓕᒐᕆᔭᐅᔪᓂᒃ ᐱᓕᕆᐊᖃᕌᖓᒥᒃ ᐃᒪᕐᒥᒃ ᐊᒃᑐᐊᔭᐅᔪᒥᒃ ᐃᑎᕕᐋᓂ
  ᐃᕐᕈᕐᓗᒋᑦ ᐃᒪᐃᑦ ᐊᒃᑐᖃᑐᔪᑐᓗᕆᐊᓇᕐᓂᖃᕈᓐᓃᖁᑉᓗᒋᑦ ᑰᒃᑎᑕᐅᓚᐅᖏᓐᓂᖏᓐᓂ ᑕᓯᕐᔪᐊᕐᒧᑦ

## Slide 8: Saline Water ᑕᕆᐅᓖᑦ ᐃᒪᐃᑦ ᓄᓇᒥᖔᖅᑐᑦ
Concerns
KIA-WL-05
Operations at Meliadine will come into contact with saline groundwater below the permafrost
There is currently no long term plan to safely dispose of the saline groundwater
ᐃᓱᒫᓗᑦ
KIA-WL-05
ᐱᓕᕆᔩᑦ ᑕᓯᕐᔪᐊᕐᒥ ᑕᕆᐅᓕᖕᒥᒃ ᐃᒪᕐᒥᒃ ᓄᓇᒥᑦ ᐊᒃᑐᓂᐊᕐᒪᑕ ᖁᐊᖏᓐᓇᓲᑉ ᐊᑖᓂᑦ
ᒫᓇ ᑕᒪᑐᒥᖓ ᐃᒪᕐᒥᒃ ᖃᓄᖅ ᐲᔭᐃᓂᐊᕐᒪᖕᓈᕐᒥᒃ ᓇᓗᓇᐃᖅᓯᒪᖏᑦᑐᑦ

## Slide 9: Saline Water
Status
The KIA have required that a saline water management plan is developed prior to any discharges to the environment
Environment Canada will need to commit to provide AEM with timely guidance so that the project can safely proceed as scheduled
ᒪᓐᓇ
KIA ᑐᑭᔅᕋᖅᓯᒪᔪᖅ ᐊᐅᓚᑦᑎᓂᐊᕐᓂᕐᒥᒃ ᑕᕆᐅᓖᑦ ᒥᒃᓵᓄᑦ ᓴᖅᑭᑦᑎᖁᔨᓯᒪᔪᑦ ᐃᒪᕐᒥᒃ ᖃᓂᐅᑦᑐᑐᐃᓐᓇᕐᓂᒃ ᑯᕕᓯᓂᖃᓚᐅᖅᑎᓐᓇᒍ ᐊᕙᑎᒧᑦ
ᐊᕙᑎᓕᕆᔩᑦ ᑲᓇᑕᒥ ᑐᓂᓯᓂᐊᕐᓂᖃᕆᐊᖃᕐᓂᐊᖅᑐᑦ AEM ᑯᓐᓄᑦ ᐃᒪᓐᓈᕈᑎᓂᒃ ᐱᓕᕆᐊᖓᑦ ᑲᔪᓯᑦᑎᐊᕈᓐᓇᖁᑉᓗᒍ

## Slide 10: Modelling
Concerns
KIA-WL-03, 09, 14, 24
The presented water balance did not account for a range of potential environmental conditions
There was uncertainty in the model predicting concentrations of the effluent in Meliadine Lake and how that effluent will mix in the receiving environment
AEM’s assessment of water quality in the collection ponds after the mine has closed needed further detail
ᐃᓱᒫᓗᑦ
t
KIA-WL-03, 09, 14, 24
ᓴᖅᑭᑕᐅᓚᐅᖅᑐᖅ ᐃᒪᐅᑉ ᒥᒃᓵᓄᑦ ᐃᓗᓕᖃᓚᐅᖏᒻᒪᑦ ᐊᒥᓱᓂᒃ ᐊᕙᑎᒧᑦ ᐊᒃᑐᖅᑕᐅᔾᔪᑕᐅᓇᔭᖅᑐᓂᒃ
ᓇᓗᓇᕐᓂᖃᓚᐅᕐᒪᑦ ᐅᒃᑑᑕᐅᔪᒧᑦ ᐃᒪᕐᓘᑦ ᑰᒃᐸᓪᓕᐊᓇᔭᖅᑐᖅ ᖃᓄᐃᓐᓇᔭᕐᓂᖓᓂᒃ ᑕᓯᕐᔪᐊᕐᒥ ᖃᓄᖅ ᐊᒃᑎᒋᓇᔭᖅᐸᑦ ᐊᒻᒪ ᖃᓄᖅ ᐊᑯᖃᓯᐅᑎᓇᔭᕐᒪᖓᑦ ᑰᒡᕕᒋᔭᖓᓄᓐᑦ
AEM ᑯᑦ ᖃᐅᔨᓴᕐᓂᖏᑦ ᐃᒪᐅᑉ ᖃᓂᐅᓐᓂᖓᑕ ᒥᒃᓵᓄᑦ ᑕᓯᕋᕐᓂ ᐅᔭᕋᒃᑕᕆᐊᖅ ᐅᑯᐊᓚᐅᖅᑎᓪᓗᒍ ᐃᓗᓕᖃᒃᑲᓐᓂᕆᐋᓕᒃ

## Slide 11: Modelling
Status
AEM has presented water balances under additional scenarios:
  Extreme wet and extreme dry
AEM has provided more information on effluent model inputs and conducted additional modeling under alternate scenarios demonstrating effluent diffused to Meliadine Lake will meet water quality guidelines for safety
AEM will revisit the water quality predictions for closure as more data is generated at the site
  Information available at this time does not indicate a significant concern for the environment
ᖃᓂᐆᓕᕐᓂᖅ
AEM ᓴᖅᑭᑦᑎᒃᑲᓐᓂᓚᐅᖅᑐᖅ ᑕᐅᑐᖅᑰᒐᒃᓴᓂᒃ ᐃᒪᐅᑉ ᖃᓂᐅᓐᓂᕆᓇᔭᖅᑕᖓᓂᒃ ᐊᔾᔨᐅᖏᑦᑐᓂᒃ:
  ᖃᐅᓯᕐᓇᕕᒡᔪᐊᖅᑎᓪᓗᒍ ᐊᒻᒪ ᐸᓂᕐᓇᕕᒡᔭᖅᑎᓪᓗᒍ
AEM ᑐᓂᓯᓯᒪᕗᑦ ᑕᐅᑐᖅᑰᒐᒃᓴᒃᑲᓐᓐᓂᕐᓂᒃ ᐊᒻᒪ ᓴᖅᑭᑦᑎᒃᑲᓐᓂᖅᖢᑎᒃ ᑕᐅᑐᖅᑰᒐᒃᓴᓂᒃ ᐊᔾᔨᒌᖏᑦᑐᓂᒃ ᓇᓗᓇᐃᕆᑉᓗᑎᒃ ᐃᒪᕐᓘᑦ ᖃᓂᐅᓐᓂᕆᓇᔭᖅᑕᖓᓂᒃ ᑯᕕᔭᐅᓕᕋᔭᖅᐸᑦ ᑕᓯᕐᔪᐊᕐᒧᑦ ᒪᓕᒐᔭᕐᓗᑎᒡᓗ ᐃᒪᐅᑉ ᓈᒻᒪᖕᓂᕆᔭᕆᐊᖃᖅᑕᖏᓐᓂᒃ
AEM ᖃᐅᔨᒋᐊᒃᑲᓐᓂᕐᓂᐊᖅᐳᑦ ᐃᒪᐅᑉ ᖃᓄᐃᓐᓂᕆᓇᔭᖅᑕᖓᓂᒃ ᐅᒃᑯᐊᓕᖅᐸᑦ ᑐᑭᓯᕙᓪᓕᐊᓂᑎᒃ ᒪᓕᒡᓗᒋᑦ ᐱᓕᕆᕝᕕᖕᓂ
  ᒫᓇ ᖃᐅᔨᒪᔭᐅᔪᑦ ᐃᓱᒫᓘᑕᐅᓗᐊᖏᑦᑐᑦ ᐊᕙᑎᒧᑦ

## Slide 12: Waste Management ᓱᕐᕈᑯᓂᒃ ᐊᐅᓚᑦᑎᓂᖅ
Concerns
KIA-WL-01, 02, 13, 21, 27
AEM will only use overburden at closure to cap the Tailings Storage Facility
  Overburden contains natural sources of vegetation that could also be used to revegetate the site at closure
There was uncertainty in the application as to when revegetation of the site could be expected after closure
Concerns regarding the timeline for progressive reclamation of the Tailings Storage Facility
Biodegradation of contaminated soil in the landfarm may not proceed fast enough to ensure no residual effects of the project
ᐃᓱᒫᓗᑦ
KIA-WL-01, 02, 13, 21, 27
AEM ᐊᑐᕐᓂᐊᖅᑐᖅ ᓯᐅᕋᖅᑕᕐᓂᑯᓂᒃ ᑲᑎᑕᕕᓂᕐᓂᒃ ᑭᓯᐋᓂ ᒪᑐᓕᖅᐸᑦ ᓴᐅᓯᔾᔪᑎᒋᓗᒋᑦ ᐅᔭᕋᒃᑕᖅᑕᐅᓂᑯᕕᓂᕐᓂᒃ ᑲᑎᖅᓱᐃᕕᖕᒥ
  ᓯᐅᕋᖅᑕᕐᓂᑯᕕᓃᑦ ᐃᓗᓕᖃᓲᑦ ᓄᓇᕋᕕᓂᕐᓂᒃ, ᐱᕈᖅᑐᕕᓂᕐᓂᒡᓗ ᐊᑐᕈᓐᓇᖅᑐᑦ ᐱᕈᖅᑐᖃᒃᑲᓐᓂᓕᖅᑎᑦᑎᓂᕐᒥᒃ
ᓇᓗᓇᐃᖅᓯᒪᓚᐅᖏᒻᒪᑦ ᑐᒃᓯᕋᐅᑎᒥ ᖃᖓ ᐱᕈᖅᑐᑦ ᓴᖅᑭᓕᕋᔭᕐᒪᖔᑖ ᐅᒃᑯᐊᓚᐅᖅᑎᓪᓗᒍ
ᐃᓱᒫᓗᑏᐃᑦ ᖃᖓ ᐱᓕᕆᐋᖑᓕᕋᔭᕐᒪᖓᑦ ᐅᔭᕋᒃᑕᖅᑕᐅᓂᑯᕕᒃᑯᕕᒃ ᓴᓗᒻᒪᖅᑕᐅᒋᐊᕋᔭᕐᒪᖓᑦ
ᓄᓇᐃᑦ ᐃᕐᕈᕆᐊᓖᑦ ᐃᕐᕈᖅᑐᐃᕝᕕᖕᒥ ᐱᐊᓚᐃᓗᐊᑐᐃᓐᓇᕆᐊᖃᕐᒪᑕ ᐃᕐᕈᖅᐸᓪᓕᐊᓂᖏᑦ ᐃᖢᐊᖏᓕᐅᕈᑐᖃᖁᓇᒍ ᐱᓕᕆᐊᖅ

## Slide 13: Waste Management ᓱᕐᕈᑯᓂᒃ ᐊᐅᓚᑦᑎᓂᖅ
Status
AEM will investigate additional means to store and use overburden to restore the mine site
Studies are being undertaken in collaboration with the University of Saskatchewan to assess revegetation and potential timelines at the site
Further information is being provided regarding biodegradation rates and potential soil amendment options
ᒪᓐᓇ ᖃᓄᐃᓐᓂᖓ
AEM ᖃᐅᔨᓴᕐᓂᐊᖅᐳᖅ ᖃᓄᖅ ᓄᓇ ᓴᓕᒃᑕᐅᓂᑯ ᑐᖅᑰᒪᔭᐅᔪᓐᓇᕐᒪᖓᑦ ᐅᔭᕋᒃᑕᕐᕕᒃ ᐅᑎᖅᑎᑕᐅᕙᓪᓕᐊᓕᖅᐸᑦ ᐊᑐᒐᒃᓴᓂᒃ
ᖃᐅᔨᓴᕐᓂᖃᖅᑐᖅ ᐱᓕᕆᖃᑎᒋᑉᓗᒋᑦ ᓴᔅᑲᑐᐊᓐ ᓯᓚᑦᑐᖅᓴᕐᕕᖓᓂᒃ ᐱᕈᖅᑐᖃᓕᒃᑲᓐᓂᕋᔭᕐᓂᐅᑉ ᒥᒃᓵᓄᑦ
ᑐᓴᒐᒃᓴᓂᒃ ᐱᕙᓪᓕᐊᒃᑲᓐᓂᖅᑐᑦ ᓄᓇᐅᑉ ᐊᒻᒪ ᐃᑉᔨᐅᑦ ᐅᑎᖅᐸᓪᓕᐊᓂᖓᑕ ᒥᒃᓵᓄᑦ
  ᐃᑉᔪᕐᓂᒃ ᐃᓚᓯᓗᑎᒃ ᓱᕈᐊᓪᓚᒃᐸᓪᓕᕈᑎᒃᓴᓂᒃ ᐅᖃᐅᓯᓖᑦ

## Slide 14: Dust Management ᐳᔪᖃᑖᖕᒥᒃ ᐊᐅᓚᑦᑎᓂᖅ
Concerns
KIA-WL-17, 18, 20, 25, 26,
AEM is now dry stacking tailings. This reduces the impact to water but has the potential to generate more dust
More detail is required on the dust monitoring program
Dust from the ore pile may not be adequately managed at closure
AEM is currently intending to use saline groundwater as a dust suppressant along the roads
Dust from the bypass road near the hamlet may reach Nipissar Lake
ᐃᓱᒫᓗᑦ
AEM ᒫᓇ ᐸᓂᖅᑐᓂᒃ ᓴᕕᒃᓴᐃᔭᖅᓯᒪᔪᓂᒃ ᐅᔭᕋᒃᑕᕐᓂᑯᓂᒃ ᑲᑎᖅᓱᐃᖕᒪᑕ ᐳᖅᑐᓯᕙᓪᓕᐊᑉᓗᒋᑦ ᑖᒻᓇ ᐃᒪᕐᒧᑦ ᐊᒃᑐᐃᖏᓐᓂᖅᓴᖅ ᑭᓯᐋᓂ ᐳᔪᖃᑖᓕᐅᑐᐃᓐᓇᕆᐋᓕᒃ
ᑐᓴᒃᑲᓐᓂᕆᐊᖃᖅᑐᒍᑦ ᐳᔪᖃᑖᑉ ᒥᒃᓴᓄᑦ ᐊᐅᓚᑦᑎᓂᕐᒥᒃ
ᓴᕕᒃᓴᖃᕐᕖᒃ ᐳᔪᖃᑖᖃᕐᓂᖏᑦ ᐅᒃᑯᐋᓕᖅᐸᑦ ᐱᓕᕆᐊᖑᑦᑎᐊᖏᑐᐃᓐᓇᕆᐊᓖᑦ
AEM ᐊᑐᕐᓂᐊᕐᓂᕋᖅᑐᑦ ᑕᕆᐅᓕᖕᓂᒃ ᐃᒪᕐᒥᒃ ᓄᓇᐅᑉ ᐃᓗᐋᓂᖓᖅᑐᒥᒃ ᐳᔪᖃᑖᒋᒃᑯᑕᐅᖁᑉᓗᒍ ᐊᑉᖁᑎᓄᑦ
ᐳᔪᖃᑖᒃ ᐊᑉᖁᒥ ᕼᐋᒻᓕᑦ ᖃᓂᒋᔮᓂ ᑕᓯᑦᓈᕐᒧᑦ ᑎᑭᑐᐃᓐᓇᕆᐊᓕᒃ

## Slide 15: Dust Management ᐳᔪᖃᑖᖕᒥᒃ ᐊᐅᓚᑦᑎᓂᖅ
Status
AEM has committed to provide more detailed dust monitoring before any disposal of tailings
Criteria triggering dust management at closure will be provided for KIA review
AEM will apply to the Government of Nunavut to permit saline groundwater from the Meliadine site as a dust suppressant
Alternative bypass routes are being explored to safeguard Nipissar Lake
ᒪᓐᓇ
AEM ᐅᖃᖅᓯᒪᔪᑦ ᐃᓗᓕᖃᕐᓂᖅᓴᒥᒃ ᓴᖅᑭᑦᑎᓂᐊᕐᓂᕋᖅᖢᑎᒃ ᐳᔪᖃᑖᑉ ᒥᒃᓵᓄᑦ ᐊᒃᑕᑰᓚᐅᖏᓐᓂᕐᒥᓂ ᐅᔭᕋᒃᑕᕐᓂᑯᕕᓂᕐᓂᒃ
ᒪᓕᒃᑕᐅᓂᐊᖅᑐᑦ ᐳᔪᖃᑖᒌᒃᑯᑏᐃᑦ ᒥᒃᓴᓄᑦ ᐅᒃᑯᐊᓕᖅᐸᑦ ᑐᓂᔭᐅᓂᐊᖅᑉᑦ kiaᑯᓐᓄᑦ ᕿᒥᕐᕈᔭᐅᔪᒃᓴᐅᓗᑎᒃ
AEM ᑐᒃᓯᕋᕐᓂᐊᖅᑐᑦ ᓄᓇᕗᑦ ᒐᕙᒪᖓᓄᑦ ᐊᑐᕈᓐᓇᐅᑎᒥᒃ ᐃᒪᕐᒥᒃ ᓄᓇᒥᙶᖅᑐᒥᒃ ᑕᕆᐆᓕᖕᒥᒃ ᐳᔪᖃᑖᒋᒃᑯᑕᐅᔪᓐᓇᖁᑉᓗᒍ
ᐊᓱᐊᒎᕐᕕᒃᓴᓂᒃ ᒫᓇ ᕿᒥᕐᕈᔪᑦ ᑕᓯᑦᓈᑉ ᒥᒃᓵᓄᑦ

## Slide 16: Environmental Monitoring ᐊᕙᑎᒥᒃ ᐅᔾᔨᖅᑐᕐᓂᖅ
Concerns
KIA-WL- 07, 08, 10, 12, 15, 16
Insufficient monitoring locations were proposed for effluent discharges to Meliadine Lake near the diffuser
No monitoring locations were proposed near Itivia Harbour
Uncertainty existed in the quality control procedures and for the environmental monitoring analytical standards
The fish tissue baseline had not been updated
Some water quality monitoring locations were not part of the adaptive management framework
ᐃᓱᒫᓗᑦ
KIA-WL- 07, 08, 10, 12, 15, 16
ᐊᒥᒐᓗᐊᓚᐅᕐᒪᑕ ᖃᐅᔨᓴᕐᕕᒃᓴᐃᑦ ᐃᒪᕐᓘᒥᒃ ᑯᕕᔭᐅᔪᓂᒃ ᑕᓯᕐᔪᐊᕐᒧᑦ ᖃᐅᔨᓴᕐᕕᐅᓇᔭᖅᑐᑦ ᐅᓗᕆᐊᓇᕈᓐᓂᕐᓯᕕᐅᑉ ᖃᓂᒋᔮᓂ
ᖃᐅᔨᓴᕐᕕᒃᓴᒥᒃ ᓇᓗᓇᐃᖅᓯᒪᔪᖃᓚᐅᖏᑦᑐᖅ ᐃᑎᕚᓂ
ᓇᓗᓇᐃᖅᓯᒪᓚᐅᖏᒻᒪᑦ ᖃᐅᐃᓴᕐᓃᑦ ᓈᒪᒐᔭᕐᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ ᐊᑐᖅᑕᐅᓇᔭᖅᑐᑦ ᐊᒻᒪ ᐊᕙᑎᒧᑦ ᖃᐅᔨᓴᐅᑏᑦ ᕿᒥᕐᕈᓂᖏᓐᓄᑦ
ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓃᑦ ᓄᑕᐅᓯᒋᐊᖅᓯᒪᖏᖦᖢᑎᒃ
ᐃᓚᖏᑦ ᐃᒪᐅᑉ ᒥᒃᓴᓄᑦ ᖃᐅᔨᓴᕐᕖᑦ ᐃᓚᐅᓚᐅᖏᑦᑐᑦ ᐅᓚᑦᑎᓂᐅᑉ ᒥᒃᓵᓄᑦ ᓇᓇᓯᒪᐅᑦ

## Slide 17: Environmental Monitoring ᐊᕙᑎᒥᒃ ᐅᔾᔨᖅᑐᕐᓂᖅ
Status
Discussions with AEM regarding additional effluent monitoring locations are ongoing
AEM is exploring monitoring locations near Itivia Harbour to characterize project related impacts
Additional detail is being provided for the quality assurance and quality control response framework
AEM is working with the KIA to ensure the analysis of water quality is sensitive enough to detect changes in the environment
AEM has collected more fish tissue samples and will update the baseline
Sample locations of concern have now been included in the adaptive management framework
ᒫᓐᓇ
ᐅᖃᖃᑎᒋᓯᒪᕙᕗᑦ AEM ᖃᐅᔨᓴᖅᑕᐅᕝᕖᑦ ᐃᒪᕐᓗᑏᑦ ᐃᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ
AEM ᕿᒥᕐᕈᔪᑦ ᖃᐅᔨᓴᕐᕕᒃᓴᐅᑉ ᒥᒃᓵᓄᑦ ᐃᑎᕕᐋᓂᖃᐅᔨᔪᓐᓇᖁᑉᓗᒍ ᐃᒃᐱᖕᓇᕐᓂᐅᓇᔭᖅᑐᑦ ᐱᓕᕋᖑᔪᓄᑦ ᐊᒃᑐᖅᑕᐅᔪᓐᓇᕐᑐᑦ
ᑐᓴᒐᒃᓴᒃᑲᓐᓂᕐᓂᒃ ᓴᖅᑭᑦᑎᕙᓪᓕᐊᔪᑦ ᐱᐅᔪᒥᒃ ᓴᖅᑭᑦᑎᔪᓐᓇᕐᓂᕐᒥᒃ ᐊᐅᓚᓐᓂᖏᓐᓄᑦ
AEM ᐱᓕᕆᖃᑎᖃᖅᐳᖅ KIA ᒥᒃ ᐃᒪᕐᒥᒃ ᖃᐅᔨᓴᕐᓂᖅ ᐃᒃᐱᒍᓱᑦᑎᐊᕋᓗᐊᕐᒪᖔᑦ ᖃᐅᔨᔪᓐᓇᕐᓗᓂ ᒥᑭᓂᖅᐹᒥᒃ ᐊᓯᔾᔨᕐᓂᖅᑕᖃᖅᐸᑦ ᐊᕙᑎᒥᒃ
AEM ᑲᑎᖅᓱᐃᓯᒪᒃᑲᓂᖅᐳᑦ ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑕ ᒥᒃᓵᓄᑦ ᐊᒻᒪ ᓄᑕᐅᓯᒋᐊᕐᓂᐊᕐᓗᒍ ᖃᐅᔨᒪᓂᑎᑦ
ᐃᓱᒫᓗᑕᐅᔪᑦ ᑲᑎᖅᓱᐃᕕᒃᓴᐃᑦ ᐃᓚᐅᑎᑕᐅᓕᖅᑐᑦ ᐊᐅᓚᑦᑎᔩᑦ ᐱᓕᕆᐊᖏᑦᑕ ᐃᓗᐋᓂ

## Slide 18: Conclusion ᐱᐋᓂᒋᐋᕈᑦ
AEM has worked with the KIA to resolve our concerns and we hope to be in agreement on all issues prior to the hearings
ᐱᓕᕆᖃᑎᖃᖅᓯᒪᕗᖅ KIA ᑯᓐᓂᑦ ᐃᓱᒫᓗᑎᕗᑦ ᐋᖅᑭᒐᓱᒃᖢᒋᑦ ᐊᒻᒪ ᓯᐅᒪᕗᒍᑦ ᐊᖏᖃᑎᒌᒍᓐᓇᕈᒪᑉᓗᑕ ᑕᒪᐃᓐᓄᑦ ᐃᓱᒫᓗᑎᓄᑦ ᓈᓚᒋᐊᖅᑐᖅᑐᑦ ᐱᒋᐋᓚᐅᖅᑎᓐᓇᒋᑦ

## Slide 19: Questions?
ᐊᐱᖅᑯᑎᑕᖃᖅᐹ?