## Slide 1: ᑕᓯᕐᔪᐊᕐᒥ ᐃᒪᕐᒥᒃ ᐊᑐᕈᓐᓇᐅᑎᑖᕐᓂᖅ
October 14-15, 2015,
Rankin Inlet, NU
Hutchinson
Environmental Sciences Ltd.

## Slide 2: Overview
This presentation accompanies our submission to the Nunavut Water Board on October 5, 2015
  “R151002_J150077_Meliadine WL A Technical Review_FINAL”
  That submission documents our concerns and resolutions as of the submission date
Our review was comprised of 27 separate information requests and technical comments
We have communicated with AEM over the past month, clarifying issues and resolving some
21 of our concerns are resolved at this point
  AEM has documented their commitments in a spreadsheet they intend to submit to the Nunavut Water Board
    This spreadsheet has yet to be reviewed by the KIA

## Slide 3
ᕿᒥᕐᕈᓂᖅ ᐱᓕᕆᐊᖑᔪᓂᒃ
ᑖᒻᓇ ᐃᓗᓕᖃᖅᑐᖅ ᑐᓂᓚᐅᖅᑕᑉᑎᓐᓂᒃ ᓄᓇᕗᒻᒥ ᐃᒪᓕᕆᔨᒃᑯᓐᓄᑦ ᐊᒃᑑᐸ 5, 2015ᒥ
“R151002_J150077_Meliadine WLA Technical Review_Final”
ᑕᐃᒻᓇ ᑐᓂᓚᐅᖅᑕᕗᑦ ᓇᓗᓇᐃᕆᔪᖅ ᐃᓱᒫᓗᑎᑉᑎᓐᓂᒃ ᐊᒻᒪ ᐋᖅᑭᒋᐊᕈᑕᐅᓚᐅᖅᑐᓂᒃ ᑕᐃᑲᓂ ᐅᑉᓗᕐᒥ.
ᕿᒥᕐᕈᓂᖅᐳᑦ ᐃᓗᓕᖃᓚᐅᖅᑐᖅ 27ᓂᒃ ᐊᔾᔨᒌᖏᑦᑐᓂᒃ ᑐᓴᒃᑲᓂᕈᒪᔾᔪᑎᓂᒃ ᐊᒻᒪ ᐃᓱᒪᒋᔭᑉᑎᓐᓂᒃ.
ᐅᖃᖃᑎᒋᓯᒪᔭᕗᑦ AEMᑯᑦ ᑕᖅᑭᐅᓚᐅᖅᑐᒥ ᑐᑭᓯᓐᓇᖅᓯᒋᐊᕈᑎᓂᒃ ᐅᖃᐅᓯᖃᖅᖢᑕ ᐊᒻᒪ ᐋᖅᑭᒃᓯᑉᓗᑕ ᐃᓚᖏᓐᓂᒃ.
21ᓂᒃ ᐃᓱᒫᓗᑕᐅᓚᐅᖅᑐᓂᒃ ᐋᖅᑭᒃᓯᓯᒪᓕᖅᑐᒍᑦ ᒫᓐᓇᒧᑦ.
    AEM ᑯᑦ ᑎᑎᕋᖅᓯᒪᔪᑦ ᐱᒋᐊᕐᓂᕆᓂᐊᖅᑕᒥᓂᒃ ᑕᑯᔭᒃᓴᓄᑦ ᑐᓂᓂᐊᖅᑕᒥᓄᑦ ᐃᒪᓕᕆᔨᒃᑯᑦ ᑲᑎᒪᔨᖏᓐᓄᑦ.
    ᑖᒻᓇ ᑕᑯᔭᒃᓴᖅ ᕿᒥᕐᕈᔭᐅᓯᒪᖏᑦᑐᖅ ᓱᓕ ᑮ ᐊᐄ ᐄ ᑯᓐᓄᑦ.

## Slide 4: Guiding Principles
Our review is guided by
  Nunavut Water Board’s (NWB) water quality framework
    protect, manage and regulate freshwaters in Nunavut in a manner that will provide the optimum benefits for the residents of the territory in particular and Canadians in general
  The Nunavut Land Claims Agreement, and
  The right of Kivalliq Inuit to minimal changes to the environment
The Kivalliq Inuit Association contracted the services of Hutchinson Environmental Sciences Ltd. and GeoVector Management Inc. to assist with the technical review of the licence.

## Slide 5: ᑐᙵᕕᒋᑉᓗᒋᑦ ᒪᓕᓚᐅᖅᑕᕗᑦ ᐅᑯᐊ
      ᕿᒥᕐᕈᓂᕆᔭᕗᑦ ᒪᓕᓚᐅᖅᑐᖅ ᐅᑯᓂᖓ
        ᓄᓇᕗᒻᒥ ᐃᒪᓕᕆᔨᒃᑯᑦ ᐃᒪᑦᑎᐊᕙᖃᕐᓂᕐᒧᑦ ᒪᓕᒐᖏᑦ
          ᒥᐊᓂᕆᓗᒍ, ᐊᐅᓚᑦᑎᐊᕐᓗᒎᖅᑐᖅᑕᐅᓂᖓ ᐃᒪᐃᑦ ᑕᓯᕐᓂ ᓄᓇᕗᒻᒥ ᐱᐅᓂᖅᐹᑎᒍᑦ ᐱᕙᓪᓕᐅᑕᐅᔪᓐᓇᖁᑉᓗᒍ ᐊᖏᓂᖅᐹᒥᒃ ᐃᓄᖁᑎᖏᓐᓄᑦ ᓄᓇᕗᑦ ᐊᒻᒪ ᑲᓇᑕᒥᐆᑦ.
        ᓄᓇᕗᑦ ᐊᖏᖃᑎᒌᒍᑖ, ᐊᒻᒪ
        ᑭᕙᓪᓕᕐᒥ ᐃᓄᐃᑦ ᐊᔪᙱᓐᓂᖏᑦ ᒥᑭᓂᖅᐹᒥᒃ ᐊᒃᑐᖅᑕᐅᖁᑉᓗᒍ ᐊᕙᑎᖓᑦ
      ᑭᕙᓪᓕᕐᒥ ᐃᓄᐃᑦ ᑲᑐᔾᔨᖃᑎᒌᑯᖏᑦ ᐱᓕᕆᔨᑖᓚᐅᖅᐳᑦ ᕼᐊᑦᑎᓐᓱᓐ ᐊᕙᑎᓕᕆᔨᒃᑯᑦ ᐊᒻᒪ ᒌᐆ ᕕᒃᑐ ᐊᐅᓚᑦᑎᔩᑦ ᑯᓐᓂᒃ ᐃᑲᔪᖁᑉᓗᒋᑦ ᕿᒥᕐᕈᓂᕐᒥᒃ ᓚᐃᓴᑖᕋᓱᒍᑎᒥᒃ.

## Slide 6: Unresolved Issues
ᐃᓱᒫᓗᑏᑦ ᐱᐋᓂᒃᓯᒪᖏᑦᑐᑦ

## Slide 7: KIA-WL-05: Saline Groundwater Inflows KIA-WL-05: ᑕᕆᐅᖃᖅᑐᑦ ᒪᓂᖅᑲᒥ ᐃᒪᐃᑦ ᐃᓗᒻᒧᑦ ᑰᖕᓂᖏᑦ
Issue
Saline groundwater is projected to flow into the underground works
The Water Management Plan does not provide full details for long term saline water management and disposal
Saline discharges may cause negative impacts to the receiving environment
ᐃᓱᒫᓘᑦ
ᑕᕆᐅᓖᑦ ᐃᒪᐃᑦ ᓄᓇᒥᑦ ᑰᖕᓂᐊᕋᓱᒋᔭᐅᕗᑦ ᓄᓇᐅᑉ ᐃᓗᐋᓄᑦ
ᐃᒪᕐᒥᒃ ᐊᐅᓚᑦᑎᓂᐊᕐᓃᑦ ᐸᕐᓇᒃᓯᒪᔾᔪᑎᖏᑦ ᓇᓗᓇᐃᕆᓯᒫᓂᖏᑐᑦ ᖃᓄᖅ ᐃᒃᐲᒡᓇᕐᓂᖃᕈᒫᕐᒪᖔᑦ ᐅᑭᐅᑦ ᐊᒥᓱᑦ ᓈᒃᐸᑕ ᖃᓄᐃᓐᓂᐊᕐᒪᖔᑦ ᐊᒻᒪ ᖃᓄᖅ ᐊᒃᑐᖅᑕᐅᓂᐊᕐᒪᖓᑦ.
ᑕᕆᐅᖃᕐᓃᑦ ᐊᓂᐋᕙᓪᓕᐋᔪᑦ ᐊᕙᑎᒧᑦ ᐱᐅᖏᓐᓂᖃᑐᐃᓐᓇᕆᐊᓖᑦ.

## Slide 8: KIA-WL-05: Saline Groundwater InflowsI KIA-WL-05: ᑕᕆᖃᖅᑐᑦ ᒪᓂᖅᑲᒥ ᐃᒪᐃᑦ ᐃᓗᒻᒧᑦ ᑰᖕᓂᖏᑦ
We recommend that the NWB include a condition in the licence that requires submission of a long-term saline groundwater management plan for approval by the NWB 6 months prior to any planned discharge
AEM is working with Environment Canada to resolve regulatory challenges posed by saline discharges to the marine environment
Environment Canada should commit to provide specific guidance to AEM to regulate discharges within the project timeline
ᑐᒃᓯᕋᐅᑦ
ᑐᒃᓯᕋᖅᐳᒍᑦ NWB (ᐃᒪᓕᕆᔩᑦ) ᐃᓗᓕᖃᖁᑉᓗᒍ ᓚᐃᓴᑖᕈᑎᒥ ᑕᑯᔪᒪᓗᑎᒃ ᐊᑯᓂ ᑕᕆᐅᓖᑦ ᖃᓄᖅ ᐃᒃᐱᖕᓇᕐᓂᖃᕐᓂᐊᕐᒪᖔᑖ ᐊᐅᓚᑦᑎᔾᔪᓂᒥᒃ ᓈᒻᒪᒋᔭᐅᔭᕆᐊᖃᖅᑐᒥᒃ NWB kunnut6 ᑕᖅᑮᑦ ᐱᒋᐊᓚᐅᖅᑎᓐᓇᒋᑦ ᑯᕕᓂᐊᖅᑎᓪᓗᒋᑦ ᑕᕆᐆᓕᖕᓂᒃ ᐃᒪᕐᓂᒃ.
AEM ᐱᓕᕆᖃᑎᖃᖅᑐᑦ ᑲᓇᑕᒥ ᐊᕙᑎᓕᕆᔨᒃᑯᓐᓂᒃ ᐊᖅᑭᒃᓯᓇᓱᒃᖢᑎᒃ ᒪᓕᒐᕐᓂᒃ ᐃᖢᐊᖏᓕᐆᕈᑕᐅᔪᓂᒃ ᑕᕆᐅᖃᖅᑐᓂᒃ ᑯᕕᓯᓂᐅᑉ ᒥᒃᓵᓄᑦ ᐃᒃᐱᖕᓇᕐᓂᖃᕈᓐᓇᕐᓂᖏᓐᓂᒃ ᐃᒪᕐᒥᐅᑕᓄᑦ.
ᐊᕙᑎᓕᕆᔨᒃᑯᑦ ᑲᓇᑕᒥ ᒪᓕᒐᒃᓴᓂᒃ ᓴᖅᑭᑦᑎᔭᕆᐊᖃᕋᔭᕐᒪᑕ AEM ᑯᓐᓄᑦ ᐊᐅᓚᑦᑐᓐᓇᕐᓂᐊᕐᓗᒋᑦ ᑯᕕᓯᖃᑦᑕᕐᓂᐅᓂᐊᖅᑐᑦ ᓈᒪᓇᖅᓯᒪᓗᒋᑦ
Request

## Slide 9: KIA-WL-06: Site-Specific Water Quality Objective Derivation KIA-WL-06: ᐱᓕᕆᕝᕕᐅᔪᒧᑦ ᑐᕌᖅᑐᑦ ᐃᒪᖃᑦᑎᐊᕐᓂᐅᑉ ᓴᖅᑭᓐᓂᖏᑦ
Issue
Site Specific Water Quality Objectives were developed for aluminum, fluoride, and iron for the Meliadine site
  No methodology was provided in the original submission
Arsenic concentrations in Collection Pond 4 could slightly exceed the site-specific water quality objective post-closure
Rainbow trout bioassay was conducted with aged waste rock rather than fresh
ᐱᓕᕆᕝᕕᖕᓂ ᑐᕌᖅᑐᑦ ᐃᒪᐃᑦ ᖃᓄᐃᑦᑐᓂᐊᕐᓂᖏᑦ ᐋᖅᑭᒃᑕᐅᓚᐅᖅᑐᑦ ᓴᕕᒃᓴᓄᑦ ᐊᕿᑦᑐᓄᑦ, ᑭᓂᖅᑐᓄᑦ, ᐊᒻᒪ ᓴᕕᒃᔅᓐᓄᑦ ᑕᓯᕐᔪᐊᕐᒥ.
  ᖃᓄᖅ ᐱᓕᕆᐊᖑᓂᐊᕐᒪᖔᑖ ᐱᑕᖃᓚᐅᖏᑦᑐᖅ ᓯᕗᓪᓕᕐᒥ ᓴᖅᑭᑕᐅᔪᒥ
ᓴᕕᒃᓴᖅᑕᓖᑦ ᐅᓗᕆᐊᓇᖅᑐᓂᒃ ᑲᑎᖅᓱᖅᑕᐅᕕᖕᓂ ᑕᓯᕋᕐᒥ naasautilik4 ᒥᒃ ᖄᖏᐅᑎᓯᒫᕐᔪᒍᓐᓇᖅᑐᑦ ᐃᒪᐅᑉ ᓇᓗᓇᐃᒃᑯᑕᕆᔭᕆᐊᖃᖅᑕᖏᓐᓂᑯᒃᑯᐊᓚᐅᖅᑎᓪᓗᒍ.
ᐃᖢᕋᐃᑦ ᖃᐅᔨᓴᖅᑕᐅᓚᐅᖅᑐᑦ ᐅᔭᕋᒃᑕᖅᑕᐅᓯᒪᓂᑯᓂᒃ ᐊᑐᖅᖢᑎᒃ ᓄᑖᓅᖏᑦᑐᖅ
ᐃᓱᒫᓗᑦ

## Slide 10: KIA-WL-06: Site-Specific Water Quality Objective Derivation KIA-WL-06: ᐱᓕᕆᕝᕕᐅᔪᒧᑦ ᑐᕌᖅᑐᑦ ᐃᒪᖃᑦᑎᐊᕐᓂᐅᑉ ᓴᖅᑭᓐᓂᖏᑦ
AEM has provided the relevant information to satisfy our concerns regarding SSWQO derivation
We are satisfied with the SSWQOs for construction and operation as all waste streams are collected in CP1 and effluent quality regulated
NWB include a condition in the licence that current SWQOs not apply for the life of the mine
  The SSWQOs for closure should be revisited using operational data
AEM ᑯᑦ ᐅᕙᑉᑎᓐᓄᑦ ᑐᓂᓯᓚᐅᖅᑐᑦ ᓈᒻᒪᒃᑐᓂᒃ ᐃᓱᒫᓗᑕᐅᓚᐅᖅᑑᑉ ᒥᒃᓵᓄᑦ ᐃᒪᐅᑉ ᒥᒃᓵᓄᑦ ᐱᓕᕆᕝᕕᖕᓂ
ᓈᒻᒪᒋᔭᕗᑦ ᐃᒪᐃᑦ ᒥᒃᓵᓄᑦ ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ ᓴᓇᓕᖅᐸᑕ ᐊᒻᒪ ᐊᐅᓪᓛᖅᑎᑦᑎᓕᖅᐸᑕ. ᑕᒪᕐᒥᒃ ᐃᒪᐃᑦ ᑰᒐᓛᖏᑦ ᑲᑎᑕᐅᓂᐊᕐᒪᑕ CP1 ᒥ ᐊᒻᒪ ᓴᓗᒪᓂᖏᑦ ᖃᐅᔨᓴᖅᑕᐅᖏᓐᓇᕐᓂᐊᖅᖢᑎᒃ
NWB ᑯᑦ ᐃᓗᓕᖃᖅᑎᑦᑎᓗᑎᒃ ᓚᐃᓴᒥ ᑖᑉᑯᐊ ᒪᓐᓇ ᐃᒪᕐᑐᕐᓂᐅᓂᐊᖅᑐᑦ ᐊᑐᕐᓂᐊᖏᓪᓗᒋᑦ ᐊᐅᓪᓛᕐᓂᓗᒃᑖᖓᓄᑦ ᐅᔭᕋᒃᑕᕆᐊᑉ
  ᑐᒃᓯᕋᐅᑏᑦ ᐅᒃᑯᐊᖅᑕᐅᓂᕆᔪᒫᖅᑕᖓᓄᑦ ᕿᒥᕐᕈᔭᐅᒃᑲᓐᓂᕋᔭᕐᒪᑕ ᐊᑐᕐᓗᑎᒃ ᐊᐅᓪᓚᕐᓂᖓᑦ ᒥᒃᓵᓄᑦ ᐊᑐᕐᓂᑯᓂᒃ
Request
ᑐᒃᓯᕋᐅᑦ

## Slide 11: KIA-WL-07: Mixing Zone Water Quality Monitoring KIA-WL-07: ᐊᑯᑦᑕᐅᕙᓪᓕᐊᔪᑦ ᐃᒪᐃᑦ ᐱᐅᓂᖓᑕ ᖃᐅᔨᓴᖅᑕᐅᓂᖏᑦ
Issue
AEM has proposed 5 sites in the near field exposure area near the diffuser
One site (MEL_03) is proposed to monitor effluent from the diffuser
Wind, flow and other mixing zone dynamics limit the capacity of a single monitoring station to appropriately characterize the mixing zone and assimilative capacity of Meliadine Lake
A minimum of three sites around the discharge point are recommended to assess the capacity of the mixing zone to assimilate the effluent and verify predictions of mixing zone size under all ambient conditions.
ᐃᓱᒫᓘᑦ
AEM ᑯᑦ 5ᓂᒃ ᓇᓗᓇᐃᕆᓯᒪᔪᑦ ᓯᓚᒥ ᖃᓂᒋᔮᓂ ᓴᓗᒻᒪᖅᓴᐃᕝᕕᐅᑉ
ᐊᑕᐅᓯᖅ (MEL_03) ᖃᐅᔨᓴᕐᕕᐅᖁᔭᐅᔪᖅ ᓴᓗᒻᒪᖅᓴᐃᕝᕕᖕᒥ ᐊᓂᐋᕙᓪᓕᐊᔪᓂᒃ
ᐊᓄᕆ, ᑰᖕᓃᑦ ᐊᒻᒪ ᐊᓯᖏᑦ ᐊᑯᑦᑎᕕᐅᑉ ᒥᒃᓵᓄᑦ ᐊᔪᕐᓇᕈᑕᐅᕙᖕᒪᑕ ᐊᑕᐅᓯᕐᒥᒃ ᖃᐅᔨᓴᕐᕕᖃᕐᓂᕐᒥᒃ ᖃᐅᔨᒪᓇᓱᒡᓗᒍ ᐊᑯᑕᐅᕙᓪᓕᐊᔪᑦ ᒥᒃᓵᓄᑦ ᑕᓯᕐᔪᐊᕐᒥ
ᒥᑭᓂᖅᐹᒥᒃ ᐱᖓᓱᓂᒃ ᖃᐅᔨᓴᕐᕕᖕᓂᒃ ᐱᑕᖃᖁᔭᐅᕗᖅ ᖃᐅᔨᓴᑦᑎᐊᕈᓐᓇᖁᑉᓗᒍ ᓈᒻᒪᒃᑲᓗᐊᕐᒪᖓᑦ ᐊᑯᑕᐅᕙᓪᓕᐊᔪᖅ ᐊᓂᐋᕙᓪᓕᐊᔪᕐᓗ ᐊᒻᒪ ᖃᐅᔨᒪᓇᓱᒡᓂᐊᕐᓗᓂ ᑕᓯᕋᖅ ᐊᑯᑦᑎᕕᐅᔪᖅ ᓈᒻᒪᒃᑲᓗᐊᕐᒪᖔᑦ ᓱᓇᓗᒃᑖᑦ ᑕᐅᑐᒃᖢᒋᑦ.

## Slide 12: KIA-WL-07: Mixing Zone Water Quality Monitoring KIA-WL-07: ᐊᑯᑦᑕᐅᕙᓪᓕᐊᔪᑦ ᐃᒪᐃᑦ ᐱᐅᓂᖓᑕ ᖃᐅᔨᓴᖅᑕᐅᓂᖏᑦ
We request that AEM increase the total number of AEMP sites in the near-field exposure area from 5 as indicated in AEMP to a total of 7 with three around the diffuser
AEM commit to include 3 sites to triangulate the predicted mixing zone boundary 100m from the diffuser
  i.e. sites at 120o, 240o and 360o, 100m from the center of the diffuser
  Samples should be collected from the highest point of conductivity as determined by a water column profile
ᑐᒃᓯᕋᖅᐳᒍᑦ AEM ᑯᑦ ᐊᒥᓱᖑᕆᐊᖁᑉᓗᒋᑦ AEMP ᖑᔪᑦ 5 ᓂᑦ, 7 ᓄᑦ, ᐱᖓᓱᑦ ᐃᕐᕈᖅᑐᐃᕝᕕᐅᑉ ᖃᓂᒋᔮᓂᖁᑉᓗᑎᒍᑦ.
AEM ᐱᓂᐊᕐᓂᖃᖁᕙᕗᑦ 3 ᐊᕙᓗᓯᒪᖁᑉᓗᒋᑦ ᐊᑯᑦᑎᕕᐆᓂᐊᖅᑐᒥᒃ 100 ᒦᑕᒥᒃ ᐅᖓᓯᖕᓂᖃᕐᓗᒋᑦ ᐃᕐᕈᖅᑐᐃᕝᕕᖕᒥᒃ.
  ᓲᕐᓗ ᐊᑕᐅᓯᖅ 120, 240, ᐊᒻᒪ 360, ᒦᓪᓗᑎᒃ 100 ᒦᑕᒥᒃ ᐅᖓᓯᖕᓂᖃᕐᓗᑎᒃ ᑕᓯᕋᐅᑉ ᐃᕐᕈᖅᑐᐃᕝᕕᐅᓂᐊᖅᑑᑉ ᕿᑎᖓᓐᓂᑦ.
  ᖃᐅᔨᓴᐅᑏᑦ ᑲᑎᑕᐅᖃᑦᑕᕐᓗᑎᒃ ᖁᑦᑎᖕᓂᖅᐹᖓᓂᑦ ᐃᒪᖃᕐᓂᐅᑉ
Request
ᑐᒃᓯᕋᐅᑦ
Notes: NOTE: The initial plume delineation study is not enough. Intent of the samples is to test the EA predictions and the delineation of the plume. MMER is requirements are to test if the effluent is toxic

## Slide 13: KIA-WL-07 Continued Site Locations
MEL_03
MEL_XX

## Slide 14: KIA-WL-08: Sample Locations at Rankin Inlet KIA-WL-08: ᖃᐅᔨᒋᐊᕐᓃᑦ ᑲᖏᖅᖠᓂᕐᒥ
Issue
Shipping and potential associated accidents may change water quality near the Itivia Harbour
AEM has not included sample locations at Itivia Harbour in the application
ᐃᓱᒫᓘᑦ
ᐅᒥᐊᕐᔪᐊᒃᑯᑦ ᐊᒡᔭᕐᑐᐃᓂᖅ ᐊᒻᒪ ᐱᕐᕈᓗᐊᕿᓂᖅ ᐊᓯᔾᔩᔪᓐᓇᕐᒪᑦ ᐃᒪᖓᓂᒃ ᐃᑎᕚᑉ
AEM ᖃᐅᔨᓴᕐᓂᕐᓂᒃ ᑎᕕᓂᐊᓂᑦ ᐃᓚᐅᑎᑦᑎᓚᐅᖏᓚᑦ ᑐᒃᓯᕋᐅᑎᒥᖕᓂᑦ

## Slide 15: KIA-WL-08: Sample Locations at Rankin Inlet KIA-WL-08: ᖃᐅᔨᒋᐊᕐᓃᑦ ᑲᖏᖅᖠᓂᕐᒥ
AEM should commit to include sample locations near the Itivia Harbour to track any negative impacts associated with mine related activity-particularly those related to shipping and fuel offloading
  Program should allow AEM to distinguish their activities from other users of the harbour
AEM ᑯᑦ ᐃᓚᐅᑎᑦᑎᓂᐊᕐᓂᕋᕐᓗᑎᒃ ᓇᓗᓇᐃᖅᓯᒪᓇᔭᕐᒪᑕ ᐃᑎᕕᐊᒥᑦ ᖃᐅᔨᓴᕈᓐᓇᖁᑉᓗᒋᑦ ᓈᒻᒪᖏᑦᑐᖅᑕᖃᓕᖏᒻᒪᖔᑦ ᐅᔭᕋᒃᑕᕐᓂᖅ ᐱᔾᔪᑎᒋᑉᓗᒍ ᐱᓗᐊᖅᑐᒥᒃ ᐅᒥᐊᕐᔪᐊᕐᓄᑦ ᐊᒻᒪ ᓂᐅᕋᐃᓂᖅ ᐅᖅᓱᐋᓗᖕᓂᒃ
  ᓇᓗᓇᐃᖅᓯᒪᓇᔭᕐᒪᑦ AEM ᐱᓕᕆᐊᖏᑦ ᐊᒻᒪ ᐊᔾᔨᒌᖏᓐᓂᖏᑦ ᐊᓯᖏᓐᓄᑦ ᐊᑐᖅᑕᐅᓂᖅ ᐃᑎᕕᐊᑉ ᑲᖏᖅᖢᐊ
Request
ᑐᒃᓯᕋᐅᑎᑦ

## Slide 16: KIA-WL-10: Quality Control Responses KIA-WL-10: ᓈᒻᒪᒃᑲᓗᐊᕐᒪᖔᑕ ᐱᓕᕆᐊᖑᔪᑦ ᖃᐅᔨᓴᕐᓂᖏᓐᓄᑦ ᑭᐅᔭᐅᔪᑏᑦ
Issue
AEM has not provided a response framework for duplicate samples with medium and low analytical precision
We are concerned low quality data will be incorporated into the assessment of mine related impacts
This may reduce the capacity for the Aquatic Environment Monitoring Program to identify and mitigate impacts to the receiving environment
ᐃᓱᒫᓗᑦ
AEM ᑯᑦ ᑐᓂᓯᓚᐅᖏᑦᑐᑦ ᖃᓄᐃᓐᓂᐊᕐᒪᖔᕐᒦᒃ ᒪᕐᕈᓕᖓᔪᓂᒃ ᖃᐅᔨᓴᕐᓂᕐᓂᒃ ᐊᑯᓪᓕᖅᐹᖑᔪᓂᒃ ᐊᒻᒪ ᐊᑦᑎᖕᓂᖅᐹᖑᔪᓂᒃ ᓇᓗᓇᐃᒃᑯᑕᓕᖕᓂᒃ.
ᐃᓱᒫᓗᑎᖃᖅᐳᒍᑦ ᓴᖅᑭᑦᑐᖃᕋᔭᕐᓂᖏᓐᓂᒃ ᒥᑭᓂᖅᐹᒥᒃ ᑐᒃᓯᕋᐅᑎᓂᒃ ᐊᑐᕋᓱᒍᓐᓇᕐᓂᖏᓐᓂᒃ ᕿᒥᕐᕈᓕᕌᖓᑕ ᐅᔭᕋᒃᑕᕆᐊᑉ ᐊᒃᑐᖅᑕᖏᓐᓂᒃ ᐃᖢᐊᖏᓕᐆᕈᑕᐅᔪᓂᒃ
ᑖᒻᓇ ᒥᒃᖦᓕᑎᑦᑎᔪᓐᓇᕐᒪᑦ ᐱᓕᕆᐊᒍᔪᓐᓇᖅᑐᓂᒃ ᐃᒪᕐᒥᐅᑕᓄᑦ ᐊᕙᑎᖏᓐᓂᒃ ᖃᐅᔨᓴᕈᓐᓇᕐᓂᕐᒥᒃ ᓇᓗᓇᐃᕆᓗᓂ ᐃᒃᐱᖕᓇᕐᓂᕆᔭᖏᓐᓂᒃ ᐊᕙᑎᖏᓐᓄᑦ ᐊᒃᑐᐋᔪᓂᒃ

## Slide 17: KIA-WL-10: Quality Control Responses KIA-WL-10: ᓈᒻᒪᒃᑲᓗᐊᕐᒪᖔᑕ ᐱᓕᕆᐊᖑᔪᑦ ᖃᐅᔨᓴᕐᓂᖏᓐᓄᑦ ᑭᐅᔭᐅᔪᑏᑦ
Duplicate samples are collected to help detect problems.
they are “…used to estimate sampling and laboratory analysis precision.” (US EPA)
AEM must provide a response framework for low and medium precision data
  Validation of sample collection techniques and precision,
  Validation of analytical precision, and
  Whether all samples from the suspect field event or those collected from a given field team be excluded from the dataset
AEM has indicated they have updated their response to be presented during the technical hearings
ᒪᕐᕈᓕᖓᓗᒋᑦ ᖃᐅᔨᓴᕈᑏᑦ ᑲᑎᑕᐅᕙᒃᑐᑦ ᓴᖅᑭᑦᑎᔪᓐᓇᖁᑉᓗᒋᑦ ᓈᒻᒪᖏᑦᑐᓂᒃ.
ᐊᑐᖅᑕᐅᓂᐊᖅᑐᑦ”… ᐊᑐᖅᑐᑦ ᒥᒃᓯᖃᕈᓐᓇᖁᑉᓗᒋᑦ ᖃᐅᔨᓴᕐᓂᕐᓄᑦ ᖃᓂᖅᑯᑦᑎᔪᓐᓇᖁᑉᓗᒋᑦ.”
AEM ᓴᖅᑭᑦᑎᔭᕆᐊᖃᖅᐳᑦ ᑭᐅᔾᔪᑎᒥᒃ ᐱᓕᕆᐊᖑᓂᐊᖅᑐᓂᒃ ᒥᑭᓂᖅᐹᖓᓄᑦ ᐊᒻᒪ ᐊᑯᓪᓕᖅᐹᖓᓄᑦ ᖃᐅᔨᓴᕐᓂᕐᓂᒃ
  ᓱᓕᓂᖏᑦ ᖃᐅᔨᓴᕐᓃᑦ ᑲᑎᑕᐅᓂᖏᑦ ᐊᒻᒪ ᖃᓄᖅ ᑲᑎᑦᑎᕙᖕᒪᖔᑖ
  ᓱᓕᓂᖏᑦ ᖃᐅᔨᓴᕐᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ, ᐊᒻᒪ
  ᑕᒪᕐᒥᒃ ᑲᑎᑕᐅᔪᑦ ᖃᐅᔨᓴᕐᓃᑦ ᐃᓕᒪᒋᔭᐅᔪᒥᑦ ᐊᓯᖏᓐᓂᓪᓗᓐᓃᑦ ᐃᓚᐅᖏᒃᑲᓗᐊᕐᒪᖓᑖ ᕿᒥᕐᕈᓂᐅᓚᐅᖅᑐᓂᑦ
AEM ᐅᖃᖅᓯᒪᔪᑦ ᓄᑕᐅᓯᒋᐊᖅᓯᒪᓂᕋᖅᖢᒍ ᑭᐅᔾᔪᑎᑎᒃ ᐊᒻᒪ ᓴᖅᑭᓐᓂᐊᕐᓂᕋᖅᖢᒍ ᑐᓴᕋᓱᖕᓂᐅᓂᐊᖅᑐᒥ
Request
ᑐᒃᓯᕋᐅᑦ

## Slide 18: KIA-WL-21: Landfarm Microbial Degradation Rates KIA-WL-21: ᓄᓇᐊᒥ ᐱᕈᖅᑐᑦ ᖁᐱᕐᕈᐃᑦ ᓱᕈᖅᐸᓪᓕᐊᓂᖏᑦ
Issue
We are concerned with the biodegradation rates expected at AEM’s proposed landfarm
  Landfarms will be relied on to treat contaminants such as oils and grease in soil
  AEM provided reference to Meadowbank and results from Resolution Island
    The area surrounding Resolution Island is dominated by a marine environment and may not be applicable
Overarching concern is preventing residual effects at the landfarm
ᐃᓱᒫᓗᑦ
ᐃᓱᒫᓗᑎᖃᕋᑉᑕ ᖁᐱᕐᕈᐃᑦ ᓱᕈᖅᐸᓪᓕᐊᓂᐊᕐᓂᖏᓐᓂᒃ AEMkut ᓄᐊᒧᑦ ᓈᕕᑦᑕᕐᕕᒋᓂᐊᖅᑕᖓᑕ ᒥᒃᓵᓄᑦ.
  ᓄᓇᐃᑦ ᐊᑐᖅᑕᐅᓂᐊᕐᒪᑕ ᓱᕈᔪᖃᖅᑐᓂᒃ ᐅᖅᓱᐋᓗᖃᖅᑐᓂᒃᓗ ᓴᓗᒻᒪᕐᕕᐅᖃᑦᑕᕐᓂᐊᕐᓗᑎᒃ
AEMkut ᓴᖅᑭᑦᑎᓚᐅᖅᑐᑦ ᐊᐳᖅᑎᓐᓈᖅᑐᒥ ᐱᓕᕆᐊᓂᒃ ᐊᒻᒪ ᕋᓴᓗᑎᐊᓐ ᕿᑭᖅᑕᖓᓂᑦ
  ᕿᑭᖅᑕᒥᑦ ᓴᖅᑭᑕᖅ ᐃᒪᕐᒥᐅᑕᓄᑦ ᐊᕙᓗᔭᐅᓯᒪᖕᒪᑦ ᐊᑑᑎᖃᕋᔭᖅᑰᖏᑦᑐᖅ ᐅᕙᑉᑎᓐᓄᑦ
ᐃᓱᒫᓗᑎᒻᒪᕆᐅᔪᖅ ᓈᒻᒪᖏᑦᑐᓂᒃ ᐃᒃᐱᖕᓇᕐᓂᖃᖁᔨᖏᓐᓐᖅ ᓄᓇᒥ
Notes: Biodegradation rates can be improved by amending soil conditions at the landfarm (eg modification of pH, salinity, nutrients, etc) to

## Slide 19: KIA-WL-21: Landfarm Microbial Degradation Rates KIA-WL-21: ᓄᓇᐊᒥ ᐱᕈᖅᑐᑦ ᖁᐱᕐᕈᐃᑦ ᓱᕈᖅᐸᓪᓕᐊᓂᖏᑦ
AEM intends to provide a discussion during the technical hearings on:
  Applicability of data from Resolution Island
  Biodegradation rates experienced at Meadowbank
  Practices which may improve biodegradation rates at Meliadine
AEM ᐅᖃᐅᓯᖃᕈᒪᔪᖅ ᑐᓴᕋᓱᓕᖅᐸᑕ ᑕᒪᑐᒪ ᒥᒃᓵᓄᑦ ᐅᑯᐊ ᐱᔾᔪᑎᒋᑉᓗᒋᑦ:
  ᖃᓄᖅ ᕋᓴᓗᑎᐊ ᕿᑭᖅᑕᖓᓂ ᐃᒃᐱᖕᓇᕐᓂᖃᕐᓂᐊᖅᐸ
  ᖁᐱᕐᕈᐃᑦ ᓱᕈᖅᐸᓪᓕᐊᓂᖏᑦ ᖃᓄᐃᑉᐸᑦ ᐊᐳᖅᑎᓐᓈᖅᑐᒥ
  ᐊᑐᖅᑕᐅᔪᓐᓇᖅᑐᑦ ᑕᓯᕐᔪᐊᕐᒥ ᖁᐱᕐᕈᐃᑦ ᐱᕙᓪᓕᕈᓐᓇᖁᑉᓗᒋᑦ
Request
ᑐᒃᓯᕋᐅᑦ

## Slide 20: Resolved Issues
ᐊᖏᖃᑎᒌᒍᑕᐅᓚᐅᖅᑐᑦ ᐃᓱᒫᓗᑎᕕᓃᑦ

## Slide 21: KIA-WL-01: Segregation of Overburden KIA-WL-01: ᓴᓂᕐᕙᖅᑕᐅᓂᖏᑦ ᓄᓇᐃᑦ ᖄᖏᑦ ᐊᑐᖏᑦᑐᑦ
Issue
AEM intends to store “about 0.1 Mt” in the temporary stockpile for use “as TSF closure cover material”.
We are concerned that segregated overburden is only intended for use as part of the TSF closure strategy
  Overburden is a source of native plant material that can also be used in the closure of roads, pads and other site infrastructure
ᐃᓱᒫᓗᑦ
AEM ᓴᓂᕐᕙᖅᓯᔪᒪᖕᒪᑕ ᐃᒻᒪᖄ 0.1 Mt ᒥᒃ ᑲᑎᑦᑎᕕᐅᓂᐊᖅᑐᒥ ᐊᑐᕈᒫᕐᓗᒍ ᐅᒃᑯᐊᕆᐊᖅᐸᑦ ᐅᔭᕋᒃᑕᕆᐊᖅ.
ᐃᓱᒫᓗᑎᖃᖅᐳᒍᑦ ᓴᓂᕐᕙᖅᓯᒪᔪᖅ ᓯᐅᕋᖅᑕᕐᓂᑯ ᐊᑐᖅᑕᐅᑐᐃᓐᓇᕐᓂᐊᕐᓂᖓᓄᑦ ᐃᓚᖓ ᒪᑐᒋᐋᓕᕐᓂᖅᐸᑦ ᑭᓯᐋᓂ ᐅᔭᕋᒃᑕᕆᐊᖅ
  ᑕᒪᓐᓇ ᐱᕈᖅᑐᖃᖅᑐᕕᓂᖅ ᓯᐅᕋᖅᑕᕐᓂᑯ ᓄᓇᒥᒃ ᐃᓗᓕᖃᕐᒪᑦ ᐊᒻᒪ ᐊᑐᖅᑕᐅᔪᓐᓇᖅᖢᓂ ᐅᒃᑯᐊᖅᓯᓂᕐᒧᑦ ᐊᑉᖁᑎᓂᒃ, ᐱᖁᑎᖃᕐᕕᕕᓂᕐᓂᒃ ᐊᒻᒪ ᐊᓯᖏᓐᓄᑦ

## Slide 22: KIA-WL-01: Segregation of Overburden KIA-WL-01: ᓴᓂᕐᕙᖅᑕᐅᓂᖏᑦ ᓄᓇᐃᑦ ᖄᖏᑦ ᐊᑐᖏᑦᑐᑦ
AEM commits to:
Minimize the loss of overburden wherever possible to allow for its use as closure material
Investigate storage options for segregated overburden
Include a section in the next iteration of the closure and reclamation plan indicating other uses for overburden at closure in addition to capping the TSF
Investigate:
  Whether the 0.1 Mt of overburden is sufficient to cap the TSF and support the closure of other site infrastructure
ᐊᖅᑭᒍᑖ
AEM ᐱᓂᐊᕐᓂᖃᖅᐳᖅ:
ᒥᑭᓂᖅᐹᒥᒃ ᐊᓯᐅᔨᓂᖃᖁᑉᓗᒍ ᐃᑉᔪᖃᕐᓂᐅᔪᓂᒃ ᐱᕈᖅᑐᖃᕈᓐᓇᕐᓂᕐᓂᒃ ᐊᑐᕈᓐᓇᕈᒫᕐᓗᒋᑦ ᐅᒃᑯᐊᕆᐊᖅᐸᑦ ᐅᔭᕋᒃᑕᕐᕕᒃ
ᕿᓂᕐᓂᖅ ᖃᓄᖅ ᑐᖂᒪᑎᐊᕋᔭᕐᒪᖔᑦ ᐊᑐᖏᓐᓂᖓᓐᓂ ᓄᓇ
ᐃᓗᓕᖃᕐᓗᒍ ᑭᖑᓪᓕᕐᒥ ᐅᖃᐅᓯᖃᓕᕈᑉᑕ ᐅᒃᑯᐊᕐᓂᕆᔪᒫᖅᑕᖕᓂᒃ ᐊᒻᒪ ᓄᓇᐅᑉ ᐅᑎᖅᑎᑕᐅᓂᕆᔪᒫᖅᑕᖓᓂᒃ ᖃᓄᐃᓕᐅᕐᓂᕆᔪᒫᖅᑕᖓᓂᒃ ᖃᓄᖅ ᐊᑐᖅᑕᐅᔪᒫᕐᒪᖔᑖ ᖄᓕᖅᑐᖅᑕᐅᓕᖅᐸᑦ ᐅᔭᕋᒃᑕᕐᕕᕕᓂᖅ ᐊᓯᖏᓐᓄᓪᓗ ᐊᑑᑎᒃᓴᐃᑦ
ᖃᐅᔨᓴᕐᓂᖅ:
  ᑖᒻᓇ 0.1ᒻᑦ ᖄᕕᓂᖓ ᓄᓇᐅᑉ ᓈᒻᒪᖕᓂᐊᕋᓗᐊᕐᒪᖔᑦ ᐊᑐᖅᑕᐅᓕᖅᐸᑦ ᒪᑐᓕᖅᑎᓪᓗᒍ ᐅᔭᕋᒃᑕᕆᐊᖃᕐᕕᒃ
Resolution

## Slide 23: KIA-WL-02: Additional Cover Material and Re-vegetation KIA-WL-02: ᓄᓇᒥ ᐱᕈᖅᑐᑦ ᓄᓇᐃᑦ ᐱᕈᖅᑐᓪᓗ ᒥᒃᓵᓄᑦ
Issue
We expressed concern with the timeline required for revegetation of the site after disturbance
AEM provided estimates with relevant case studies
ᐃᓱᒫᓗᑦ
ᐃᓱᒫᓗᑎᖃᓚᐅᕋᑉᑕ ᐊᑯᓂᐅᓂᕆᓂᐊᖅᑕᖓᓂᒃ ᓄᓇᒥ ᐱᕈᖅᑐᑦ ᒥᒃᓵᓄᑦ ᐊᒃᑐᖅᑕᐅᓚᐅᖅᑎᓪᓗᒋᑦ
AEM ᓴᖅᑭᑦᑎᓚᐅᖅᐳᑦ ᖃᓂᖅᑯᑦᑎᔪᓂᒃ ᐱᕈᒃᑲᓐᓂᕋᔭᕐᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᓯᒪᓂᑯᓂᒃ
Notes: Specific concerns on a) grasses, b) woody shrubs and c) lichens

## Slide 24: KIA-WL-02: Additional Cover Material and Re-vegetation KIA-WL-02: ᓄᓇᒥ ᐱᕈᖅᑐᑦ ᓄᓇᐃᑦ ᐱᕈᖅᑐᓪᓗ ᒥᒃᓵᓄᑦ
AEM has committed to generate site specific revegetation information through targeted studies
AEM is clarifying the feasibility of lichens recolonizing the disturbed areas based on the best available scientific understanding at this time
  AEM is working with the University of Saskatoon to provide site specific revegetation data
AEM ᓴᖅᑭᑦᑎᓂᐊᕐᓂᕋᖅᑐᑦ ᐱᕈᖅᑐᖃᕐᓂᐅᑉ ᒥᒃᓵᓄᑦ ᑐᕌᖅᑐᓂᒃ ᐱᓕᕆᕝᕕᖕᒥ ᖃᐅᔨᓴᕐᓂᒃᑯᑦ
AEM ᓇᓗᓇᐃᕆᕙᓪᓕᐊᔪᑦ ᑎᖓᐅᔭᐃᑦ ᐱᕈᖅᐸᓪᓕᐊᔪᓐᓇᕐᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ ᐊᐅᓚᔾᔭᒃᑕᐅᓯᒪᓂᑯᑦ ᓄᓇᐃᑦ ᒥᒃᓵᓄᑦ ᕿᒥᕐᕈᑉᓗᑎᒃ ᑕᒪᑐᒪ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᓯᒪᓂᑯᓂᒃ
AEM ᐱᓕᕆᖃᑎᖃᖅᑐᖅ ᓴᔅᑲᑑᓐ ᓯᓚᑦᑐᖅᓴᕐᕕᖓᓂᒃ ᓄᓐᒥ ᐱᕈᖅᑐᑦ ᒥᒃᓵᓄᑦ
Resolution
ᐋᖅᑭᒋᐊᕈᑏᑦ

## Slide 25: KIA-WL-03: Water Balance Assumptions KIA-WL-03: ᐃᒪᐅᑉ ᐊᐅᓚᓂᖓᑕ ᒥᒃᓵᓄᑦ ᐃᓱᒪᓕᐊᑦ
Issue
AEM had only presented a water balance for a mean precipitation year scenario
ᐃᓱᒫᓗᑦ
AEM ᓴᖅᑭᑦᑎᑐᐃᓐᓇᓚᐅᕐᒪᑦ ᐃᒪᖅᑐᓂᐅᑉ ᒥᒃᓴᓄᑦ ᐅᑭᐅᓗᒃᑖᒧᑦ ᑕᐅᑐᖅᑰᖅᖢᑎᒃ

## Slide 26: KIA-WL-03: Water Balance Assumptions KIA-WL-03: ᐃᒪᐅᑉ ᐊᐅᓚᓂᖓᑕ ᒥᒃᓵᓄᑦ ᐃᓱᒪᓕᐊ
AEM has provided a memo outlining two additional scenarios on October 1, 2015
  1:100 wet precipitation
  1:100 dry precipitation
This has alleviated our concerns
ᐊᖏᕈᑕᐅᓚᐅᖅᑐᖅ
  AEM ᑐᓂᓯᓚᐅᖅᑐᖅ ᑎᑎᖅᑲᒥᒃ ᓇᓗᓇᐃᕆᔪᒥᒃ ᒪᕐᕈᒃᑲᓐᓃᖕᓂᒃ ᑕᐅᑐᖅᑰᒐᒃᓴᓂᒃ ᐊᒃᑐᐸ 1,2015ᒥ
  1:100 ᖃᐅᓯᕐᓇᖅᑎᓪᓗᒍ ᒥᐊᖅᑐᓂᖅ
  1:100 ᐸᓂᕐᓇᖅᑎᓪᓗᒍ ᐃᒪᖅᑐᓂᖅ
ᑖᒻᓇ ᐃᓱᒫᓗᑎᑉᑎᓐᓂᒃ ᐊᖅᑮᓚᐅᖅᑐᖅ
Resolution

## Slide 27: KIA-WL-04: Incorporation of Inuit Qaujimajatuqangit into Monitoring Activities KIA-WL-04 ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᑦᑕ ᐊᑐᖅᑕᐅᓂᖏᑦ ᖃᐅᔨᓴᕐᓂᕐᓂ
Issue
AEM had not included information outlining how Inuit Qaujimajatuqangit has been incorporated into ongoing monitoring activities
ᐃᓱᒫᓗᑦ
AEM ᐃᓚᐅᑎᑦᑎᓚᐅᖏᒻᒪᑦ ᖃᓄᖅ ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᑦ ᐊᑐᖅᑕᐅᖕᒪᖔᑖ ᖃᐅᔨᓴᕐᓂᕐᓂ

## Slide 28: KIA-WL-04: Incorporation of Inuit Qaujimajatuqangit into Monitoring Activities KIA-WL-04 ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᑦᑕ ᐊᑐᖅᑕᐅᓂᖏᑦ ᖃᐅᔨᓴᕐᓂᕐᓂ
Through the Inuit Impact Benefit Agreement, AEM is committed to work with the KIA to develop techniques that better use Inuit Qaujimajatuqangit to monitor and report to the community
AEM has committed to:
  Embed an Inuit Qaujimajatuqangit holder with the aquatic monitoring team
  Engage with the KIA in Q3 or Q4 of 2016 to further develop Inuit Qaujimajatuqangit aquatic monitoring methods
ᐃᓄᐃᑦ ᐊᒃᑐᖅᑕᐅᓂᖏᓐᓄᑦ ᐊᖏᕈᓯᐅᖅᓯᒪᔫᑉ ᒥᒃᓵᓄᑦ, AEM ᐱᓂᐊᕐᓂᖃᖅᐳᖅ ᐱᓕᕆᖃᑎᖃᕐᓂᐊᕐᓂᕐᒥᒃ ᑮ ᐊᐄ ᐄ ᑯᓐᓂᒃ ᓴᖅᑭᑦᑎᓂᐊᕐᓂᕐᒥᒃ ᐱᐅᓂᖅᓴᒥᒃ ᐊᑐᕐᓂᕐᒥᒃ ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᓐᓂᒃ ᖃᐅᔨᓴᓕᕌᖓᑕ ᐊᒻᒪ ᑐᓴᖅᑎᑦᑎᓂᐊᕐᖢᑎᒃ ᓄᓇᓕᖕᒥᒃ
AEM ᐱᓂᐊᕐᓂᖃᖅᐳᖅ :
  ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᓐᓂᒃ ᐃᓗᓪᓕᖃᖁᑉᓗᒍ ᐃᒪᕐᒥᐅᑕᐃᑦ ᒥᒃᓵᓄᑦ ᖃᐅᔨᒪᔨᓄᑦ
  ᐱᓕᕆᖃᑎᒋᓗᒋᑦ ᑮ ᐊᐄ ᐄ ᑯᑦ Q3 ᒥ ᐅᕝᕙᓗᓐᓃᑦ Q4 ᒥ 2016 ᒥ ᐱᒋᐊᒃᑲᓐᓂᖁᑉᓗᒋᑦ ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᑦ ᐃᒪᕐᒥᐅᑕᐃᑦ ᖃᐅᔨᓴᖅᑕᐅᓂᖏᑦᑕ ᒥᒃᓵᓄᑦ
Resolution
ᐊᖏᖃᑎᒌᒍᑕᐅᓚᐅᖅ
Notes: Build aquatic monitoring capacity in the community,
Provide additional employment opportunities,
Monitor IQ assessments of the aquatic environment that
Refine station locations so they overlap with locations of specific importance to Inuit
IQ method engagement will follow with the KIA’s own work

## Slide 29: KIA-WL-09: Plume Delineation Model Assumptions KIA-WL-09 ᓄᓇᐅᑉ ᑕᐅᑦᑐᕆᔪᒫᖅᑕᖓᑕ ᑎᑎᕋᐅᔭᖅᓯᒪᔪᑦ ᐃᓱᒪᒃᓴᓕᐊᑦ
Issue
AEM had not provided full rationale for each CORMIX input used to model the effluent plume in Meliadine Lake
We were also concerned with their input for ambient temperature
  Discharges will occur in the open water season
  Inputs of ambient temperature has been calculated using data from June and July resulting in an input of 13.5oC
  The temperature does not capture the full range of potential temperatures and does not accurately estimate the density of colder, denser water
ᐃᓱᒫᓗᑦ
AEM ᐃᓗᐃᑦᑐᒥᒃ ᐅᓂᑉᑳᓕᐅᖅᓯᒪᖏᑦᑐᑦ ᖃᓄᖅ ᐊᑯᓯᒪᓂᐊᕐᒪᖓᑖ ᓄᓇᐃᑦ ᐊᑐᖅᑕᐅᔪᒫᖅᑐᑦ ᑕᓯᕐᔪᐊᕐᒥ ᐅᑎᖅᑎᖅᑕᐅᓕᖅᐸᑦ ᓄᓇᕕᓂᖓ
ᐃᓱᒫᓗᑎᖃᕆᕗᒍᑦ ᓯᓚᐅᑉ ᒥᒃᓵᓄᑦ ᐅᖃᐅᓯᖏᑦᑕ
  ᐃᒪᕐᓗᖕᓂᒃ ᑯᕕᓯᖃᑦᑕᕐᓂᐊᕐᒪᑕ ᐊᐅᔭᒃᑯᑦ
  ᓯᓚᐅᑉ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓂᖏᑦ ᐊᑐᕐᒪᑕ ᔫᓂ ᒥᒃ ᐊᒻᒪ ᔪᓚᐄ ᒥᒃ ᐅᖅᑰᓇᕐᓂᖃᕐᓂᐊᖅᖢᓂ 13.5 ᒥᒃ
  ᐅᖅᑰᓇᕐᓂᖓ ᑎᒍᓯᓯᒪᖏᒻᒪᑦ ᐊᔾᔨᒌᖏᑦᑐᓂᒃ ᓯᓚᓂᒃ ᐊᒻᒪ ᑐᖓᐅᑦᑎᓯᒪᑉᓗᓂ ᓯᓚᒥᒃ ᐃᒃᑮᕐᓇᕐᓂᖅᓴᐅᑎᓪᓗᒍ, ᐊᒻᒪ ᐃᒪᖅ ᑭᓂᕐᓂᖅᓴᐅᑎᓪᓗᒍ

## Slide 30: KIA-WL-09: Plume Delineation Model Assumptions KIA-WL-09 ᓄᓇᐅᑉ ᑕᐅᑦᑐᕆᔪᒫᖅᑕᖓᑕ ᑎᑎᕋᐅᔭᖅᓯᒪᔪᑦ ᐃᓱᒪᒃᓴᓕᐊᑦ
Resolution
AEM has:
  Provided additional model input information
  Modeled effluent dispersion using colder temperature (4oC) and found the density change had “little to no impact on the dilution factors or the conclusions”
AEM ᐃᒪᓐᓇᐃᓯᒪᕗᖅ:
  ᑕᑯᔭᒃᓴᒃᑲᓐᓂᕐᓂᒃ ᓴᖅᑭᑦᑎᓯᒪᕗᑦ
  ᐃᒪᐃᑦ ᒥᒃᓵᓄᑦ ᓴᖅᑭᑦᑎᓯᒪᒃᑲᓐᓂᖅᐳᑦ ᐊᑐᖅᖢᓂᒃ ᐃᒃᑮᕐᓇᕐᓂᖅᓴᒥᒃ ᓯᓚ 4 ᒥᒃ ᐅᖅᑰᓂᖃᖅᑎᓪᓗᒍ ᐊᒻᒪ ᑐᑭᓯᓚᐅᖅᐳᑦ ᐃᒪᐅᑉ ᑭᓂᕐᓂᐋ ᐃᒃᐱᖕᓇᕐᓂᖃᓚᐅᖏᓚᖅ ᐃᕐᕈᖅᑕᐅᓂᖓᓂᒃ ᐃᒪᕐᓘᑎᐅᑉ
ᐊᖏᖃᑎᒌᖕᓂᖅ

## Slide 31: KIA-WL-11: Significance Thresholds for Water Quality, Sediment Quality, and Fish Tissue Chemistry KIA-WL-11 ᖃᐅᔨᒋᐊᕐᓃᑦ ᑐᙵᕕᒃᓴᖏᑦ ᐃᒪᕐᒧᑦ, ᑕᓯᕋᐅᑉ ᓇᑎᐋᑕ ᒥᒃᓵᓄᑦ ᓈᒻᒪᖕᓂᖏᑦ ᐊᒻᒪ ᐃᒪᕐᒥᐅᑕᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓃᑦ
Issue
AEM has proposed three significance thresholds which do not directly address changes to water quality, quantity, flow, sediment quality or fish tissue chemistry
Thresholds do not address the loss of cultural value to Inuit
ᐃᓱᒫᓗᑦ
AEM ᐱᖓᓱᓂᒃ ᑐᙵᕕᒃᓴᓂᒃ ᖃᐅᔨᒪᓂᕐᒧᑦ ᓴᖅᑭᑦᑎᔪᒪᖕᒪᑕ ᔭᐅᔨᔾᔪᑕᐅᓇᔭᖏᑦᑐᓂᒃ ᐃᒪᐅᑉ ᐊᓯᔾᔨᕋᔭᖅᐸᑦ ᐃᒪᑦᑎᐊᕙᐅᓂᐋ, ᑰᖕᓂᖓ, ᐃᒪᒃᖠᓂᖓ, ᓇᑎᐋ ᐱᐅᔪᓐᓂᕐᐸᓪᓕᐊᓂᖓ, ᐅᕝᕙᓗᓐᓃᑦ ᐊᒥᕋᕐᓗᓕᕋᔭᕐᓂᖏᑦ ᐃᖃᓗᐃᑦ.
ᖃᐅᔨᒪᓂᖏᑦ ᐅᖃᐅᓯᖃᖏᒻᒪᑕ ᐃᓂᐅᑦ ᐃᓅᓂᖏᓐᓄᑦ ᐊᒃᑐᐋᔪᓂᒃ

## Slide 32: KIA-WL-11: Significance Thresholds for Water Quality, Sediment Quality, and Fish Tissue Chemistry KIA-WL-11 ᖃᐅᔨᒋᐊᕐᓃᑦ ᑐᙵᕕᒃᓴᖏᑦ ᐃᒪᕐᒧᑦ, ᑕᓯᕋᐅᑉ ᓇᑎᐋᑕ ᒥᒃᓵᓄᑦ ᓈᒻᒪᖕᓂᖏᑦ ᐊᒻᒪ ᐃᒪᕐᒥᐅᑕᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓃᑦ
The NWB should require AEM to host a working group to
  Determine significance thresholds to specific aquatic VEC
  Incorporate cultural value to Inuit in assessing project related changes to the environment
This request is in line with AEM’s commitment to collaborate with the KIA to modify the Aquatic Environment Monitoring Program and incorporate IQ into the monitoring programs
This can be explored during the discussions committed to in KIA-WL-04
ᐃᒪᓕᕆᔨᒃᑯᑦ NWB ᑎᓕᓯᓇᔭᕐᒪᑕ AEM ᑯᓐᓂᒃ ᑎᒥᓕᐅᖁᓗᒋᑦ ᐱᓕᕆᓂᐊᖅᑐᓂᒃ ᐅᑯᓂᖓ
  ᓴᖅᑭᑦᑎᓗᑎᒃ ᐆᒃᑐᕋᐅᑎᒃᓴᓂᒃ ᖃᐅᒪᔾᔪᑕᐅᓂᐊᖅᑐᓂᒃ ᐃᒪᕐᒥᐅᑕᓄᑦ ᐱᕈᖅᑐᖏᓐᓄᓪᓗ
  ᐃᓚᐅᑎᓪᓗᒋᑦ ᐃᓄᐃᑦ ᐅᐱᒋᔭᖏᑦ ᖃᐅᔨᓴᓕᕌᖓᑕ ᐊᕙᑎᐅᑉ ᐊᓯᔾᔨᖅᐸᓪᓕᐊᓂᖏᓐᓂᒃ.
ᑖᒻᓇ ᑐᒃᓯᕋᐅᑦ ᒪᓕᒃᑐᖅ AEM ᑯᑦ ᐱᓂᐊᕐᓂᕆᔭᖓᓂᒃ ᐱᓕᕆᖃᑎᖃᕐᓂᐊᕐᓂᕐᒥᒃ ᑮ ᐊᐄ ᐄ ᑯᓐᓂᒃ ᐊᖅᑭᒋᐊᖅᓯᓂᕐᒥᒃ ᐃᒪᕐᒥᐅᑕᐃᑦ ᖃᐅᔨᓴᕐᓂᖏᓐᓂᒃ ᐊᒻᒪ ᐃᐊᓗᑎᑦᑎᓂᕐᒥᒃ ᐃᓄᐃᑦ ᖃᐅᔨᒪᔭᑐᖃᖏᓐᓂᒃ ᕿᒥᕐᕈᓂᐅᓂᐊᖅᑐᓄᑦ
ᑕᒪᓐᓇ ᐅᖃᐅᓯᐅᔪᓐᓇᖅᑐᖅ ᐅᖃᓪᓚᓕᕈᑉᑕ ᐱᓂᐊᕐᓂᕆᔭᑉᑎᓐᓂ ᓇᓗᓇᐃᖅᓯᒪᔪᓂ KIA-WL-04 ᒥ.
Resolution
ᐋᖅᑭᒋᐊᕈᑏᑦ

## Slide 33: KIA-WL-12: Fish Tissue Baseline KIA-WL-12 ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓴᓐᓄᑦ ᖃᐅᔨᒪᔭᐅᕙᒌᖅᑐᑦ ᐆᒃᑐᕋᐅᑕᐅᔪᒃᓴᓕᐊᑦ
Issue
AEM committed to update the fish tissue baseline during the Nunavut Impact Review Board hearings
ᐃᓱᒫᓗᑦ
AEM ᓄᑕᐅᓯᒋᐊᖅᑎᑦᑎᓂᐊᓚᐅᖅᑐᑦ ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᒪᔭᒃᓴᓂᒃ ᓄᓇᕗᑦ ᕿᒥᕐᕈᔨᖏᑦ ᓂᕐᑉ ᑲᑎᒪᑎᑦᑎᑎᓪᓗᒋᑦ

## Slide 34: KIA-WL-12: Fish Tissue Baseline KIA-WL-12 ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓴᓐᓄᑦ ᖃᐅᔨᒪᔭᐅᕙᒌᖅᑐᑦ ᐆᒃᑐᕋᐅᑕᐅᔪᒃᓴᓕᐊᑦ
Resolution
AEM collected the fish tissue data in 2015
AEM has committed to
  Update the fish tissue baseline report prior to construction
  Evaluate how the 2015 fish tissue data compares with the historical data and if it changes assumptions presented in the Environmental Impact Statement
ᐋᖅᑭᒋᐊᕈᑦ
AEM ᐃᖃᓗᐃᑦ ᐊᒥᕋᖏᑦᑕ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓂᖃᓚᐅᖅᑐᑦ 2015 ᒥ
AEM ᐱᓇᐃᕐᓂᖃᖅᐳᖅ ᐅᑯᓂᖓ
  ᓄᑕᐅᓯᒋᐊᖅᑎᑦᑎᓂᐊᖅᑐᑦ ᐊᒥᕋᐃᑦ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓂᕐᒥᒃ ᓴᓇᒋᐊᓚᐅᖏᓐᓂᕐᒥᓂᒃ
  ᕿᒥᕐᕈᓂᐊᖅᑐᑦ ᖃᓄᖅ 2015ᒥ ᖃᐅᔨᓴᕐᓃᑦ ᐊᔾᔨᒌᖏᓐᓂᖃᕐᒪᖓᑖ ᐊᒻᒪ ᐱᑕᖃᖅᐸᑦ ᖃᓄᐃᑦᑑᖕᒪᖔᑖ ᓴᖅᑭᓪᓗᒋᑦ ᐊᕙᑎᒧᑦ ᐃᒃᐱᖕᓇᕐᓂᐅᓂᐊᖅᑐᑦ ᐅᖃᖅᓯᒪᔪᑦ ᐃᓗᐃᐋᓂ

## Slide 35: KIA-WL-13 and KIA-WL-14 KIA-WL-13 ᐊᒻᒪ KIA-WL-14
Issue
Potential missing information was highlighted in our review of the Concordance Table regarding:
  Additional Supplemental Information Guidelines
  Plans for Abandonment and Restoration
ᐃᓱᒫᓗᑦ
ᐃᓗᓪᓕᖅᑕᐅᖏᑦᑐᕕᓂᐅᑐᐃᓐᓇᕆᐊᖃᕐᓂᖓᓂᒃ ᐃᓗᐊᓃᑦᑕᕆᐊᓕᖕᓂᒃ ᓇᓗᓇᐃᖅᓯᒪᔪᖃᓚᐅᕐᒪᑦ ᕿᒥᕐᕈᑎᓪᓗᑕ ᐃᓗᓕᕆᔭᐅᔭᕆᐊᖃᖅᑐᓂᒃ ᐱᔾᔪᑎᒋᑉᓗᒋᑦ ᐅᑯᐊ:
  ᐃᓚᒋᐊᕈᑏᑦ ᑐᓴᖅᐸᓪᓕᕈᑏᑦ ᒪᓕᒐᒃᓴᐃᑦ
  ᒪᓕᒐᒃᓴᐃᑦ ᕿᒪᒃᑕᐅᓇᔭᕐᓂᖓᓄᑦ ᐊᒻᒪ ᐋᖅᑭᒋᐊᕐᓂᖓᓄᑦ

## Slide 36: KIA-WL-13 and KIA-WL-14 KIA-WL-13 ᐊᒻᒪ KIA-WL-14
Resolution
AEM has provided the required information
ᐊᖅᑭᒋᐊᕈᑏᑦ
AEM ᑐᓂᓯᓚᐅᖅᑐᑦ ᐃᓗᓕᕆᔭᐅᔭᕆᐊᖃᖅᑐᓐᓂᒃ

## Slide 37: KIA-WL-15: Sample Station Categorization KIA-WL-15: ᐆᒃᑐᕋᕐᕖᑦ ᐊᔾᔨᒌᖏᓐᓂᖏᑦ
Issue
AEM categorized MEL-05, MEL-06 and MEL-07 as “verification samples”
Verification samples are “for operational and management purposes by Agnico Eagle”
General Aquatic samples are “subject to compliance assessment to confirm sampling was carried out using established protocols, included quality assurance/quality control provisions, and addresses identified issues.”
KIA are concerned that these stations drain to Meliadine Lake and any problems detected should trigger management action
ᐃᓱᒫᓗᑦ
AEM ᑎᑎᖅᓯᓚᐅᕐᒪᑕ MEL-05, MEL-06 ᐊᒻᒪ MEL-07 “ ᑐᑭᓯᒋᐊᕐᕕᒃᓴᐃᑦ ᐆᒃᑑᑏᑦ”
ᑐᑭᓯᒋᐊᕐᕕᒃᓴᐃᑦ ᐆᒃᑐᑏᑦ ᐊᑐᕆᐊᖃᕐᒪᑕ “ ᐊᐅᓪᓚᕐᓂᖓᓄᑦ ᐊᒻᒪ ᐊᐅᓚᑦᑎᓂᖓᓄᑦ ᐊᒡᓃᑯ ᐄᒍᑯᓐᓄᑦ”
ᐃᒪᕐᒥᐅᑕᐃᑦ ᐆᒃᑐᑏᑦ ᐃᒪᐃᒻᒪᑕ “ ᐊᒃᑐᐊᖕᒪᑕ ᒪᓕᒃᑲᓗᐊᕐᒪᖔᑕ ᖃᐅᔨᓴᕐᓂᕐᓄᑦ ᓇᓗᓇᐃᕆᓂᐊᕐᓗᑎᒃ ᖃᐅᔨᓴᕐᓂᖅ ᐊᑐᖅᑕᐅᓚᐅᕐᒪᖔᑦ ᑕᐅᖅᖢᑎᒃ ᒪᓕᒃᑕᐅᓲᓂᒃ ᖃᐅᔨᓴᕐᓂᕐᒧᑦ, ᐃᓚᐅᑉᓗᒋᑦ ᐱᓕᕆᑦᑎᐊᕐᓂᖅ, ᐳᐃᔪᓂᖅ ᐊᑐᕐᓂᖅ ᐊᒻᒪ ᑐᕌᖅᑕᕐᓂᒃ ᓇᓗᓇᐃᕆᓇᓱᖕᓂᖅ”
ᑮ ᐊᐄ ᐄ ᑯᑦ ᐃᓱᒫᓗᒃᑐᑦ ᑖᑉᑯᐊ ᖃᐅᔨᓴᕐᕖᑦ ᑰᖕᒪᑕ ᑕᓯᕐᔪᐊᕐᒧᑦ ᐊᒻᒪ ᓱᓇᒥᐊᖅ ᐅᓗᕆᐊᓇᖅᑐᖅ ᓴᖅᑭᑉᐸᑦ ᐅᐸᓗᖅᑕᐅᔭᕆᐊᓕᒃ ᐊᐅᓚᑦᑎᔨᓄᑦ

## Slide 38: KIA-WL-15 Continued
MEL_05
MEL_06
MEL_07

## Slide 39: KIA-WL-15: Sample Station Categorization KIA-WL-15: ᐆᒃᑐᕋᕐᕖᑦ ᐊᔾᔨᒌᖏᓐᓂᖏᑦ
Resolution
AEM’s low action level response for these three locations will be:
  To recategorize the specific location of concern as a General Aquatic Monitoring Station,
  Include the location as an additional station in the Aquatic Environment Monitoring Program,
  Investigate the source of contamination, and
  Mitigate the source to prevent further contamination of the water body.
ᑐᑭᓯᖃᑎᒌᒍᑦ
AEM ᑭᐅᔾᔪᑎᖏᑦ ᐅᐸᓗᐊᖏᓪᓗᒋᑦ ᑖᑉᑯᐊ ᐱᖓᓱᑦ ᐃᓂᖏᑦ ᐅᑯᐋᖑᓂᐊᖅᐳᑦ:
ᓴᖅᑮᒃᑲᓐᓐᓂᕐᓂᖅ ᐃᓂᒋᔭᐅᓂᐊᖅᑐᖅ ᐃᒪᕐᒥᐅᑕᐃᑦ ᐃᓱᒫᓗᑕᐅᔾᔪᑦ ᐃᓃᑦ ᒥᒃᓵᓄᑦ ᖃᐅᔨᓴᕐᓂᕐᓂᒃ
ᐃᐊᓗᑎᓪᓗᒍ ᐃᓂ ᖃᐅᔨᓴᕐᕕᐅᖃᑕᐆᓕᕐᓗᓂ ᐃᒪᕐᒥᐅᑕᐃᑦ ᐊᕙᑎᖏᓐᓄᑦ ᖃᐅᔨᓴᕐᕕᖕᓂ
ᕿᓂᕐᓂᖅ ᓇᑭᑦ ᐱᖕᒪᖔᑦ ᐅᓗᕆᐋᓇᖅᑐᖅ, ᐊᒻᒪ
ᐋᖅᑭᒋᐊᕐᓗᒍ ᐅᓗᕆᐊᓇᖅᑐᖃᕐᕕᒃ ᐅᓗᕆᐊᓇᖅᑐᖃᒃᑲᓐᓂᖁᓇᒍ ᐃᒪᕐᒧᑦ

## Slide 40: KIA-WL-16: Detection Limits KIA-WL-16:ᖃᐅᔨᔪᑏᑦ ᑭᒡᓕᖏᑦ
Issue
AEM has indicated no accredited laboratory will be located on site
Proposed the use of six analytical laboratories
  Concerned for interlab variability
AEM did not provide detection limits that will be used at the laboratories
ᐃᓱᒫᓗᑦ
AEM ᓇᓗᓇᐃᖅᓯᒪᔪᑦ ᖃᐅᔨᓴᕐᕕᓪᓚᑦᑖᒥᒃ ᐱᑕᖃᕐᓂᐊᓂᑦᑐᖅ ᐱᓕᕆᕝᕕᖕᒥ
ᐊᕐᕕᓂᓕᖕᓂᒃ ᖃᐅᔨᓴᕐᕕᖕᓂᒃ ᐊᑐᕈᒪᓂᖃᖅᑐᑦ
  ᐃᓱᒫᓗᑎᖓᑦ ᐊᔾᔨᒌᖏᑦᑐᓕᕆᔪᓐᓇᕐᓂᖅ
AEM ᓇᓗᓇᐃᕆᓚᐅᖏᑦᑐᑦ ᖃᐅᔨᔾᔪᑎᒃᓴᓂᒃ ᑭᒡᓕᖃᕐᓂᐅᓂᐊᖅᑐᓂᒃ ᖃᐅᔨᓴᕐᕕᖕᓂ
Notes: Reporting detection limits in the licence application is essential to establish that the analytical sensitivity is sufficient to detect mine related changes so that they can be mitigated prior to the occurrence of adverse effects in the receiving environment.
Methodological and detection limit differences between labs may introduce unnecessary variability.

## Slide 41: KIA-WL-16: Detection Limits KIA-WL-16:ᖃᐅᔨᔪᑏᑦ ᑭᒡᓕᖏᑦ
AEM has committed to work with the KIA to achieve acceptable detection limits for all laboratories and parameters
  Limits will be based on those proposed in our submission
  Agreed upon limits will be included in the Quality Assurance / Quality Control Plan
Detection limits will apply to all contracted analytical laboratories for water quality samples collected at specific sites indicated in our submission
AEM ᐱᓂᐋᕐᓂᖃᖅᐳᖅ ᐱᓕᕆᖃᑎᒋᓗᒋᑦ ᑮ ᐊᐄ ᐄ ᑯᑦ ᓈᒻᒪᒃᑐᓂᒃ ᖃᐅᔨᒋᐊᕐᓂᕐᒧᑦ ᑭᒡᓕᓯᓂᐋᕈᑎᖃᕈᓐᓇᖁᑉᓗᒋᑦ ᑕᒪᐃᓐᓄᑦ ᖃᐅᔨᓴᕐᕕᖕᓄᑦ ᐊᒻᒪ ᐊᕙᑎᖏᓐᓄᑦ
  ᑭᒡᓕᖏᑦ ᑕᐃᑉᑯᐊᖑᓂᐊᖅᐳᑦ ᓴᖅᑭᑕᑉᑎᓐᓂ ᓇᓗᓇᐃᖅᓯᒪᔪᑦ
  ᐊᖏᕈᑕᐅᔪᑦ ᑭᒡᓕᒃᓴᐃᑦ ᐃᓚᐅᓂᐊᖅᐳᑦ ᐱᐅᔪᓂᒃ ᓈᒻᒪᒃᓴᕈᑎᓂ/ᓈᒪᑏᐊᖅᑐᓂᒃ ᐱᓕᕆᐊᖃᕐᓂᕐᒧᑦ ᐸᕐᓇᒍᑏᑦ ᐃᓪᓗᐋᓂ
ᖃᐅᔨᔾᔪᑏᑦ ᑭᒡᓕᖏᑦ ᐊᑐᖅᑕᐅᓂᐊᖅᐳᑦ ᑕᒪᐃᓐᓄᑦ ᑲᓐᑐᓛᒃᓯᒪᔪᓄᑦ ᖃᐅᔨᓴᕐᑎᓄᑦ ᐃᒪᐃᑦ ᓈᒻᒪᖕᒪᖔᑖ ᖃᐅᔨᒋᐊᕐᕕᖕᓄᑦ ᓇᓗᓇᐃᖅᓯᒪᔪᓂ ᓴᖅᑭᑕᑉᑎᓐᓂᒃ
Resolution
ᐋᖅᑭᔾᔪᑕᐅᓚᐅᖅᑐᖅ
Notes: General Aquatic Monitoring Stations,
Aquatic Environment Monitoring Program Stations,
Regulated Monitoring Stations, and
The MEL_05, MEL_06 and MEL_07 Verification Locations.

## Slide 42: KIA-WL-17: Potential Impacts to Lake B7 KIA-WL-17: ᐃᒃᐱᖕᓇᕐᓂᕆᔪᓐᓇᖅᑕᖏᑦ ᑕᓯᖅ B7 ᒧᑦ
Issue
AEM has moved to dry stack storage of the tailings
  This reduces impacts to the aquatic environment
  The main concern of dry stacking is dust generation during operation
AEM has not provided a map indicating all dust fall monitoring stations in the application
Lake B7 is now potentially subject to dust deposition originating from the dry stack tailings
ᐃᓱᒫᓗᑦ
AEM ᓅᓚᐅᕐᒪᑕ ᐸᓂᖅᑐᓂᒃ ᑐᖅᑯᖅᓯᒪᔾᔨᓂᖅ ᐃᕐᕈᖅᑐᐃᔾᔪᑎᕕᓂᕐᓂᒃ ᐅᔭᕋᒃᑕᖅᑕᐅᓂᑯᓄᑦ
  ᑖᒻᓇ ᒥᒃᖠᕙᓪᓕᖅᑎᑦᑎᖕᒪᑦ ᐅᓗᕆᐊᓇᕐᓂᕐᓄᑦ ᐃᒪᕐᒦᑦᑐᓄᑦ
  ᐸᓂᖅᑐᓂᒃ ᑲᑎᖅᓱᐃᓂᖅ ᐃᓱᒫᓗᑎᖃᕈᑎᖃᕐᒪᑦ ᐳᔪᖃᑖᒃᑎᑦᑎᖃᑦᑕᕐᓂᖓᓂᒃ ᑲᑎᖅᓱᖅᑕᐆᓕᕌᖓᑦ
  AEM ᑐᓂᓯᓚᐅᖏᒻᒪᑦ ᓱᓕ ᓄᓇᖑᐊᕐᒥᒃ ᓇᓗᓇᐃᕆᔪᒥᒃ ᓱᑯᑦᑎᐊᓂ ᖃᐅᔨᓴᖅᑕᐅᕙᖕᒪᖔᑦ ᐳᔪᖃᑖᑉ ᐃᖏᕐᕋᓂᖏᑦ
  ᑕᓯᖅ B7 ᑎᒃᑕᐅᕕᐅᑐᐃᓐᓇᕆᐊᖃᕐᒪᑦ ᐃᕐᕈᖅᑑᑎᕕᓂᕐᓂᒃ ᑲᑎᑕᐅᓯᒪᔪᓂᒃ

## Slide 43: KIA-WL-17: Potential Impacts to Lake B7 KIA-WL-17: ᐃᒃᐱᖕᓇᕐᓂᕆᔪᓐᓇᖅᑕᖏᑦ ᑕᓯᖅ B7 ᒧᑦ
AEM has committed to include all dust fall monitoring stations and locations within the Dust Management Plan prior to any material being placed in the Tailings Storage Facility
AEM ᐅᖃᖅᓯᒪᔪᑦ ᓇᓗᓇᐃᕆᓂᐊᖅᓯᒪᑉᓗᑎᒃ ᑕᒪᐃᓐᓂᒃ ᐳᔪᖃᑖᕐᓂᒃ ᖃᐅᔨᓴᕐᕖᑦ ᐃᓂᖏᓐᓂᒃ ᐳᔪᖃᑖᑦ ᒥᒃᓵᓄᑦ ᐊᐅᐊᑦᑎᓂᐅᓂᐊᖅᑐᑦ ᐸᕐᓇᒃᓯᒪᔾᔪᑎᖏᓐᓂ ᐃᕐᕈᖅᑑᑎᕕᓂᕐᓂᒃ ᐃᓕᓯᔪᖃᒃᑲᓐᓂᓚᐅᖅᑎᓐᓇᒍ ᐃᕐᕈᖅᑑᑎᕕᓂᐅᓯᕝᕕᒃᓴᒧᑦ
Resolution
ᐋᖅᑭᒋᐊᕈᑕᐅᓯᒪᔪᑦ

## Slide 44: KIA-WL-18: Dust Management at Closure KIA-WL-18: ᐳᔪᖃᑖᓂᒃ ᐊᐅᓚᑦᑎᓂᖅ ᒪᑐᔭᐅᒋᐊᖅᐸᑦ
Issue
AEM indicated that dust control would be “evaluated and implemented during closure activities as required”
Dust management is an issue of significant concern to the community
AEM had not provided the thresholds to determine if dust control will be required at closure
ᐃᓱᒫᓗᑦ
AEM ᓇᓗᓇᐃᕆᓚᐅᕐᒪᑕ ᐳᔪᖃᑖᒃ “ ᕿᒥᕐᕈᔭᐅᔪᒫᕐᒪᑦ ᐊᒻᒪ ᐱᓕᕆᐋᖑᓗᓂ ᒪᑐᕙᓪᓕᐊᓕᖅᐸᑦ ᐊᒻᒪ ᐱᓕᕆᐋᖑᔭᕆᐊᖃᓕᕌᖓᑦ”
ᐳᔪᖃᑖᒃ ᐃᓱᒫᓗᑕᐅᒻᒪᕆᖕᒪᑦ ᓄᓇᓕᖕᒧᑦ
AEM ᓴᖅᑭᑦᑎᓚᓗᖏᑦᑐᖅ ᓱᓕ ᐳᔪᖃᑖᑦ ᒥᒃᓵᓄᑦ ᖃᐅᔨᒪᔾᔪᑎᒃᓴᓂᒃ ᐊᒻᒪ ᐳᔪᖃᑖᒃ ᐃᓱᒫᓗᑎᒃᓴᐅᓕᕋᔭᕐᒪᖔᑦ ᒪᑐᓕᖅᐸᑦ

## Slide 45: KIA-WL-18: Dust Management at Closure KIA-WL-18: ᐳᔪᖃᑖᓂᒃ ᐊᐅᓚᑦᑎᓂᖅ ᒪᑐᔭᐅᒋᐊᖅᐸᑦ
AEM has committed to including a discussion of these thresholds in the next iteration of the Closure Plan
AEM ᑕᒪᑐᒪ ᒥᒃᓵᓄᑦ ᐅᖁᓯᖃᖃᓯᐅᑎᓂᐊᕐᓂᕋᖅᑐᑦ ᑭᒍᓪᓕᕐᒥ ᑲᑎᒍᑉᑕ ᐅᒃᑯᐊᕈᒫᕐᓂᐊᑕ ᒥᒃᓵᓂᒃ ᐅᖃᐅᓯᖃᓕᕈᑉᑕ
Resolution
ᐋᖅᑭᒋᐊᖅᑕᐅᓯᒪᔪᖅ

## Slide 46: KIA-WL-19: Fuel Contact Water Discharge Criteria KIA-WL-19: ᐅᖅᓱᐊᓘᑉ ᐊᒃᑐᕋᔭᕐᓂᖓᑕ ᐃᒪᕐᒧᑦ ᖃᓄᐃᓕᐅᕈᑎᒃᓴᐃᑦ ᒪᓕᒐᑦ
Issue
AEM had not provided discharge criteria for melting snow and precipitation within secondary contact berms of the Fuel Tanks at Itivia Harbour
Concern given Itivia is located away from treatment infrastructure and will contain fuel tanks and potential contact water
ᐃᓱᒫᓗᑦ
AEM ᐊᑐᐃᓐᓇᕈᐃᓚᐅᖏᑦᑐᑦ ᖃᓄᖅ ᐊᐳᑦ ᐊᐅᒃᐸᓪᓕᐊᔪᖅ ᐊᒻᒪ ᐃᒪᖅ ᐱᓕᕆᐊᖑᓂᐊᕐᒪᖓᑦ ᐅᖅᓱᐋᓗᖃᕐᕕᒃᓴᓂ ᐃᑎᕕᐋᓂ
ᐃᓱᒫᓗᑦ ᐃᑎᕕᐊ ᐅᖓᓯᖕᓂᖓ ᐃᒪᕐᒧᑦ ᐱᓕᕆᔨᓄᑦ ᐊᒻᒪ ᐃᓗᓕᖃᕐᓂᐊᖅᖢᑎᒃ ᐅᖅᓱᐋᓗᖕᓂᒃ ᐊᒻᒪ ᐃᒪᕐᒧᑦ ᐊᒃᑐᐃᑐᐃᓐᓇᕆᐊᖃᕐᓂᖓ
Notes: it is important to establish what the receiver would be should contact water exceed the discharge criteria.

## Slide 47: KIA-WL-19: Fuel Contact Water Discharge Criteria KIA-WL-19: ᐅᖅᓱᐊᓘᑉ ᐊᒃᑐᕋᔭᕐᓂᖓᑕ ᐃᒪᕐᒧᑦ ᖃᓄᐃᓕᐅᕈᑎᒃᓴᐃᑦ ᒪᓕᒐᑦ
Water meeting discharge criteria will be used as a dust suppressant along the roads
Water not meeting criteria will be discharged to the tundra
AEM intends to apply discharge criteria currently used at Meadowbank and will include it in the next iteration of the dust management plan prior to construction
ᐃᒪᖅ ᐅᓗᕆᐊᓇᖏᑦᑐᖅ ᐊᕙᑎᒧᑦ ᐊᐅᑦᖅᑕᐅᓂᐊᖅᐳᖅ ᐳᔪᖃᑖᒋᒃᑯᑕᐅᓗᓂ ᐊᑉᖁᑎᓄᑦ
ᐃᒪᖅ ᐊᑐᒐᒃᓴᐅᖏᑦᑐᖅ ᓄᓇᒧᑦ ᑰᒃᑎᑕᐅᓂᐊᖅᐳᖅ
AEM ᐊᑐᕐᓂᐊᖅᐳᖅ ᒪᓕᒡᓗᑎᒃ ᐊᑐᖅᑕᒥᓂᒃ ᒫᓐᓇ ᐊᐳᖅᑎᓐᓈᖅᑐᒥ ᐊᒻᒪ ᐃᓚᐅᑎᓐᓂᐊᕐᓗᒍ ᐳᔪᖃᑖᑉ ᒥᒃᓵᓄᑦ ᐱᓕᕆᐋᖃᓕᕈᑎᒃ ᓴᓇᒋᐊᓚᐅᖏᓐᓂᕐᒥᖕᓂᒃ ᐅᔭᕋᒃᑕᕆᐊᒥᒃ
Resolution
ᐋᖅᑭᒋᐊᖅᑕᐅᓯᒪᔪᖅ

## Slide 48: KIA-WL-20: Incinerator Dust Fall Monitoring KIA-WL-20: ᐊᒃᑕᑯᓂᒃ ᐃᑭᑎᑦᑎᑎᓪᓗᒋᑦ ᐃᓯᐋᕿᓂᖏᓐᓂᒃ ᖃᐅᔨᓴᕐᓂᖅ
Issue
Our concern follows from KIA-WL-17
  We require more detail regarding AEM’s dust fall monitoring
The incinerator management plan only included emissions guidelines for mercury, dioxins and furans
ᐃᓱᒫᓗᑦ
ᐃᓱᒫᓗᑎᕗᑦ ᒪᓕᖕᒪᑦ ᑭᐊ-WL-17 ᒥᒃ
  ᑐᑭᓯᒃᑲᓐᓂᕆᐊᖃᖅᐳᒍᑦ AEM ᑯᑦ ᖃᐅᔨᓴᕐᓂᕆᓂᐊᖅᑕᖏᓐᓂᒃ ᐳᔪᖃᑖᑦ ᒥᒃᓵᓄᑦ
ᐊᒃᑕᑯᓄᑦ ᐃᑭᑎᑦᑎᓂᖏᑦᑕ ᐊᐅᓚᑦᑎᓂᖏᑦ ᐅᖃᐅᓯᖃᓚᐅᕐᒪᑕ ᒪᓕᒐᓂᒃ ᐅᓗᕆᐊᓇᖅᑐᓐᒃ ᐃᒃᑎᑦᑎᓂᖅ ᑭᓵᓂ ᓲᕐᓗ ᒨᑯᕆ, ᓇᐃᔭᕐᓗᖕᓇᖅᑐᓂᒡᓗ ᐊᓯᖏᓐᓂᒃ
Notes: While this is in line with other arctic mines, metals can still be released through incomplete combustion or operator failures.

## Slide 49: KIA-WL-20: Incinerator Dust Fall Monitoring KIA-WL-20: ᐊᒃᑕᑯᓂᒃ ᐃᑭᑎᑦᑎᑎᓪᓗᒋᑦ ᐃᓯᐋᕿᓂᖏᓐᓂᒃ ᖃᐅᔨᓴᕐᓂᖅ
AEM has committed to:
  Include a summary of all dust monitoring stations
  Specify which sources they are able to characterize
  Place high volume air samples downwind of the open pits and the Tailings Storage Facility
  Specify detection limits and analytical procedures
  Monitor the snowpack
This will be included in the Dust Management Plan prior to any material being placed in the Tailings Storage Facility
AEM ᐱᓂᐊᕐᓂᖃᖅᐳᖅ:
  ᐃᓚᐅᑎᑦᑎᓂᐊᕐᓗᑎᒃ ᑕᒪᐃᓐᓂᒃ ᐳᔪᖃᑖᓂᒃ ᖃᐅᔨᓴᕐᕕᖕᓂᒃ
  ᓇᓗᓇᐃᕆᓗᑎᒃ ᓱᓇᓂᒃ ᖃᐅᔨᔪᓐᓇᕐᒪᖔᑖ
  ᐊᖏᔪᓂᒃ ᓯᓚᒥᒃ ᖃᐅᔨᓴᕐᓂᖃᕈᓐᓇᕐᓗᑎᒃ ᐅᖅᑯᖅᖠᓂᕐᓂ ᐅᔭᕋᒃᑕᕐᕖᑦ ᐊᒻᒪ ᐃᕐᕈᖅᑐᐃᔾᔪᑎᕕᓃᑦ ᐃᓂᖏᓐᓂᒃ
  ᓇᓗᓇᐃᕆᓗᑎᒃ ᑭᒡᓕᖏᓐᓂᒃ ᖃᐅᔨᓴᕈᑏᑦ ᐊᒻᒪ ᖃᓄᖅ ᐱᓕᕆᕙᖕᓂᖏᓐᓂᒃ
  ᖃᐅᔨᓴᕐᓗᑎᒃ ᐊᐳᑏᑦ ᒥᒃᓵᓄᑦ
ᑕᒪᓐᓇ ᐃᐊᓗᓂᐊᖅᑐᖅ ᐳᔪᕐᓂᒃ ᖃᐅᔨᓴᕐᓂᕐᒧᑦ ᐊᐅᓚᑦᑎᓂᕐᒧᓪᓗ ᐱᓕᕆᐊᖑᓂᐊᖅᑐᓂᒃ ᐃᕐᕈᖅᑐᐃᔾᔪᑎᕕᓂᕐᓐᓄᑦ ᑲᑎᖅᓱᐃᕝᕕᒃᓴᖅ ᐊᑐᓕᐊᐅᖅᑎᓐᓇᒍ
Resolution
ᐋᖅᑭᒋᐊᖅᑕᐅᓯᒪᔪᖅ

## Slide 50: KIA-WL-22: STP Discharge Criteria KIA-WL-22: STP ᑯᕕᔭᐅᓂᖓᓄᑦ ᒪᓕᒐᒃᓴᖅ
Issue
AEM intends to use “Biological reactors like Bionest Kodiak units… to treat camp waste water.”
  No discharge criterion has been included for oil and grease
  This request is conservative as discharges go to CP1 prior to the receiving environment
ᐃᓱᒫᓗᑦ
AEM ᐊᑐᕐᓂᐊᕐᒪᑕ “ ᐃᕐᕈᖅᑐᐃᔾᔪᑎᓂᒃ ᒥᐊᕐᓘᑎᒥᒃ ᐱᓕᕆᕝᕕᖕᓂ ᐃᕐᕈᖅᑐᐃᔪᓐᓇᖅᑐᓂᒃ”
  ᖃᓄᖅ ᑯᕕᓯᓂᐊᕐᒪᖓᕐᒦᒃ ᐅᖅᓯᖅᑎᕈᑎᓂᒃ ᐃᓚᐅᔪᖃᖏᑦᑐᖅ
  ᑖᒻᓇ ᑐᒃᓯᕋᐅᑦ ᒥᑭᓂᖅᓴᐅᕗᖅ ᑯᕕᖅᑕᖅᑕᐅᔪᑦ ᑐᕌᓱᖑᖕᒪᑕ CP1 ᒧᑦ ᓯᓚᒧᑦ ᐊᕙᑎᒧᑦ ᑎᑭᓚᐅᕐᓇᑎᒃ

## Slide 51: KIA-WL-22: STP Discharge Criteria KIA-WL-22: STP ᑯᕕᔭᐅᓂᖓᓄᑦ ᒪᓕᒐᒃᓴᖅ
AEM will confirm grease traps from the outlet of the kitchens and other possible sources of oil and grease
AEM has clarified the sewage treatment plant will only ever discharge to CP1 – there will be no discharge to tundra
AEM ᓇᓗᓇᐃᕆᓂᐊᖅᐳᑦ ᐳᓐᓂᕐᓂᕐᓂᒃ ᑲᑎᖅᓱᐃᕝᕕᒃᓴᓂᒃ ᐃᒐᕝᕕᖕᒥ ᐊᒻᒪ ᐊᓯᖏᓐᓂ ᐅᖅᓱᖃᕐᕕᖕᓂ, ᐳᓐᓂᕐᓂᖃᕐᕕᖕᓂ.
AEM ᓇᓗᓇᐃᕆᓯᒪᔪᖅ ᖁᕐᕕᖕᒧᑦ ᑯᕕᖅᑕᕐᕕᒃ ᑯᕕᓯᖃᑦᑕᕐᓂᐊᖅᑐᖅ CP-! ᒧᑦ ᑭᓯᒥ – ᓄᓇᐃᓐᓇᕐᒧᑦ ᑯᕕᔪᖃᖃᑦᑕᕐᓂᐊᖏᑦᑐᖅ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 52: KIA-WL-23: Untested Cyanide Detoxification Process KIA-WL-23: ᐆᒃᑐᖅᑕᐅᓯᒪᖏᑦᑐᑦ ᑐᖁᓐᓇᖅᑐᑦ ᓴᐃᔭᓇᐃᑦ ᐅᓗᕆᐊᓇᕈᓐᓂᖅᑎᑕᐅᓂᖏᓐᓄᑦ ᒪᓕᒋᐊᓖᑦ
Issue
The cyanide detoxification has yet to be tested at the Meliadine Site
The total volume of process water to be managed has yet to be confirmed
ᐃᓱᒫᓗᑦ
ᓴᐃᔭᓇᐃᑦ ᒥᒃ ᐅᓗᕆᐊᓇᕈᓐᓃᖅᑎᑦᑎᓂᖅ ᐆᒃᑐᖅᑕᐅᓯᒪᖏᑦᑐᖅ ᓱᓕ ᑕᓯᕐᔪᐊᕐᒥ ᐱᓕᕆᕝᕕᐊᓂ
ᐃᒪᕐᒥᒃ ᖃᓄᖅ ᐊᒃᑎᒋᔪᒥᒃ ᐊᑐᕐᓂᐊᕐᒪᖓᕐᒦᒃ ᓱᓕ ᓇᓗᓇᐃᖅᓯᒪᖏᑦᑐᑦ

## Slide 53: KIA-WL-23: Untested Cyanide Detoxification Process KIA-WL-23: ᐆᒃᑐᖅᑕᐅᓯᒪᖏᑦᑐᑦ ᑐᖁᓐᓇᖅᑐᑦ ᓴᐃᔭᓇᐃᑦ ᐅᓗᕆᐊᓇᕈᓐᓂᖅᑎᑕᐅᓂᖏᓐᓄᑦ ᒪᓕᒋᐊᓖᑦ
AEM has confirmed they will use the same technology to detoxify cyanide applied at Meadowbank
AEM has committed to an “as needed” treatment approach for discharges to Meliadine Lake from CP1
  AEM will add cyanide detoxification to the treatment plant if they are unable to meet the cyanide discharge criteria
  AEM will recirculate effluent that does not meet discharge criteria and store it in CP1 until the treatment system has been installed and is operational
AEM ᓇᓗᐊᐃᖅᓯᒪᔪᑦ ᒪᓕᖕᓂᐊᕐᓂᕐᒥᓂᒃ ᐅᓗᕆᐊᓇᕈᓐᓃᖅᑎᑦᑎᓂᖏᑦ ᐊᐳᖅᑎᓐᓈᖅᑐᒥ ᐊᑐᖅᑕᐅᔪᑦ ᒪᓕᒃᑕᐅᓂᐊᕐᒪᑕ ᑕᓯᕐᔪᐊᕐᒥ
AEM ᐱᓕᕆᓂᐊᕐᓂᕋᖅᑐᑦ “ ᐊᑐᕆᐊᖃᕌᖓᒥᒃ ᑭᓯᐊᓂ” ᐋᖅᑭᒋᐊᖅᓯᖃᑦᑕᕐᓂᐊᕐᓂᕐᒥᒃ ᑯᕕᑎᑦᑎᔭᕌᖓᒥᒃ ᑕᓯᕐᔪᐊᕐᒧᑦ CP1 ᒥᑦ
        AEM ᐃᓚᓯᖃᑦᑕᕐᓂᐊᖅᐳᑦ ᓴᐃᔭᓇᐃᑦ ᒧᑦ ᐅᓗᕆᐊᓇᕈᓐᓃᕈᑎᒥᒃ ᐅᖓᐅᖅᑯᑦᑎᓯᒪᔭᕌᖓᒥᒃ ᓴᐃᔭᓇᐃᑦ ᑯᕕᔭᐅᔪᓐᓇᕐᓂᖏᑦᑕ ᒪᓕᒐᖏᓐᓂᒃ
        AEM ᐊᑐᒃᑲᓐᓂᖃᑦᑕᕐᓂᐊᖅᐳᑦ ᐃᒪᕐᓘᒻᒥᒃ ᓈᒻᒪᖏᒃᑲᖓᑦ ᑯᕕᔭᐅᔪᓐᓇᕐᓂᖓ ᐊᒻᒪ ᑐᖅᑯᖅᑕᐅᖃᑦᑕᕐᓂᐊᖅᖢᓂ CP1 ᒧᑦ ᐋᖅᑭᒋᐊᕈᑖ ᐃᓕᔭᐅᓚᐅᖅᑎᓐᓇᒍ ᐊᒻᒪ ᐊᐅᓪᓛᓕᓚᐅᖅᑎᓐᓇᒍ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 54: KIA-WL-24: Application of Water Quality Criteria to Modelled Results KIA-WL-24: ᐊᑐᖅᑕᐅᓂᐊ ᐃᒪᑦᑎᐊᕙᖃᕐᓂᐅᑉ ᒪᓕᒋᐊᖃᕐᓂᖏᑦ ᐊᑐᓕᖅᑕᐅᓯᒪᔪᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᓂᑯᓄᑦ
Issue
Metal Mining Effluent Regulations (MMER) have been compared to modeled dissolved metals concentrations in the collection ponds
  MMER applies to total metals
AEM has provided modeled results with the maximum average Total Suspended Solids concentration added to the dissolved fraction
ᐃᓱᒫᓗᑦ
ᓴᕕᒃᓴᒥᒃ ᐅᔭᕋᖕᓂᐊᕐᓃᑦ ᒪᓕᒐᖏᑦ ᐊᔾᔨᓯᔭᐅᓯᒪᖕᒪᑕ ᓄᖑᓴᖅᓯᒪᔪᓄᑦ ᓴᕕᒃᓴᓄᑦ ᑲᑎᖅᓱᖅᓯᒪᔪᓄᑦ ᑕᓯᕋᓕᐊᕐᓂ
    MMER ᑐᕌᖅᐳᖅ ᑕᒪᐃᓐᓄᑦ ᓴᕕᖕᓄᑦ
AEM ᑐᓂᓯᓯᒪᕗᖅ ᖃᐅᔨᓂᕐᓂᒃ ᐊᖏᓂᖅᐹᒥᒃ ᐳᒃᑕᓛᖅᑐᓂᒃ ᓴᕕᒃᓴᓂᒃ ᐃᓚᔭᐅᓯᒪᔪᓂᒃ ᓄᖑᓴᖅᓯᒪᔪᓄᑦ

## Slide 55: KIA-WL-24: Application of Water Quality Criteria to Modelled Results KIA-WL-24: ᐊᑐᖅᑕᐅᓂᐊ ᐃᒪᑦᑎᐊᕙᖃᕐᓂᐅᑉ ᒪᓕᒋᐊᖃᕐᓂᖏᑦ ᐊᑐᓕᖅᑕᐅᓯᒪᔪᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᓂᑯᓄᑦ
We are no longer concerned regarding the comparison of MMER criteria to the dissolved fraction operations
  Water in all collection ponds will report to CP1
During post closure, all collection ponds are considered the receiving environment
  They will be maintained until they are acceptable for discharge to the environment
  Final discharge criteria will be established in a later version of the Closure Plan
ᐃᓱᒫᓗᒋᔪᓐᓃᖅᑕᕗᑦ MMER ᒪᓕᒐᖏᑦ ᓄᖑᓴᖅᓯᒪᔪᓄᑦ ᐊᐅᓪᓛᕈᑎᓄᑦ
    ᑕᒪᕐᒥᒃ ᐃᒪᐃᑦ ᑲᑎᑕᐅᔪᑦ ᑕᓯᕋᕐᓂ ᐃᓕᔭᐅᓂᐊᖅᐳᑦ CP1 ᒧᑦ
ᐅᒃᑯᐊᓚᐅᖅᑎᓪᓗᒍ ᑕᒪᕐᒥᒃ ᑕᓯᕋᐃᑦ ᐃᓱᒪᒋᔭᐅᓂᐊᖅᐳᑦ ᐊᕙᑎᒧᑦ ᑲᑎᖅᓱᕐᕕᒃᑐᑦ
    ᒥᐊᓂᕆᔭᐅᓂᐊᖅᐳᑦ ᑯᕕᔭᐅᔪᓐᓇᖅᓯᓚᐅᖅᑎᓐᓇᒋᑦ ᓄᓇᒧᑦ
    ᑭᖑᓪᓕᖅᐹᖅᓯᐅᑦ ᒪᓕᒐᒃᓴᖅ ᓴᖅᑭᑕᐅᓂᐊᖅᐳᖅ ᖃᑯᒍᒃᑲᓐᓂᖅ ᐸᕐᓇᖕᓂᕐᒧᑦ ᐅᒃᑯᐊᕐᓂᒃᓴᖓᓄᑦ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 56: KIA-WL-25: Dust Suppression Along Roads KIA-WL-25: ᐊᑉᖁᑏᑦ ᑭᒡᓕᐊᓂ ᐳᔪᖃᑖᖃᓗᐊᖅᑕᐃᓕᓂᖅ
Issue
AEM intends to use saline groundwater as a dust suppressant
  Saline water is not approved for use in Nunavut as a dust suppressant
  Saline brines are also considered a contaminant under the United States Environmental Protection Agency
ᐃᓱᒫᓗᑦ
AEM ᐊᑐᓕᒑᔪᑦ ᑕᕆᐅᓕᖕᓂᒃ ᐃᒪᕐᒥᒃ ᐳᔪᖃᑖᒌᒃᑯᑎᒋᓗᒍ
    ᑕᕆᐅᓕᒃ ᐃᒪᖅ ᐊᖏᖅᑕᐅᓯᒪᖏᑦᑐᖅ ᐊᑐᖅᑕᐅᓂᖓ ᓄᓇᕗᑦ ᐃᓗᐋᓂ ᐳᔪᖃᑖᒋᒃᑯᑎᒋᓗᒍ
    ᑕᕆᐅᓖᑦ ᐊᑯᓯᒪᔪᑦ ᐅᓗᕆᐊᓇᖅᑐᒦᑎᑕᐅᔪᑦᑕᐅᖅ ᐊᒥᐅᕆᑲᓐ ᓄᓇᖓᓐᓂ ᐊᕙᑎᓕᕆᓂᕐᒧᑦ ᒥᐊᓂᖅᓯᔨᖏᓐᓄᑦ

## Slide 57: KIA-WL-25: Dust Suppression Along Roads KIA-WL-25: ᐊᑉᖁᑏᑦ ᑭᒡᓕᐊᓂ ᐳᔪᖃᑖᖃᓗᐊᖅᑕᐃᓕᓂᖅ
AEM has committed to apply to the Government of Nunavut to approve application of saline groundwater originating from the Meliadine Site as a dust suppressant prior to its use
AEM ᑐᒃᓯᕋᕐᓂᐊᕐᓂᕋᖅᑐᖅ ᓄᓇᕗᑦ ᒐᕙᒪᒃᑯᖏᓐᓂᑦ ᐊᖏᖅᑕᐅᔾᔪᑎᒥᒃ ᐊᑐᕈᓐᓇᕐᓂᕐᒥᒃ ᑕᕆᐅᓕᖕᒥᒃ ᐃᒪᕐᒥᒃ ᑕᓯᕐᔪᐊᕐᒥᙶᖅᑐᒥᒃ ᐊᑐᕐᓂᐊᕐᓗᒍ ᐳᔪᖃᑖᒌᒃᑯᑎᒧᑦ ᐊᑐᕆᐋᓚᐅᖏᓐᓂᕐᒥᓂᒃ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 58: KIA-WL-26: Dust Deposition to Nippisar Lake KIA-WL-26: ᐳᔪᖄᑖᖃᓕᖅᑎᑦᑎᓂᖅ ᑕᓯᓐᓈᕐᒥᒃ
Issue
Concern regarding the impact of dust from the bypass road on the Rankin Inlet water supply located in Nippisar Lake
ᐃᓱᒫᓗᑦ
ᐃᓱᒫᓗᑦ ᐱᑉᓗᒍ ᐳᔪᖃᑖᒃ ᐃᒃᐱᖕᓇᕐᓂᕆᓂᐊᖅᑕᖓ ᑲᖏᖅᖠᓂᐅᑉ ᐃᒥᖅᑕᕐᕕᐊᓄᑦ ᑕᓯᓐᓈᕐᒥ

## Slide 59: KIA-WL-26: Dust Deposition to Nippisar Lake KIA-WL-26: ᐳᔪᖄᑖᖃᓕᖅᑎᑦᑎᓂᖅ ᑕᓯᓐᓈᕐᒥᒃ
Alternative road routes are being discussed with the hamlet council of Rankin Inlet
ᐊᓯᐊᒍᑦ ᐊᑉᖁᓯᐅᕋᔭᕐᓂᖅ ᒫᓇ ᐅᖃᐅᓯᐅᔪᖅ ᕼᐊᒻᓕᑦᑯᑦ ᑲᑎᒪᔨᖏᓐᓄᑦ ᑲᖏᖅᖠᓂᕐᒥ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 60: KIA-WL-27: Reclamation of Dry Stack Tailings KIA-WL-27: ᐊᑐᒐᒃᓴᖑᖅᑎᑦᑎᓂᖅ ᐸᓂᖅᑐᓂᒃ ᐅᔭᕋᒃᓴᐃᔭᕐᕕᐅᔪᕕᓂᕐᓂᒃ
Issue
Concern regarding the time line for progressive reclamation of the dry stack tailings.
ᐃᓱᒫᓗᑦ
ᐃᓱᒫᓗᑦ ᐊᑯᓂᐆᓂᕆᓂᐊᖅᑕᖓ ᐊᑐᒐᒃᓴᕈᒃᑲᓐᓂᕈᓐᓇᕐᓂᖏᑦ ᐸᓂᖅᑐᑦ ᐅᔭᒐᒃᑕᖅᑕᐅᓂᑯᕕᓃᑦ.

## Slide 61: KIA-WL-27: Reclamation of Dry Stack Tailing KIA-WL-27: ᐊᑐᒐᒃᓴᖑᖅᑎᑦᑎᓂᖅ ᐸᓂᖅᑐᓂᒃ ᐅᔭᕋᒃᓴᐃᔭᕐᕕᐅᔪᕕᓂᕐᓂᒃ
AEM has indicated progressive reclamation will be started in year 7
AEM ᓇᓗᓇᐃᖅᓯᒪᔪᑦ ᐱᓕᕆᐊᖃᒻᒪᕆᖕᓂᖅ ᐅᑎᖅᑎᑦᑎᕙᓪᓕᐊᓂᕐᒥᒃ ᓄᓇᒥᒃ ᑕᐅᑦᑐᕆᓚᐅᖅᑕᖓᓄᑦ ᐱᒋᐊᕐᓂᐊᖅ ᐅᑭᐅᖅ 7 ᖓᓂ
Resolution
ᐋᖅᑭᒋᐊᕈᑦ

## Slide 62: Questions?
ᐊᐱᕐᖅᑯᑏᑦ ?