## Slide 1: ᓄᓇᕗᒻᒥ ᐃᒪᓕᕆᔩᑦ ᑲᑎᒪᔨᖏᑕ ᑲᑎᒪᓂᖓ
ᐃᒥᕐᒧᑦ ᓚᐃᓴᖓᓐᓄ ᐋᖅᑭᒋᐊᕈᑦ
ᑲᖏᖅᖠᓂᖅ 3AM-GRA-1624
ᕕᕗᐊᕆ 18, 2021

## Slide 2: ᐃᒥᕐᒧᑦ ᓚᐃᓴᖓ: 3AM-1624
ᐅᓪᓗᖅ ᓚᐃᓴᑖᕐᕕᒋᓯᒪᔭᖓ: ᒪᐃ 2, 2016
ᓚᐃᓴᖓᑕ ᐃᓱᓕᕝᕕᖓᓴ: ᒪᐃ 1, 2024
ᖃᓄᐃᓕᖓᓂᖓ ᓚᐃᓴᖓᑕ:
"ᑖᓐᓇ ᓚᐃᓴᖓ ᐱᔪᓐᓇᐅᑎᖃᖅᑎᑦᑎᓂᐊᖅᑐᖅ ᐃᒥᖅᑕᕈᓐᓇᖅᑎᑦᑎᓂᕐᒥᑦ ᐊᒻᒪᓗ ᐊᐅᓚᓕᖓᓄᑦ ᐃᒥᖃᖅᑎᑦᑎᓂᕐᒧᑦ ᐃᒥᖅᑕᕐᕕᖓᓐᓂᒃ, ᓱᓪᓗᓕᒃᑯᑦ ᐊᒻᒪᓗ ᑭᓈᓗᒻᒥᑦ ᓴᓗᒻᒪᖅᓴᐃᕕᒻᒥᑦ ᓄᓇᕗᑦ ᒐᕙᒪᒃᑯᓐᓂᑦ, ᓄᓇᓕᓐᓂ ᒐᕙᒪᒃᑯᓂᓪᓗ ᐱᔨᑦᓯᕋᖅᑎᒃᑯᑦ"
ᒫᓐᓇ ᑐᔅᓯᕋᐅᑎᐅᔪᖅ ᐋᖅᑭᒋᐊᖅᓯᔪᒪᓂᕐᒧᑦ ᒫᓐᓇ ᐊᑐᖅᑕᐅᕙᒌᖅᑐᒥᑦ ᐃᒥᕐᒧᑦ ᓚᐃᓴᒥᑦ, ᐃᒥᖅᑕᕐᕕᐅᖃᑦᑕᖅᑐᒥᑦ ᐊᒻᒪᓗ ᖃᓄᑎᒋ ᐊᖏᓂᓕᒻᒥᑦ ᐃᒥᖅᑕᖃᑦᑕᕐᓂᐊᕐᒪᖔᑕ.

## Slide 3: ᐱᓕᕆᐊᖑᓯᒪᔪᑦ
ᓂᐱᓴ ᑕᓯᖅ ᑖᓐᓇ ᐃᓄᓐᓄᑦ ᐃᒥᖅᑖᕐᕕᐅᖃᑦᑕᖅᑐᖅ ᓄᓇᓕᒻᒧᑦ ᑲᖏᖅᖠᓂᕐᒥᑦ, ᐃᓄᒋᐊᓐᓂᖃᑦᑐᖅ 2,842 (2016ᒥ ᓈᓴᖅᑕᐅᓯᒪᔪᑦ)
ᑖᓐᓇ ᖁᐊᖑᖃᑦᑕᖅᑐᖅ ᑕᖅᑭᓄᑦ 7ᓂᑦ 9ᓄᑦ ᐊᕐᕌᒎᑉ ᐃᓗᐊᓂ, ᑕᐃᒪᐃᓐᓂᖓᓄᑦ ᑕᓯᕐᒥᑦ ᐃᒥᖅᑕᖅᓯᒪᖃᑦᑕᕆᐊᓖᑦ ᖁᐊᓚᐅᙱᓐᓂᖓᓂᒃ ᐊᕐᕌᒍᑕᒫᑦ.
2009ᖑᑎᓪᓗᒍ, ᐃᓐᓇᐃᑦ ᓄᓇᓕᖓᓐᓂᒃ ᐃᓱᒫᓘᑎᖃᓚᐅᖅᑐᑦ ᐅᖃᐅᔾᔨᓪᓗᑎᑦ ᕼᐋᒻᒪᓚᒃᑯᖏᓐᓂᑦ ᐊᒻᒪᓗ ᓄᓇᓕᓐᓂ ᒐᕙᒪᒃᑯᓂᓪᓗ ᐱᔨᑦᓯᕋᖅᑎᒃᑯᓐᓄᑦ ᑕᓯᕐᒥᑦ ᐃᒪᖓ ᓄᖑᐸᓪᓕᐊᓯᒪᓗᐊᓕᕐᒪᑦ.
2009ᖑᑎᓪᓗᒍ ᖃᐅᔨᓴᖅᑕᐅᑎᓪᓗᒍ ᖃᐅᔨᔭᐅᓚᐅᖅᑐᑦ ᓄᓇᓖᑦ ᐃᒥᕐᒥᑦ ᐊᑐᕐᓂᕆᕙᑦᑕᖏᑦ ᐊᖏᓂᖅᓴᐅᕚᓪᓕᖅᓯᒪᓕᕐᒪᑕ ᑖᓐᓇ ᑕᓯᖅ ᐃᒻᒪᒌᕈᓐᓇᓚᐅᖅᑎᓐᓇᒍ ᓱᓕ.
Notes: A water supply pipeline from the nearby Char River to augment water supplies in Nipissar Lake was consequently constructed; however, concerns regarding the viability of this secondary supply source have been expressed in light of sustainable flow and water depth objectives imposed by the Nunavut Water Board (NWB) and Canada Department of Fisheries and Oceans (DFO).

## Slide 4: ᐱᓕᕆᐊᖑᓯᒪᔪᑦ
ᐃᒥᖃᕐᕕᐅᔪᒥᑦ ᓱᓪᓗᓕᐊᓗᒃ ᑕᐃᑲᙶᖓᔪᖅ ᐃᖃᓗᒑᕐᔪᒻᒥ ᓴᓇᔭᐅᓯᒪᔪᖅ 2012ᒥᑦ ᑖᓐᓇ ᐃᒻᒪᐸᓪᓕᐊᑲᓐᓂᖃᑦᑕᕐᓂᐊᕐᒪᑦ ᓂᐱᓴᐅᑉ ᑕᓯᖓ, ᑖᓐᓇᓗ ᐅᖅᓱᐊᓗᑐᐃᓐᓇᕐᒧᑦ ᐊᐅᓚᔾᔪᑎᖃᖅᑐᖅ ᐅᖅᓴᑦᑕᐅᖃᑦᑕᕆᐊᖃᖃᑦᑕᖅᑐᖅ ᐊᒻᒪᓗ ᖃᐅᔨᒋᐊᖅᑕᐅᖃᑦᑕᕐᓗᓂ ᐅᓪᓗᑕᒫᖅ.
ᐃᓱᒫᓗᑕᐅᖃᑦᑕᐃᓐᓇᑦᑐᖅ ᐃᒥᖅᑕᕐᕕᐅᔪᖅ ᑯᕕᔭᐅᓂᖓᑕ ᓴᙱᓂᖓ ᒥᓪᓗᐊᕐᕕᐅᓇᖅᓯᓯᒪᑎᓪᓗᒍ.
ᒥᓪᓗᐊᖅᑎᑦᑎᓐᓇᐅᑎᓪᓗᒍ ᑕᖅᑭᓄᑦ ᐱᖓᓱᓄᑦ ᐅᖓᑖᓄᓪᓗ ᐊᕐᕌᒍᑕᒫᖅ ᐃᒥᖅᑕᕐᕕᐅᖃᑦᑕᖅᑐᖅ ᒥᓪᓗᐊᖅᑎᑦᑎᓪᓗᑎᑦ, ᔫᓂ ᕿᑎᕋᓕᖅᑎᓪᓗᒍ ᐱᒋᐊᕐᓗᑎᑦ ᓯᑎᐱᕆ ᕿᑎᐊᓄᑦ ᑎᑭᓪᓗᒍ.
ᕿᒥᕐᕈᔭᐅᑎᓪᓗᒋᑦ ᑕᓰᑦ ᖃᓂᒋᔮᓃᑦᑐᑦ ᐊᑐᖅᑕᐅᓪᓗᑎᑦ ᖃᐅᔨᓴᕈᑏᑦ ᐃᒪᐅᑉ ᐃᑎᓂᖓᓂᒃ ᐊᒻᒪᓗ ᐊᖏᓂᖓᓂᒃ ᖃᐅᔨᓴᕈᑎᒥᑦ ᖃᐅᔨᔭᐅᓯᒪᔪᑦ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖅ ᐱᐅᓛᖑᑐᐃᓐᓇᕆᐊᖃᕐᓂᖓᓂᒃ ᐃᒥᖅᑕᕐᕕᐅᖃᑦᑕᕐᓗᓂ ᓂᐱᓴᒧᑦ ᑕᓯᕐᒧᑦ ᐃᒻᒪᐃᕕᐅᖃᑦᑕᓕᕐᓗᓂ ᓱᓪᓗᓕᐊᓗᑦᑎᒍᑦ
ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓ ᐃᒻᒪᐃᕙᓪᓕᐊᓲᖑᕗᖅ ᐊᖅᑰᒑᕐᔫᑉ ᑰᖓᓂ ᑕᐅᓄᖓᓗ ᑰᓕᖅᑐᓂ ᑲᖏᖅᓱᐊᓘᒧᑦ ᐃᒪᕐᒧᑦ.
Notes: Lower Landing Lake and Char River are part of the same watershed. Water quality has been annually monitored in both water bodies (GRA‐6, GRA‐7), along with Nipissar Lake (GRA‐1), since 2014.
The water chemistry for Nipissar Lake, Char River and Lower Landing Lake is very similar.
No impacts on the water quality of Nipissar Lake have been apparent or are anticipated.

## Slide 5: ᐃᒪᖓᑕ ᐊᖏᓂᖓ ᖃᓄᐃᓕᖓᓕᕐᓂᖓ
2015 | 
2016 | 
2017 | 
2018 | 
2019 | 
2020 | 
3.1464 m
2.9718 m
3.2449 m
2.9972 m
2.7209 m
2.5337 m
*ᖃᐅᔨᒪᔭᐅᒋᐊᓕᒃ ᐅᓇ ᐃᒪᐅᑉ ᐃᑎᓂᖓ ᖃᐅᔨᓴᖅᑕᐅᓂᖓ ᐱᔭᐅᖃᑦᑕᖅᑐᖅ ᓄᓇᖓᓂ ᐱᒋᐊᕐᕕᒋᓯᒪᔭᖓᓐᓂᒃ ᖃᐅᔨᓴᖅᑕᐅᓂᖓ, ᑕᐃᒪᐃᒻᒪᑦ ᓈᓴᐅᑏᑦ ᐊᖏᓂᖅᓴᑦ ᓇᓗᓇᐃᖅᓯᔪᑦ ᐃᒪᖓᓐᓂᒃ ᐃᑲᓂᖅᓴᐅᔪᒥᑦ
ᐊᕐᕌᒍ
*ᓂᐱᓴᐅᑉ ᑕᓯᖓᓂ ᐃᒪᐅᑉ ᐊᖏᓂᖓ
Notes: Golder Associates included water level data dating back to 1994 in their 2016 Water Balance Assessment Study, that displaced continual dropping of the water level in Nipissar Lake. This indicated that the natural recharge within the watershed to Nipissar Lake was inadequate to meet the domestic water demand in the community. Water level measurements taken by CGS over the past 5 years continue to display this pattern, even while supplementing using Char River. This is due to the significant challenges associated with pumping from the River, which flows fullest during freshet, and then lessons throughout the season.

## Slide 6: ᓄᓇᓕᓐᓂᑦ ᐃᒥᕐᒥᑦ ᐊᑐᖃᑦᑕᕐᓂᖏᑕ ᖃᓄᐃᓕᖓᓯᒪᓂᖓ
ᐊᕐᕌᒍ | ᐃᒥᕐᒥᑦ ᐊᑐᖃᑦᑕᕐᓂᐅᔫᑉ ᖃᓄᐃᓕᖓᓯᒪᓂᖓ*
2016 | 
2017 | 
2018 | 
2019 | 
2020 | 
*ᐊᔾᔨᒌᙱᑦᑐᓂᑦ ᐱᑕᖃᑐᐃᓐᓇᕆᐊᓕᒃ ᐊᐅᓚᓂᕐᒧᑦ ᐊᑲᐅᙱᓕᐅᕈᑕᐅᖃᑦᑕᖅᓯᒪᔪᑦ ᐱᔾᔪᑕᐅᓪᓗᑎᑦ.
650,020m3
713,911m3
732,412m3
690,169m3
776,956m3
Notes: *May not keep this slide… not really meaningful

## Slide 7: ᐃᓄᐃᑦ ᑭᒃᑯᑐᐃᓐᓇᐃᑦ ᖃᓄᙱᑦᑎᐊᕆᐊᖃᕐᓂᖏᓐᓄᑦ ᐃᓱᒫᓗᑕᐅᔪᑦ
ᐊᖏᖅᑕᐅᓚᐅᖅᑐᖅ ᑖᓐᓇ ᒥᓪᓗᐊᖅᑎᑦᑎᕕᐅᖃᑦᑕᕐᓂᐊᖅᑐᖅ ᐊᒻᒪ ᖃᓄᑎᒋᐅᒐᔭᕐᓂᖓ ᑕᐃᑲᙵᑦ ᐃᖃᓗᒑᕐᔪᓐᓂᒃ ᓈᒻᒪᙱᓗᐊᖅᑐᒥᒃ ᐃᒥᖅᑕᕐᕕᒋᔭᐅᖃᑦᑕᖅᑐᖅ ᓄᓇᓕᓐᓂᑦ ᐃᓄᖏᓐᓄᑦ ᐃᒥᖃᕆᐊᖃᕐᓂᖏᑦ ᐱᕙᓪᓕᐊᑐᐃᓐᓇᑎᓪᓗᒋᑦ.
ᑕᒪᓐᓇ ᐱᔾᔪᑕᐅᑕᓯᒪᒻᒥᔪᖅ ᐃᓱᖅᓯᓯᒪᓂᕆᕙᑦᑕᖓᓐᓂᒃ ᐅᐱᕐᖔᒃᑯᑦ ᐱᒋᐊᖅᑐᓂᑦ, ᑎᖅᑎᑦᑎᖃᑦᑕᕆᐊᖃᓕᕈᑕᐅᓪᓗᓂ ᐊᒻᒪᓗ ᐃᓱᒫᓗᓕᕈᑕᐅᓪᓗᓂ ᐃᒥᔅᓴᖃᑦᑎᐊᙱᓗᐊᕐᓂᕐᒥᑦ ᓄᓇᓕᒻᒧᑦ ᐅᐱᕐᖔᒃᑯᑦ ᐊᐅᓐᓇᖅᓯᓚᐅᖅᑎᓐᓇᒍ ᓱᓕ.
ᐊᖏᖅᑕᐅᓯᒪᔪᖅ ᐋᓐᓂᐊᖃᕐᓇᖏᑦᑐᓕᕆᒻᒪᕆᒻᒧᑦ ᐊᐅᔭᐅᑎᓪᓗᒍ 2018ᒥᑦ ᑐᐊᕕᕐᓇᖅᑑᑎᑕᐅᓪᓗᓂ, ᑖᓐᓇ ᒥᓪᓗᐊᖃᑦᑕᕐᓂᐅᔪᖅ ᐃᖃᓗᒑᕐᔫᑉ ᑕᓯᖓᓐᓂᒃ ᐊᑦᑎᓂᖅᓴᒧᑦ ᑕᓯᕐᒧᑦ ᐊᖅᑯᒑᕐᔪᒻᒧᑦ ᐊᐅᓪᓛᖅᑕᐅᓯᒪᔪᖅ ᐃᒻᒪᑦᑕᐅᖁᓪᓗᒍ ᓂᐱᓴᐅᑉ ᑕᓯᖓ ᐃᒪᐅᑎᓪᓗᒍ ᑕᓯᖅ
ᐊᑦᑎᓂᖅᓴᖅ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖅ ᐊᑐᖅᑕᐅᖃᑦᑕᖅᑐᖅ ᑭᐱᙳᐃᔭᕐᕕᐅᓪᓗᓂ, ᐃᖅᑲᓪᓕᐊᕐᕕᐅᓪᓗᓂ, ᐅᒥᐊᖅᑐᕐᕕᐅᓪᓗᓂ ᐊᒻᒪᓗ ᑎᒻᒥᓲᓄᑦ ᐃᒫᓄᑦ ᒥᒍᓐᓇᖅᑐᓄᑦ. ᑕᒪᒃᑯᐊ ᐱᓪᓗᒋᑦ ᐅᓗᕆᐊᓇᕈᑎᖃᐃᓐᓇᖅᓯᒪᔪᖅ ᐃᒥᖅᑕᕐᕕᒋᔭᐅᓗᓂ ᑖᓐᓇ ᑕᓯᖅ, ᐅᖅᓱᐊᓗᒻᒥᑦ ᑯᕕᔪᖃᑲᓪᓚᓂᖅᐸᑦ ᑖᕗᖓ ᐃᒫᓄᑦ ᑕᓯᕐᒧᑦ.
Notes: In 2018 an amendment to the licence to move pumping locations was commenced, but then was delayed due to unknown reasons. Extremely low water levels within the lake under the ice, prior to melt, contributed to high turbidity in the drinking water and to concerns of water shortages. The Chief Public Health Officer directed CGS to move the resupply to Lower Landing Lake, and sent a letter to the NWB informing the board on July 24, 2018
- Additional public health concerns include the usage of Lower Landing Lake for recreational purposes, which has always been a risk to the water supply for Rankin Inlet. The use if Lower Landing Lake for float planes and refueling planes and boats may need to be discussed with the Hamlet and with the Public. This has not changed due to the relocation, as the risk was just a significant when Char River was the supply location.

## Slide 8
ᑖᓐᓇ ᐱᔪᓐᓇᐅᑎᔪᖅ ᐊᖅᑰᒑᕐᔫᑉ ᑰᖓᓂ ᒥᓪᓗᐊᖅᑎᑦᑎᓂᕐᒧᑦ ᐃᓂᒋᔭᖓ ᑕᐃᑲᓃᑉᐳᖅ ᓯᕗᓂᐊᓂ ᐊᖅᑰᒑᕐᔫᑉ ᑕᓯᖓᓂ.
ᑖᓐᓇ ᓄᑖᖅ ᒥᓪᓗᐊᖅᑎᑦᑎᕕᐅᖃᑦᑕᖅᑐᖅ ᐃᒥᕐᒥᑦ ᐃᓂᖃᖅᑐᖅ ᐃᒻᒪᖄ 200 ᒦᑕ ᐅᐊᓐᓇᖅᐸᓯᖓᓂᒃ, ᐊᑦᑎᓂᖅᓴᖅ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓ.
12" ᓴᕕᒃ ᑎᓯᔪᒥᑦ ᓴᓇᓯᒪᔪᖅ ᓱᓪᓗᓕᒃ ᐃᓚᔭᐅᓚᐅᖅᑐᖅ ᐃᖃᓗᒑᕐᔪᒃ ᑕᓯᖓᒍᑦ.
ᑖᓐᓇ ᐃᒻᒥᕐᕕᖓᓐᓂᒃ ᐃᒻᒪᐃᔾᔪᑕᐅᔪᖅ ᓱᓪᓗᓕᒃ 10" ᐊᖏᓂᓕᒃ ᐊᕐᕌᒍᑕᒫᖅ ᐋᖅᑭᑦᑕᐅᖃᑦᑕᖅᑐᖅ, ᐊᑦᑐᐃᓂᖃᖃᑦᑕᖏᑦᑐᖅ ᑰᒻᒥ.
ᐃᒥᖅᑕᕐᕕᒻᒧᑦ ᐃᒻᒪᐃᕕᖓ ᐃᓂᖓ

## Slide 9: ᐃᒥᖅᑕᕐᕕᒻᒧᑦ ᐃᒻᒪᐃᕕᖓ ᐃᓂᖓ
Notes: The same equipment is currently used for the seasonal transfer of water from Lower Landing Lake to Nipissar Lake as was used at the Char River location.
The floating intake with fish screen is used along with the same pump and generator within the relocated sea can.
An extension of approximately 200 m to the 4.05 km overland pipeline was installed to bring the pipeline from Char River to Lower Landing Lake.

## Slide 10: ᐃᒥᖅ ᓈᒻᒪᓈᖅᓯᒪᔭᕆᐊᖃᕐᓂᖓᓄᑦ ᖃᐅᔨᓴᖅᑕᐅᖁᔨᔾᔪᑎ (ᒎᑐ ᐱᓕᕆᖃᑎᒌᖏᓪᓗ, 2016)
  ᐃᒥᖅᑕᖅᑎᓪᓗᒋᑦ ᑭᓪᓕᖃᖅᑎᑕᐅᔪᖅ 10%ᒥᑦ ᑲᑎᓪᓗᒍ ᐊᕐᕌᒍᑕᒫᖅ ᐃᒻᒪᒍᓐᓇᕐᓂᕆᔭᖓᓐᓂᒃ ᐃᖃᓗᒑᕐᔪᒻᒥᑦ, ᑕᒪᓐᓇ ᐊᑑᑎᖃᑦᑕᖅᑐᖅ ᑕᑕᓗᐊᕈᑎᓚᐅᖅᑎᓪᓗᒍ
    ᒥᓪᓗᐊᖅᑎᑦᑎᓂᕆᕙᑦᑕᖓᓐᓂᒃ ᐃᖏᕐᕋᑦᑎᐊᕈᑕᐅᖃᑦᑕᖅᑐᖅ ᓈᒻᒪᑦᑎᖅᓯᒪᓂᖓ ᒪᓕᓪᓗᒍ.
    ᑕᓯᕐᒥᑦ ᐃᒥᖓ ᒥᑭᓪᓕᕚᓪᓕᖅᑎᑕᐅᓪᓗᓂ ᐊᑦᑎᓂᖅᓴᒥᑦ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓᓂᒃ ᒥᓪᓗᐊᖅᑎᑦᑎᓐᓇᐅᑉ ᐅᓪᓗᖏᑦ ᐊᓂᒍᖅᑎᓪᓗᒍ.
    ᑕᒪᓐᓇ ᐱᕕᖃᖅᑎᑦᑎᒍᑕᐅᓪᓗᓂ ᐅᐱᕐᖔᒃᑯᑦ ᐊᐅᐸᓪᓕᐊᓕᖅᑎᓪᓗᒍ ᑕᕝᕙᓂ ᐃᖃᓗᒑᕐᔪᒃ ᐃᒪᖓᓂᒃ ᖃᐅᔨᓴᕈᑎᒥᑦ.
    ᐃᒥᖅᑕᕐᕕᐅᓂᖓᑕ ᑭᓪᓕᖃᖅᑎᑕᐅᖁᔭᐅᓂᖓ: 0.202 ᒦᑕ ᐱᖓᓱᐊᖅᑎᓪᓗᒍ/s (17,452.8 ᒦᑕ ᐱᖓᓱᐊᖅᑎᓪᓗᒍ), ᐱᔭᐅᓗᓂ ᖁᐊᕋᓱᓐᓂᖓᓂᑦ ᐅᕙᓗ ᑕᓯᖅ ᐃᒻᒪᑦᑕᐅᓯᒪᓕᖅᑎᓪᓗᒍ ᓈᒻᒪᑦᑐᒥᑦ.
  ᖃᐅᔨᓴᖅᐸᓪᓕᐊᓂᖅ ᐃᒥᖓᑕ ᖃᓄᐃᓕᖓᓕᕐᓂᕆᔭᖓᓐᓂᒃ ᐊᑦᑎᓂᖅᓴᒥᑦ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓᓂᒃ ᐊᒻᒪᓗ ᓂᐱᓴᐅᑉ ᑕᓯᖓᓂᒃ.
Notes: The recommended water taking limit is of 10% of the total annual flow in the Char River. Water taking under this approach would take place following the spring freshet and continue until lake freeze up. This option allows water taking to be carried out with a steady pumping rate. Water taking under this second approach would reduce Lower Landing Lake water levels through the end of the open water season, with flow from the following spring melt contributing to fill Lower Landing Lake and drive the spring freshet hydrograph in the Char River.

## Slide 11
ᐊᓯᔾᔨᖁᔭᐅᓯᒪᔪᑦ ᐃᒥᕐᒧᑦ ᓚᐃᓴᖓᓐᓂᒃ
ᐊᓯᔾᔨᖁᔭᐅᔪᖅ | ᐱᔾᔪᑕᐅᔪᖅ
ᓅᑦᑕᐅᓗᓂ ᐃᒥᖅᑕᕐᕕᐅᖃᑦᑕᖅᑐᖅ ᐊᑦᑎᓂᖅᓴᒧᑦ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓᓄᑦ | ᑰᓐᓂᖓ ᓱᕐᕋᖏᑦᑐᖅ ᐃᖃᓗᒑᕐᔪᐃᑦ ᑰᖓᓂᒃ, ᑕᒪᓐᓇ ᒥᓪᓗᐊᖅᑎᑦᑎᕕᐅᔪᓐᓇᕐᓂᖓᓂᒃ ᐊᖏᓪᓕᒋᐊᖅᑎᑦᑎᔪᓐᓇᖅᑐᖅ.
ᐊᖏᓪᓕᒋᐊᖅᑕᐅᓗᓂ ᐅᓪᓗᑕᒫᖅ ᒥᓪᓗᐊᖅᑎᑦᑎᓂᐅᖃᑦᑕᖅᑐᖅ ᐃᒻᒪᓐᓇᑎᒋᐅᒻᒪᑦ 3,485 ᒦᑕ ᐱᖓᓱᐃᖅᓱᕐᓗᒍ/ᐅᓪᓗᖅ ᐃᒻᒪᓐᓇᑎᒋᐅᖔᓕᕐᓗᓂ 10,000 ᒦᑕ ᐱᖓᓱᐃᖅᓱᕐᓗᒍ/ᐅᓪᓗᖅ | ᐃᒥᐅᑉ ᐊᖏᓂᖓᑕ ᖃᓄᐃᓕᖓᓂᖓ ᖃᐅᔨᓴᖅᑕᐅᕙᓪᓕᐊᓂᖓ ᓇᓗᓇᐃᖅᓯᓯᒪᔪᖅ ᐅᓪᓗᑕᒫᖅ ᐊᖏᓛᖑᔪᓐᓇᖅᑐᖅ ᑎᑭᖅᑲᔪᖅ 17,452 ᒦᑕ ᐱᖓᓱᐃᖅᓱᕐᓗᒍ/ᐅᓪᓗᖅ ᑖᓐᓇ ᑲᔪᓯᑦᑎᐊᕈᓐᓇᖅᑐᖅ, ᐊᒻᒪᓗ ᐊᑖᓂ 10% ᐊᕐᕌᒍᑕᒫᖅ ᑰᖃᑦᑕᖅᑐᖅ ᐃᖃᓗᒑᕐᔫᑉ ᑰᖓᓄᑦ; ᑖᓐᓇ ᓈᒻᒪᒃᑐᒥᒃ ᐱᕕᐅᔪᓐᓇᖅᑐᖅ ᐃᓚᒋᐊᕈᑎᔅᓴᖓᓐᓂᒃ ᑕᓯᐅᑉ ᐃᒪᖓᓄᑦ ᓂᐱᓴᒧᑦ.
ᐲᖅᑕᐅᓂᖓ ᑕᖅᑮᑦ ᐱᖓᔪᐊᓐᓂᒃ ᐅᓂᒃᑳᓕᐅᕆᐊᖃᕐᓂᖅ ᒫᓐᓇ ᐊᑐᖅᑕᐅᔪᒥᑦ ᐃᒥᕐᒧᑦ ᓚᐃᓴᒥᑦ | ᐱᔭᕆᐊᖃᙱᑦᑐᖅ.
Notes: Along with the maximum daily pumping request, CGS is open to an annual limit on pumping volume (700,000 – 800,000). The 10,000 m3/day aims to allow for unplanned challenges such as equipment failures, shortened season due to weather etc. The 10,000 m3/day allows CGS to remain in compliance with the licence, while not impacting the river (as per the water balance assessment) and ensuring Nipissar is adequately supplemented.

## Slide 12
ᐊᓯᔾᔨᖁᔭᐅᓯᒪᔪᑦ ᐃᒥᕐᒧᑦ ᓚᐃᓴᖓᓐᓂᒃ
ᐊᓯᔾᔨᖁᔭᐅᔪᖅ | ᐱᔾᔪᑕᐅᔪᖅ
ᓄᑖᕈᕆᐊᖅᑕᐅᓯᒪᔪᖅ ᒥᓪᓗᖅᑎᑦᑎᖃᑦᑕᕐᓂᕐᒧᑦ ᐸᕐᓇᐅᑎᖓᓐᓂᒃ ᑐᓂᔭᐅᓂᐊᖅᑐᖅ ᑕᖅᑮᑦ ᐱᖓᓲᔪᖅᑐᑦ ᓈᑉᐸᑕ, ᐊᒻᒪᓗ ᓄᑖᕈᕆᐊᖅᑕᐅᓕᕐᒥᓗᓂ ᑭᓯᐊᓂ ᐱᔭᕆᐊᖃᖅᐸᑕ ᒪᓕᓪᓗᒋᑦ ᐊᐅᓚᓂᕐᒧᑦ ᒪᓕᒐᖏᓐᓂᑦ ᐊᓯᔾᔨᖅᑐᖃᕐᓂᖅᐸᑦ. | ᐊᑐᖁᔭᐅᔪᓂᑦ ᒪᓕᓐᓂᐊᖅᑐᑦ ᑖᓐᓇ ᐃᒥᖅ ᖃᓄᐃᓕᖓᓕᕐᓂᖓᑕ ᖃᐅᔨᖅᓴᖅᑕᐅᕙᓪᓕᐊᓂᖓ ᒪᓕᓪᓗᒍ, ᐊᒻᒪᓗ ᓄᓇᒥᑦ ᖃᐅᔨᓴᖅᑎᐅᖃᑦᑕᖅᑐᓄᑦ.
ᐲᖅᑕᐅᓂᖓ ᒪᓕᑦᑎᐊᕆᐊᖃᕐᓂᖅ ᐃᓚᖓ GRA-6 (ᓄᓇᕗᒻᒥ ᐃᒥᓕᕆᓂᕐᒧᑦ ᑲᑎᒪᔩᑦ ᖃᐅᔨᓴᖅᐸᓪᓕᐊᓂᕐᒧᑦ ᐱᓕᕆᕝᕕᖓ ᑕᕝᕙᓂ ᐃᖃᓗᒑᕐᔫᑉ ᑰᖓᓂᒃ) | ᐃᒥᖓᑕ ᐊᖏᓂᖓ ᐊᒻᒪᓗ ᐱᐅᓂᖓ ᐱᔭᐅᓗᓂ ᐊᑦᑎᓂᖅᓴᒥᑦ ᐊᖅᑯᒑᕐᔪᒃ ᑕᓯᖓᓂᒃ ᐊᒻᒪᓗ ᓂᐱᓴᐅᑉ ᑕᓯᖓᓂᒃ.

## Slide 13
ᐃᓱᐊ